## Slide 1: Configuring EIGRP
Introducing EIGRP

## Slide 2: EIGRP Features
  Flexible network design
  Multicast and unicast instead of broadcast address
  Manual summarization at any point
  100% loop-free classless routing
  Easy configuration for WANs and LANs
  Load balancing across equal- and unequal-cost pathways
  Advanced distance vector
  Fast convergence
  Support for VLSM and discontiguous subnets
  Partial updates
  Support for multiple network-layer protocols

## Slide 3: EIGRP Key Technologies
  Neighbor discovery/recovery
    Uses hello packets between neighbors
  Reliable Transport Protocol (RTP)
    Guaranteed, ordered delivery of EIGRP packets to all neighbors
  DUAL finite-state machine
    Selects lowest-cost, loop free, paths to each destination
  Protocol-dependent modules (PDMs)
    EIGRP supports IP, AppleTalk, and Novell NetWare.
    Each protocol has its own EIGRP module and operates independently of any of the others that may be running.

## Slide 4: EIGRP Neighbor Table

## Slide 5: DUAL Terminology
  Selects lowest-cost, loop-free paths to each destination
  AD = cost between the next-hop router and the destination
  FD = cost from local router = AD of next-hop router + cost between the local router and the next-hop router
  Lowest-cost = lowest FD
  (Current) successor = next-hop router with lowest-cost, loop free path
  Feasible successor = backup router with loop-free path (AD of feasible successor must be less than FD of current successor route)

## Slide 6: EIGRP Topology Table

## Slide 7: EIGRP IP Routing Table

## Slide 8: Example: EIGRP Tables
Router C Tables:

## Slide 9: EIGRP Packets
  Hello: Establish neighbor relationships.
  Update: Send routing updates.
  Query: Ask neighbors about routing information.
  Reply: Respond to query about routing information.
  ACK: Acknowledge a reliable packet.

## Slide 10: Initial Route Discovery

## Slide 11: EIGRP Metric
  Same metric components as IGRP:
    Bandwidth
    Delay
    Reliability
    Loading
    MTU
  EIGRP metric is IGRP metric multiplied by 256.

## Slide 12: EIGRP Metric Calculation
  By default, EIGRP metric:
    Metric = bandwidth (slowest link) + delay (sum of delays)
  Delay = sum of the delays in the path, in tens of microseconds, multiplied by 256
  Bandwidth = [107 / (minimum bandwidth link along the path, in kilobits per second)] * 256
  Formula with default K values (K1 = 1, K2 = 0, K3 = 1, K4 = 0, K5 = 0):
    Metric = [K1 * BW + ((K2 * BW) / (256 – load)) + K3 * delay]
  If K5 not equal to 0:
    Metric = metric * [K5 / (reliability + K4)]:

## Slide 13: EIGRP Metrics Calculation Example
A  B  C  D Least bandwidth 64 kbps Total delay 6,000
A  X  Y  Z  D Least bandwidth 256 kbps Total delay 8,000
  Delay is the sum of all the delays of the links along the paths: Delay = [delay in tens of microseconds] x 256
  Bandwidth is the lowest bandwidth of the links along the paths: Bandwidth = [10,000,000 / (bandwidth in kbps)] x 256

## Slide 14: EIGRP Metrics Are Backward-Compatible with IGRP

## Slide 15: Summary
  EIGRP capabilities include fast convergence and support for VLSM, partial updates, and multiple network layer protocols.
  EIGRP key technologies are neighbor discovery/recovery, RTP, DUAL finite-state machine, and PDMs.
  EIGRP uses three tables: neighbor table, topology table, and routing table. The routing table contains the best route to each destination, called the successor route. A feasible successor route is a backup route to a destination; it is kept in the topology table.
  EIGRP uses the same metric components as IGRP: delay, bandwidth, reliability, load, and MTU.
  By default, EIGRP metric equals bandwidth (slowest link) plus delay (sum of delays).
  EIGRP metrics are backward-compatible with IGRP; the EIGRP-equivalent metric is the IGRP metric multiplied by 256.