## Slide 1: Configuring EIGRP
Implementing and Verifying EIGRP

## Slide 2: Configuring EIGRP
router eigrp autonomous-system-number
Defines EIGRP as the IP routing protocol.
All routers in the internetwork that must exchange EIGRP routing updates must have the same autonomous system number.
network network-number [wildcard-mask]
Identifies attached networks participating in EIGRP.
The wildcard-mask is an inverse mask used to determine how to interpret the address. The mask has wildcard bits, where 0 is a match and 1 is “don’t care.”
Router(config)#
Router(config-router)#

## Slide 3: Configuring EIGRP (Cont.)
bandwidth kilobits
Defines the interface’s bandwidth for the purposes of sending routing update traffic.
Router(config-if)#

## Slide 4: Configuring EIGRP for IP
Network 192.168.1.0 is not configured on router A, because it is not directly connected to router A.
Notes: <number>

## Slide 5: Using the Wildcard Mask in EIGRP
Notes: <number>

## Slide 6: Using and Configuring the ip default-network Command for EIGRP
Notes: <number>

## Slide 7: Example EIGRP Configuration
Notes: <number>

## Slide 8: R2 EIGRP Configuration
<output omitted>
interface FastEthernet0/0
ip address 172.17.2.2 255.255.255.0
<output omitted>
interface Serial0/0/1
bandwidth 64
ip address 192.168.1.102 255.255.255.224
<output omitted>
router eigrp 100
network 172.17.2.0 0.0.0.255
network 192.168.1.0
Notes: <number>

## Slide 9: Verifying EIGRP: show ip eigrp neighbors
R1#show ip eigrp neighbors
IP-EIGRP neighbors for process 100
H Address Interface Hold Uptime SRTT RTO Q Seq
(sec) (ms) Cnt Num
0 192.168.1.102 Se0/0/1 10 00:07:22 10 2280 0 5
R1#

## Slide 10: Verifying EIGRP: show ip route eigrp
R1#show ip route eigrp
D 172.17.0.0/16 [90/40514560] via 192.168.1.102, 00:07:01, Serial0/0/1
172.16.0.0/16 is variably subnetted, 2 subnets, 2 masks
D 172.16.0.0/16 is a summary, 00:05:13, Null0
192.168.1.0/24 is variably subnetted, 2 subnets, 2 masks
D 192.168.1.0/24 is a summary, 00:05:13, Null0
R1#show ip route
<output omitted>
Gateway of last resort is not set
D 172.17.0.0/16 [90/40514560] via 192.168.1.102, 00:06:55, Serial0/0/1
172.16.0.0/16 is variably subnetted, 2 subnets, 2 masks
D 172.16.0.0/16 is a summary, 00:05:07, Null0
C 172.16.1.0/24 is directly connected, FastEthernet0/0
192.168.1.0/24 is variably subnetted, 2 subnets, 2 masks
C 192.168.1.96/27 is directly connected, Serial0/0/1
D 192.168.1.0/24 is a summary, 00:05:07, Null0

## Slide 11: Verifying EIGRP: show ip protocols
R1#show ip protocols
Routing Protocol is "eigrp 100"
Outgoing update filter list for all interfaces is not set
Incoming update filter list for all interfaces is not set
Default networks flagged in outgoing updates
Default networks accepted from incoming updates
EIGRP metric weight K1=1, K2=0, K3=1, K4=0, K5=0
EIGRP maximum hopcount 100
EIGRP maximum metric variance 1
Redistributing: eigrp 100
EIGRP NSF-aware route hold timer is 240s
<output omitted>
Maximum path: 4
Routing for Networks:
172.16.1.0/24
192.168.1.0
Routing Information Sources:
Gateway Distance Last Update
(this router) 90 00:09:38
Gateway Distance Last Update
192.168.1.102 90 00:09:40
Distance: internal 90 external 170

## Slide 12: Verifying EIGRP: show ip eigrp interfaces
R1#show ip eigrp interfaces
IP-EIGRP interfaces for process 100
Xmit Queue Mean Pacing Time Multicast Pending
Interface Peers Un/Reliable SRTT Un/Reliable Flow Timer Routes
Fa0/0 0 0/0 0 0/10 0 0
Se0/0/1 1 0/0 10 10/380 424 0

## Slide 13: Verifying EIGRP: show ip eigrp topology
R1#show ip eigrp topology
IP-EIGRP Topology Table for AS(100)/ID(192.168.1.101)
Codes: P - Passive, A - Active, U - Update, Q - Query, R - Reply,
r - reply Status, s - sia Status
P 192.168.1.96/27, 1 successors, FD is 40512000
via Connected, Serial0/0/1
P 192.168.1.0/24, 1 successors, FD is 40512000
via Summary (40512000/0), Null0
P 172.16.0.0/16, 1 successors, FD is 28160
via Summary (28160/0), Null0
P 172.16.1.0/24, 1 successors, FD is 28160
via Connected, FastEthernet0/0
P 172.17.0.0/16, 1 successors, FD is 40514560
via 192.168.1.102 (40514560/28160), Serial0/0/1

## Slide 14: Verifying EIGRP: show ip eigrp traffic
R1#show ip eigrp traffic
IP-EIGRP Traffic Statistics for AS 100
Hellos sent/received: 429/192
Updates sent/received: 4/4
Queries sent/received: 1/0
Replies sent/received: 0/1
Acks sent/received: 4/3
Input queue high water mark 1, 0 drops
SIA-Queries sent/received: 0/0
SIA-Replies sent/received: 0/0
Hello Process ID: 113
PDM Process ID: 73

## Slide 15: Summary
  The configuration commands for basic EIGRP include:
    router eigrp autonomous-system
    network network-number [wildcard-mask]
    bandwidth kilobits
  The optional wildcard-mask parameter in the network command is an inverse mask used to determine how to interpret the network-number parameter. A wildcard bit of 0 is a match and of 1 is “don’t care.”
  Create and advertise a default route in an EIGRP AS with the ip default-network network-number command.
Notes: <number>

## Slide 16: Summary (Cont.)
  Use the show ip eigrp neighbors command to verify that the router recognizes its neighbors. Use the show ip route eigrp command to verify that the router recognizes routes from its neighbors.
  Use the show ip protocols, show ip eigrp interfaces, show ip eigrp neighbors, show ip eigrp topology, and show ip eigrp traffic commands to verify EIGRP operations.
Notes: <number>