## Slide 1: Configuring EIGRP
Configuring Advanced EIGRP Options

## Slide 2: EIGRP Route Summarization: Automatic
  Purpose: Smaller routing tables, smaller updates
  Automatic summarization:
    On major network boundaries, subnetworks are summarized to a single classful (major) network.
    Automatic summarization occurs by default.
Notes: <number>

## Slide 3: EIGRP Route Summarization: Manual
Manual summarization has the following characteristics:
  Summarization is configurable on a per-interface basis in any router within a network.
  When summarization is configured on an interface, the router immediately creates a route pointing to null0.
    Loop-prevention mechanism
  When the last specific route of the summary goes away, the summary is deleted.
  The minimum metric of the specific routes is used as the metric of the summary route.

## Slide 4: Configuring Route Summarization
no auto-summary
(config-router)#
Turns off automatic summarization for the EIGRP process
ip summary-address eigrp as-number address mask [admin-distance]
(config-if)#
Creates a summary address that this interface will generate

## Slide 5: Manually Summarizing EIGRP Routes
Notes: <number>

## Slide 6: Router C Routing Table
RouterC#show ip route
<output omitted>
Gateway of last resort is not set
172.16.0.0/16 is variably subnetted, 3 subnets, 2 masks
D 172.16.0.0/16 is a summary, 00:00:04, Null0
D 172.16.1.0/24 [90/156160] via 10.1.1.2, 00:00:04, FastEthernet0/0
D 172.16.2.0/24 [90/20640000] via 10.2.2.2, 00:00:04, Serial0/0/1
C 192.168.4.0/24 is directly connected, Serial0/0/0
10.0.0.0/8 is variably subnetted, 3 subnets, 2 masks
C 10.2.2.0/24 is directly connected, Serial0/0/1
C 10.1.1.0/24 is directly connected, FastEthernet0/0
D 10.0.0.0/8 is a summary, 00:00:05, Null0
RouterC#
Notes: <number>

## Slide 7: EIGRP Load Balancing
  Routes with a metric equal to the minimum metric are installed in the routing table (equal-cost load balancing).
  There can be up to six entries in the routing table for the same destination:
    The number of entries is configurable.
    The default is four.
    Set to 1 to disable load balancing.

## Slide 8: EIGRP Unequal-Cost Load Balancing
variance multiplier
Allows the router to include routes with a metric smaller than the multiplier value times the minimum metric route to that destination
Router(config-router)#

## Slide 9: Variance Example
  Router E chooses router C to get to network Z, because it has lowest FD of 20.
  With a variance of 2, router E chooses router B to get to network Z (20 + 10 = 30) < [2 * (FD) = 40].
  Router D is never considered to get to network Z (because 25 > 20).
Notes: <number>

## Slide 10: Configuring WAN Links
  EIGRP supports different WAN links:
    Point-to-point links
    NBMA
      Multipoint links
      Point-to-point links
  EIGRP uses up to 50% of bandwidth by default; this bandwidth utilization can be changed.

## Slide 11: Bandwidth Utilization over WAN Interfaces
  Bandwidth utilization over point-to-point subinterfaces using Frame Relay:
    Treats bandwidth as T1 by default
    Should manually configure bandwidth as the CIR of the PVC
  Bandwidth utilization over multipoint Frame Relay, ATM, and ISDN PRI:
    EIGRP uses the bandwidth on the physical interface divided by the number of neighbors on that interface to calculate the bandwidth attributed per neighbor.

## Slide 12: Bandwidth Utilization over WAN Interfaces (Cont.)
  Each PVC can have a different CIR, creating an EIGRP packet-pacing problem.
  Multipoint interfaces:
    Convert these to point-to-point configuration or manually configure bandwidth by multiplying the lowest CIR by the number of PVCs.

## Slide 13: EIGRP WAN Configuration: Frame Relay Hub-and-Spoke Topology
Configure each virtual Circuit as point-to-point, specify bandwidth = 1/10 of link capacity
Increase EIGRP utilization to 50% of actual VC capacity
Notes: <number>

## Slide 14: EIGRP WAN Configuration: Hybrid Multipoint
  Configure lowest CIR virtual circuit as point-to-point, specify bandwidth = CIR.
  Configure higher CIR virtual circuits as multipoint, combine CIRs.
Notes: <number>

## Slide 15: Summary
  EIGRP performs automatic network-boundary summarization, but administrators can disable automatic summarization and perform manual route summarization on an interface-by-interface basis. Summarizing routes creates smaller routing tables.
  Use the no auto-summary command to disable automatic summarization. Use the ip summary-address eigrp command to create a summary address.
  EIGRP performs equal-cost load balancing by default for up to four paths (up to six paths can be supported).
  Use the variance command to configure unequal-cost load balancing.
Notes: <number>

## Slide 16: Summary (Cont.)
  EIGRP uses up to 50 percent of the bandwidth of an interface by default. Because of the inherent differences in the operational characteristics of WAN links, this default may not be the best option for all WAN links.
  Use the ip bandwidth-percent eigrp command to configure EIGRP bandwidth use across WAN links.
Notes: <number>