## Slide 1: Configuring EIGRP
Using EIGRP in an Enterprise Network

## Slide 2: Factors That Influence EIGRP Scalability
  Quantity of routing information exchanged between peers; without proper route summarization, this can be excessive.
  Number of routers that must be involved when a topology change occurs.
  Depth of topology: the number of hops that information must travel to reach all routers.
  Number of alternate paths through the network.

## Slide 3: EIGRP Query Process
  Queries are sent when a route is lost and no feasible successor is available.
  The lost route is now in active state.
  Queries are sent to all neighboring routers on all interfaces except the interface to the successor.
  If the neighbors do not have the lost-route information, queries are sent to their neighbors.
  If a router has an alternate route, it answers the query; this stops the query from spreading in that branch of the network.

## Slide 4: Updates and Queries in Hub-and-Spoke Topology
You do not want to use these paths!
Notes: <number>

## Slide 5: EIGRP Stub
  The EIGRP stub routing feature improves network stability, reduces resource utilization, and simplifies remote router (spoke) configuration.
  Stub routing is commonly used in a hub-and-spoke topology.
  A stub router sends a special peer information packet to all neighboring routers to report its status as a stub router.
  A neighbor that receives a packet informing it of the stub status does not query the stub router for any routes.

## Slide 6: Configuring EIGRP Stub
  receive-only: Prevents the stub from sending any type of route.
  connected: Permits stub to send connected routes (may still need to redistribute).
  static: Permits stub to send static routes (must still redistribute).
  summary: Permits stub to send summary routes.
  Default is connected and summary.
eigrp stub [receive-only|connected|static|summary]
Router(config-router)#

## Slide 7: Limiting Updates and Queries: Using EIGRP Stub
Notes: <number>

## Slide 8: Example: eigrp stub Parameters
If stub connected is configured:
  B will advertise 10.1.2.0/24 to A.
  B will not advertise 10.1.2.0/23, 10.1.3.0/23, or 10.1.4.0/24.
If stub summary is configured:
  B will advertise 10.1.2.0/23 to A.
  B will not advertise 10.1.2.0/24, 10.1.3.0/24, or 10.1.4.0/24.

## Slide 9: Example: eigrp stub Parameters (Cont.)
If stub static is configured:
  B will advertise 10.1.4.0/24 to A.
  B will not advertise 10.1.2.0/24, 10.1.2.0/23, or 10.1.3.0/24.
If stub receive-only is configured:
  B will not advertise anything to A, so A needs to have a static route to the networks behind B to reach them.

## Slide 10: EIGRP Query Process Stuck in Active
  The router has to get all the replies from the neighbors with an outstanding query before the router calculates the successor information.
  If any neighbor fails to reply to the query within 3 minutes by default, the route is SIA, and the router resets the neighbor relationship with the neighbor that fails to reply.

## Slide 11: Active Process Enhancement
Before
Router A resets relationship to router B when the normal active timer expires. However, the problem is the link between router B and C.
After
Router A sends an SIA-Query at half of the normal active timer. Router B acknowledges the query there by keeping the relationship up.
Notes: Instructions: Please add this as new page in module 3, lesson 6 after “EIGRP Query Process SIA” page 3-87.
Use the given ppt for visual and the below text for content in ms-word.
SIA-Query and SIA-Reply are two new additions to the TVL (Type/Value/Length) triplets in the EIGRP packet header. These are generated automatically with no configuration from IOS version 12.1(5) and later. These packets allow an EIGRP router to monitor the progression of the search for a successor route and ensure that the neighbor is still reachable. The result is improved network reliability by reducing the unintended termination of neighbor adjacency.
The figure shows router A sending a query for network 10.1.1.0/24 to router B. Router B has no entry and in turn queries router C. If problems exist between router B and C, the reply packet from router C to router B may be delayed or lost. Router A has no visibility of downstream progress and assumes that no response indicates problems with router B. After router A’s three minute active timer expires, the neighbor relationship with router B is reset along with all known router from router B.
SIA-Query allows router A to query status at the midway point of the active timer to the downstream router B. Router B responds that it is searching for a replacement route. Upon receiving this SIA-Reply response packet, router A will validate the status of router B and not terminate the relationship. Meanwhile router B will send up to three SIA-Queries that go unanswered from router C. Router B will then terminate the neighbor relationship with router C. Then router B will update router A that the network 10.1.1.0/24 is unreachable. Router A and B then remove the active router from their topology tables and their neighbor relationship remains intact between router A and B.

## Slide 12: Graceful Shutdown

## Slide 13: Summary
  Factors that affect network scalability include these:
    Amount of information exchanged between neighbors
    Number of routers
    Depth of the topology
    Number of alternate paths through the network
  When a route is lost and no feasible successor is available, queries are sent to all neighboring routers on all interfaces.
  The eigrp stub command is used to enable the stub routing feature, which improves network stability, reduces resource utilization, and simplifies stub router configuration.
Notes: <number>

## Slide 14: Summary (Cont.)
  After a route goes active and the query sequence is initiated, it can only come out of the active state and move to passive state when it receives a reply for every generated query. If the router does not receive a reply to all the outstanding queries within 3 minutes (the default time), the route goes to the SIA state.
  The active process enhancement feature enables an EIGRP router to monitor the progression of the search for a successor route so that neighbor relationships are not reset unnecessarily.
  With graceful shutdown, a goodbye message is broadcast when an EIGRP routing process is shut down, to inform adjacent peers about the impending topology change.
Notes: <number>