## Slide 1: Configuring OSPF
Introducing the OSPF Protocol

## Slide 2: Link-State Protocols
Notes: <number>

## Slide 3: Link-State Data Structures
  Neighbor table:
    Also known as the adjacency database
    Contains list of recognized neighbors
  Topology table:
    Typically referred to as LSDB
    Contains all routers and their attached links in the area or network
    Identical LSDB for all routers within an area
  Routing table:
    Commonly named a forwarding database
    Contains list of best paths to destinations

## Slide 4: Link-State Routing Protocols
  Link-state routers recognize more information about the network than their distance vector counterparts.
  Each router has a full picture of the topology.
  Consequently, link-state routers tend to make more accurate decisions.

## Slide 5: Link-State Data Structure: Network Hierarchy
  Link-state routing requires a hierachical network structure that is enforced by OSPF.
  This two-level hierarchy consists of the following:
    Transit area (backbone or area 0)
    Regular areas (nonbackbone areas)

## Slide 6: OSPF Areas
OSPF area characteristics:
  Minimizes routing table entries
  Localizes impact of a topology change within an area
  Detailed LSA flooding stops at the area boundary
  Requires a hierarchical network design
Notes: <number>

## Slide 7: Area Terminology
  Routers A and B are backbone routers.
  Backbone routers make up area 0.
  Routers C, D, and E are known as area border routers (ABRs).
  ABRs attach all other areas to area 0.
Notes: <number>

## Slide 8: OSPF Adjacencies
  Routers discover neighbors by exchanging hello packets.
  Routers declare neighbors to be up after checking certain parameters or options in the hello packet.

## Slide 9: Forming OSPF Adjacencies
  Point-to-point WAN links:
    Both neighbors become fully adjacent.
  LAN links:
    Neighbors form a full adjacency with the DR and BDR.
    Routers maintain two-way state with the other routers (DROTHERs).
  Routing updates and topology information are passed only between adjacent routers.
  Once an adjacency is formed, LSDBs are synchronized by exchanging LSAs.
  LSAs are flooded reliably throughout the area (or network).
Notes: <number>

## Slide 10: OSPF Calculation
Routers find the best paths to destinations by applying Dijkstra’s SPF algorithm to the link-state database as follows:
  Every router in an area has the identical link-state database.
  Each router in the area places itself into the root of the tree that is built.
  The best path is calculated with respect to the lowest total cost of links to a specific destination.
  Best routes are put into the forwarding database (routing table).

## Slide 11: SPF Calculation
Assume all links are Ethernet, with an OSPF cost of 10.
Notes: <number>

## Slide 12: Link-State Data Structures: LSA Operation
Notes: <number>

## Slide 13: Summary
  Link-state routing protocols respond quickly to changes, send triggered updates when changes occur, and send periodic updates every 30 minutes.
  A two-tier hierarchical network structure is used by OSPF in which the network is divided into areas. This area structure is used to separate the LSDB into more manageable sizes.
  Adjacencies are built by OSPF routers using the Hello protocol. Over these logical adjacencies, LSUs are sent to exchange database information between adjacent OSPF routers.
Notes: <number>

## Slide 14: Summary (Cont.)
  Dijkstra’s SPF algorithm is used to calculate best paths for all destinations. SPF is run against the LSDB, and the outcome is a table of best paths, known as the routing table.
  After an LSA entry ages, the router that originated the entry sends an LSU about the network to verify that the link is still active. The LSU can contain one or more LSAs.
Notes: <number>