## Slide 1: Configuring OSPF
Configuring OSPF Routing

## Slide 2: Configuring Basic OSPF
router ospf process-id [vrf vpn-name]
Router(config)#
Enables one or more OSPF routing processes
network ip-address wildcard-mask area area-id
Router(config-router)#
Defines the interfaces that OSPF will run on
Router(config-if)#
ip ospf process-id area area-id [secondaries none]
Optional method to enable OSPF explicitly on an interface

## Slide 3: Configuring OSPF on Internal Routers of a Single Area
Notes: <number>

## Slide 4: Configuring OSPF for Multiple Areas
Notes: <number>

## Slide 5: OSPF Router ID
  The router is known to OSPF by the OSPF router ID number.
  LSDBs use the OSPF router ID to differentiate one router from the next.
  By default, the router ID is the highest IP address on an active interface at the moment of OSPF process startup.
  A loopback interface can override the OSPF router ID. If a loopback interface exists, the router ID is the highest IP address on any active loopback interface.
  The OSPF router-id command can be used to override the OSPF router ID.
  Using a loopback interface or a router-id command is recommended for stability.

## Slide 6: Loopback Interfaces
Router(config)#interface loopback 0
Router(config-if)#ip address 172.16.17.5 255.255.255.255
  If the OSPF process is already running, the router must be reloaded or the OSPF process must be removed and reconfigured before the new loopback address will take effect.
Notes: <number>

## Slide 7: OSPF router-id Command
router-id ip-address
  This command is configured under the router ospf [process-id] command.
  Any unique arbitrary 32-bit value in an IP address format (dotted decimal) can be used.
  If this command is used on an OSPF process that is already active, then the new router ID is used after the next reload or manual OSPF process restart using:
Router(config-router)#
Router(config)#router ospf 1
Router(config-router)#router-id 172.16.1.1
Router#clear ip ospf process
clear ip ospf process
Router#

## Slide 8: OSPF Router ID Verification
RouterB#sh ip ospf
Routing Process "ospf 50" with ID 10.64.0.2
<output omitted>
Number of areas in this router is 2. 2 normal 0 stub 0 nssa
Number of areas transit capable is 0
External flood list length 0
Area BACKBONE(0)
Area BACKBONE(0)
Area has no authentication
SPF algorithm last executed 00:01:25.028 ago
SPF algorithm executed 7 times
<output omitted>
Area 1
Number of interfaces in this area is 1
Area has no authentication
SPF algorithm last executed 00:00:54.636 ago
SPF algorithm executed 3 times
<output omitted>

## Slide 9: Verifying OSPF Operation
show ip protocols
Router#
Verifies the configured IP routing protocol processes, parameters, and statistics
show ip route ospf [process-id ]
Router#
Displays all OSPF routes learned by the router
show ip ospf interface [type number]
Router#
Displays the OSPF router ID, area ID, and adjacency information

## Slide 10: Verifying OSPF Operation (Cont.)
show ip ospf
Router#
Displays the OSPF router ID, timers, and statistics
show ip ospf neighbor [type number] [neighbor-id] [detail]
Router#
Displays information about the OSPF neighbors, including DR and BDR information on broadcast networks

## Slide 11: Example: The show ip route ospf Command
RouterA#show ip route ospf
10.0.0.0/8 is variably subnetted, 3 subnets, 2 masks
O IA 10.2.1.0/24 [110/782] via 10.64.0.2, 00:03:05, FastEthernet0/0
RouterA#

## Slide 12: Example: The show ip ospf interface Command
RouterA#show ip ospf interface fastEthernet 0/0
FastEthernet0/0 is up, line protocol is up
Internet Address 10.64.0.1/24, Area 0
Process ID 1, Router ID 10.64.0.1, Network Type BROADCAST, Cost: 1
Transmit Delay is 1 sec, State DROTHER, Priority 0
Designated Router (ID) 10.64.0.2, Interface address 10.64.0.2
No backup designated router on this network
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
oob-resync timeout 40
Hello due in 00:00:04
Supports Link-local Signaling (LLS)
Index 1/1, flood queue length 0
Next 0x0(0)/0x0(0)
Last flood scan length is 1, maximum is 4
Last flood scan time is 0 msec, maximum is 4 msec
Neighbor Count is 1, Adjacent neighbor count is 1
Adjacent with neighbor 10.64.0.2 (Designated Router)
Suppress hello for 0 neighbor(s)

## Slide 13: Example: The show ip ospf neighbor Command
RouterB# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
10.64.0.1 0 FULL/DROTHER 00:00:30 10.64.0.1 FastEthernet0/0
10.2.1.1 0 FULL/ - 00:00:34 10.2.1.1 Serial0/0/1
RouterB# show ip ospf neighbor detail
Neighbor 10.64.0.1, interface address 10.64.0.1
In the area 0 via interface FastEthernet0/0
Neighbor priority is 0, State is FULL, 16 state changes
DR is 10.64.0.2 BDR is 0.0.0.0
<output omitted>
Neighbor 10.2.1.1, interface address 10.2.1.1
In the area 1 via interface Serial0/0/1
Neighbor priority is 0, State is FULL, 6 state changes
DR is 0.0.0.0 BDR is 0.0.0.0
<output omitted>

## Slide 14: Summary
  Configuration of OSPF is a two-step process:
    Enter OSPF configuration with the router ospf command.
    Use the network command to describe which interfaces will run OSPF in which area.
  OSPF selects a router ID at startup time:
    The router ID’s specified in the router-id command under the OSPF process.
    Otherwise, the highest IP address of a loopback interface, if there are any, is used.
    By default, the highest IP address of all active interfaces
  Use the show ip ospf command to verify the router ID.
  Use the show ip protocols, show ip route ospf, show ip ospf interface, show ip ospf, and show ip ospf neighbor commands to verify OSPF operation.
Notes: <number>