## Slide 1: Configuring OSPF
OSPF Network Types

## Slide 2: OSPF Network Types
The three types of networks defined by OSPF are:
  Point-to-point: A network that joins a single pair of routers.
  Broadcast: A multiaccess broadcast network, such as Ethernet.
  Nonbroadcast multiaccess (also called NBMA): A network that interconnects more than two routers but that has no broadcast capability. Frame Relay, ATM, and X.25 are examples of NBMA networks.
    Five modes of OSPF operation are available for NBMA networks.

## Slide 3: Point-to-Point Links
  Usually a serial interface running either PPP or HDLC.
  May also be a point-to-point subinterface running Frame Relay or ATM.
  No DR or BDR election required.
  OSPF autodetects this interface type.
  OSPF packets are sent using multicast 224.0.0.5.
Notes: <number>

## Slide 4: Multiaccess Broadcast Network
  Generally these are, LAN technologies like Ethernet and Token Ring.
  DR and BDR selection are required.
  All neighbor routers form full adjacencies with the DR and BDR only.
  Packets to the DR and the BDR use 224.0.0.6.
  Packets from DR to all other routers use 224.0.0.5.
Notes: <number>

## Slide 5: Electing the DR and BDR
  Hello packets are exchanged via IP multicast.
  The router with the highest OSPF priority is selected as the DR. The router with the second-highest priority value is the BDR.
  Use the OSPF router ID as the tiebreaker.
  The DR election is nonpreemptive.
Notes: <number>

## Slide 6: Setting Priority for DR Election
  This interface configuration command assigns the OSPF priority to an interface.
  Different interfaces on a router may be assigned different values.
  The default priority is 1. The range is from 0 to 255.
  0 means the router cannot be the DR or BDR.
  A router that is not the DR or BDR is DROTHER.
ip ospf priority number
Router(config-if)#

## Slide 7: NBMA Topology
  A single interface interconnects multiple sites.
  NBMA topologies support multiple routers, but without broadcasting capabilities.
Notes: <number>

## Slide 8: DR Election in NBMA Topology
  OSPF considers NBMA to be like other broadcast media.
  The DR and BDR need to have fully meshed connectivity with all other routers, but NBMA networks are not always fully meshed.
  The DR and BDR need a list of neighbors.
  OSPF neighbors are not automatically discovered by the router.

## Slide 9: Frame Relay Topologies
Notes: <number>

## Slide 10: OSPF over NBMA Topology Modes of Operation
  RFC 2328-compliant modes are as follows:
    Nonbroadcast (NBMA)
    Point-to-multipoint
  Additional modes from Cisco are as follows:
    Point-to-multipoint nonbroadcast
    Broadcast
    Point-to-point

## Slide 11: Selecting the OSPF Network Type for NBMA Networks
ip ospf network [{broadcast | non-broadcast | point-to-multipoint [non-broadcast] | point-to-point}]
  Defines OSPF network type
Router(config-if)#
Router(config)#interface serial 0/0/0
Router(config-if)#encapsulation frame-relay
Router(config-if)#ip ospf network broadcast
Example: Broadcast Mode

## Slide 12: Nonbroadcast Mode (NBMA Mode)
  Treated as a broadcast network by OSPF (acts like a LAN).
  All serial ports are part of the same IP subnet.
  Frame Relay, X.25, and ATM networks default to nonbroadcast mode.
  Neighbors must be statically configured.
  Duplicates LSA updates.
  Complies with RFC 2328.
Notes: <number>

## Slide 13: Using the neighbor Command
  Used to statically define neighbor relationships in an NBMA network
neighbor ip-address [priority number] [poll-interval number] [cost number] [database-filter all]
Router(config-router)#

## Slide 14: neighbor Command Example
RouterA(config)# router ospf 100
RouterA(config-router)# network 192.168.0.0 0.0.255.255 area 0
RouterA(config-router)# neighbor 192.168.1.2 priority 0
RouterA(config-router)# neighbor 192.168.1.3 priority 0
RouterA(config-router)# network 172.16.0.0 0.0.255.255 area 0

## Slide 15: The show ip ospf neighbor Command
RouterA# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
192.168.1.3 0 FULL/DROTHER 00:01:57 192.168.1.3 Serial0/0/0
192.168.1.2 0 FULL/DROTHER 00:01:33 192.168.1.2 Serial0/0/0
172.16.1.1 1 FULL/BDR 00:00:34 172.16.1.1 FastEthernet0/0

## Slide 16: Point-to-Multipoint Mode
  The point-to-multipoint mode allows for NBMA networking.
  The point-to-multipoint mode fixes partial-mesh and star topologies.
  No DR is required and only a single subnet is used.
  A 30-second hello is used.
  This mode is RFC 2328-compliant.
Notes: <number>

## Slide 17: Point-to-Multipoint Configuration
interface Serial0/0/0
ip address 192.168.1.1 255.255.255.0
encapsulation frame-relay
ip ospf network point-to-multipoint
<output omitted>
router ospf 100
log-adjacency-changes
network 172.16.0.0 0.0.255.255 area 0
network 192.168.0.0 0.0.255.255 area 0
interface Serial0/0/0
ip address 192.168.1.3 255.255.255.0
encapsulation frame-relay
ip ospf network point-to-multipoint
ip ospf priority 0
Router A
Router C

## Slide 18: Point-to-Multipoint Example
RouterA#sh ip ospf int s0/0/0
Serial0/0/0 is up, line protocol is up
Internet Address 192.168.1.1/24, Area 0
Process ID 100, Router ID 192.168.1.1, Network Type POINT_TO_MULTIPOINT, Cost: 781
Transmit Delay is 1 sec, State POINT_TO_MULTIPOINT
Timer intervals configured, Hello 30, Dead 120, Wait 120, Retransmit 5
oob-resync timeout 120
Hello due in 00:00:26
Supports Link-local Signaling (LLS)
Index 2/2, flood queue length 0
Next 0x0(0)/0x0(0)
Last flood scan length is 1, maximum is 1
Last flood scan time is 0 msec, maximum is 4 msec
Neighbor Count is 2, Adjacent neighbor count is 2
Adjacent with neighbor 192.168.1.3
Adjacent with neighbor 192.168.1.2
Suppress hello for 0 neighbor(s)
RouterA#

## Slide 19: Point-to-Multipoint Nonbroadcast
  Cisco extension to RFC-compliant point-to-multipoint mode
  Must statically define neighbors, like nonbroadcast mode
  Like point-to-multipoint mode, DR and BDR not elected
  Used in special cases where neighbors cannot be automatically discovered

## Slide 20: Using Subinterfaces
  The physical serial port becomes multiple logical ports.
  Each subinterface requires an IP subnet.
interface serial number.subinterface-number {multipoint | point-to-point}
Router(config)#

## Slide 21: Point-to-Point Subinterfaces
  Each PVC and SVC gets its own subinterface.
  OSPF point-to-point mode is the default on point-to-point Frame Relay subinterfaces.
    No DR/BDR
    Do not need to configure neighbors
interface serial number.subinterface-number point-to-point
Router(config)#

## Slide 22: Point-to-Point Subinterface Example
  PVCs are treated like point-to-point links.
  Each subinterface requires a subnet.
Notes: <number>

## Slide 23: Multipoint Subinterfaces
  Multiple PVCs and SVCs are on a single subinterface.
  OSPF nonbroadcast mode is the default.
    DR and BDR are required.
    Neighbors need to be statically configured.
interface serial number.subinterface-number multipoint
Router(config)#

## Slide 24: Multipoint Subinterface Example
  Single interface serial 0/0/0 has been logically separated into two subinterfaces: one point-to-point (S0/0/0.1) and one point-to-multipoint (S0/0/0.2).
  Each subinterface requires a subnet.
  OSPF defaults to point-to-point mode on point-to-point subinterfaces.
  OSPF defaults to nonbroadcast mode on point-to-multipoint subinterfaces.
Notes: <number>

## Slide 25: OSPF over NBMA Topology Summary
OSPF Mode | NBMA Preferred Topology | Subnet Address | Hello Timer | Adjacency | RFC or Cisco
Broadcast | Full or partial mesh | Same | 10 sec | Automatic, DR/BDR elected | Cisco
Nonbroadcast (NBMA) | Full or partial mesh | Same | 30 sec | Manual configuration, DR/BDR elected | RFC
Point-to-multipoint | Partial-mesh or star | Same | 30 Sec | Automatic, no DR/BDR | RFC
Point-to-multipoint nonbroadcast | partial-mesh or star | Same | 30 sec | Manual configuration, no/DR/BDR | Cisco
Point-to-point | Partial-mesh or star, using subinterface | Different for Each Subinterface | 10 sec | Automatic, no DR/BDR | Cisco
Notes: <number>

## Slide 26: Creation of Adjacencies for Point-to-Point Mode
RouterA# debug ip ospf adj
OSPF: Interface Serial0/0/0.1 going Up
OSPF: Build router LSA for area 0, router ID 192.168.1.1, seq 0x80000023
OSPF: Rcv DBD from 192.168.1.2 on Serial0/0/0.1 seq 0xCF0 opt 0x52 flag 0x7 len 32 mtu 1500 state INIT
OSPF: 2 Way Communication to 192.168.1.2 on Serial0/0/0.1, state 2WAY
OSPF: Send DBD to 192.168.1.2 on Serial0/0/0.1 seq 0xF4D opt 0x52 flag 0x7 len 32
OSPF: NBR Negotiation Done. We are the SLAVE
OSPF: Send DBD to 192.168.1.2 on Serial0/0/0.1 seq 0xCF0 opt 0x52 flag 0x2 len 132
OSPF: Rcv DBD from 192.168.1.2 on Serial0/0/0.1 seq 0xCF1 opt 0x52 flag 0x3 len 132 mtu 1500 state EXCHANGE
OSPF: Send DBD to 192.168.1.2 on Serial0/0/0.1 seq 0xCF1 opt 0x52 flag 0x0 len 32
OSPF: Database request to 192.168.1.2
OSPF: sent LS REQ packet to 192.168.1.2, length 12
OSPF: Rcv DBD from 192.168.1.2 on Serial0/0/0.1 seq 0xCF2 opt 0x52 flag 0x1 len 32 mtu 1500 state EXCHANGE
OSPF: Exchange Done with 192.168.1.2 on Serial0/0/0.1
OSPF: Send DBD to 192.168.1.2 on Serial0/0/0.1 seq 0xCF2 opt 0x52 flag 0x0 len 32
OSPF: Synchronized with 192.168.1.2 on Serial0/0/0.1, state FULL
%OSPF-5-ADJCHG: Process 100, Nbr 192.168.1.2 on Serial0/0/0.1 from LOADING to FULL, Loading Done
OSPF: Build router LSA for area 0, router ID 192.168.1.1, seq 0x80000024

## Slide 27: Creation of Adjacencies for Broadcast Mode
RouterA# debug ip ospf adj
OSPF: Interface FastEthernet0/0 going Up
OSPF: Build router LSA for area 0, router ID 192.168.1.1,seq 0x80000008
OSPF: 2 Way Communication to 172.16.1.1 on FastEthernet0/0, state 2WAY
OSPF: end of Wait on interface FastEthernet0/0
<output omitted>
OSPF: Neighbor change Event on interface FastEthernet0/0
OSPF: DR/BDR election on FastEthernet0/0
OSPF: Elect BDR 172.16.1.1
OSPF: Elect DR 192.168.1.1
DR: 192.168.1.1 (Id) BDR: 172.16.1.1 (Id)
OSPF: Rcv DBD from 172.16.1.1 on FastEthernet0/0 seq 0x14B 7 opt 0x52 flag 0x7 len 32 mtu 1500 state EXSTART
OSPF: First DBD and we are not SLAVE-if)#
OSPF: Send DBD to 172.16.1.1 on FastEthernet0/0 seq 0xDCE opt 0x52 flag 0x7 len 32
OSPF: Retransmitting DBD to 172.16.1.1 on FastEthernet0/0[1]
OSPF: Rcv DBD from 172.16.1.1 on FastEthernet0/0 seq 0xDCE
opt 0x52 flag 0x2 len 152 mtu 1500 state EXSTART
<output omitted>

## Slide 28: Summary
  OSPF defines three types of networks: point-to-point, broadcast, and NBMA.
  On point-to-point links, adjacency is dynamic, uses multicast addresses, and has no DR or BDR.
  On broadcast links, adjacency is dynamic and includes election of a DR and BDR. All updates are sent to the DR, which forwards the updates to all routers.
  The router with the highest OSPF priority is selected as the DR. The router with the second-highest priority value is the BDR.
  By default on NBMA links, adjacency requires manual definition of neighbors for the DR and BDR because OSPF will consider the network similar to broadcast media.
Notes: <number>

## Slide 29: Summary (Cont.)
  The OSPF mode of operation on Frame Relay depends on the underlying Frame Relay network. OSPF mode options include nonbroadcast, broadcast, point-to-multipoint, point-to-multipoint nonbroadcast, and point-to-point.
  In nonbroadcast mode, a DR and BDR are elected, and neighbors must be statically configured.
  In point-to-multipoint mode, no DR and BDR are needed and neighbors are automatically discovered. In point-to-multipoint nonbroadcast mode, no DR and BDR are needed, but neighbors must be statically configured.
  A physical interface can be split into multiple logical interfaces called subinterfaces. Each subinterface requires an IP subnet.
  Using the debug ip ospf adj command enables you to see OSPF packet exchanges and the status of neighbor adjacencies.
Notes: <number>