## Slide 1: Configuring OSPF
Link-State Advertisements

## Slide 2: Issues with Maintaining a Large OSPF Network
Notes: <number>

## Slide 3: The Solution: OSPF Hierarchical Routing
  Consists of areas and autonomous systems
  Minimizes routing update traffic

## Slide 4: Types of OSPF Routers
Notes: <number>

## Slide 5: Defining Virtual Links
  Virtual links are used to connect a discontiguous area to area 0.
  A logical connection is built between router A and router B.
  Virtual links are recommended for backup or temporary connections.
Notes: <number>

## Slide 6: Configuring Virtual Links
area area-id virtual-link router-id [authentication [message-digest | null]] [hello-interval seconds] [retransmit-interval seconds] [transmit-delay seconds] [dead-interval seconds] [[authentication-key key] | [message-digest-key key-id md5 key]]
Router(config-router)#
Creates a virtual link
remoterouter#sh ip ospf
Routing Process "ospf 1000" with ID 10.2.2.2
Supports only single TOS(TOS0) routes
Supports opaque LSA
Supports Link-local Signaling (LLS)
Supports area transit capability
It is an area border router
<output omitted>

## Slide 7: OSPF Virtual Link Configuration Example
Notes: <number>

## Slide 8: The show ip ospf virtual-links Command
RouterA#sh ip ospf virtual-links
Virtual Link OSPF_VL0 to router 10.2.2.2 is up
Run as demand circuit
DoNotAge LSA allowed.
Transit area 1, via interface Serial0/0/1, Cost of using 781
Transmit Delay is 1 sec, State POINT_TO_POINT,
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
Hello due in 00:00:07
Adjacency State FULL (Hello suppressed)
Index 1/2, retransmission queue length 0, number of retransmission 1
First 0x0(0)/0x0(0) Next 0x0(0)/0x0(0)
Last retransmission scan length is 1, maximum is 1
Last retransmission scan time is 0 msec, maximum is 0 msec
RouterA#

## Slide 9: LSA Types
LSA Type | Description
1 | Router LSAs
2 | Network LSAs
3 or 4 | Summary LSAs
5 | Autonomous system external LSAs
6 | Multicast OSPF LSA
7 | Defined for not-so-stubby areas
8 | External attributes LSA for Border Gateway Protocol (BGP)
9, 10, 11 | Opaque LSAs
Notes: <number>

## Slide 10: LSA Type 1: Router LSA
  One router LSA (type 1) for every router in an area
    Includes list of directly attached links
    Each link identified by IP prefix assigned to link and link type
  Identified by the router ID of the originating router
  Floods within its area only; does not cross ABR

## Slide 11: LSA Type 2: Network LSA
  One network (type 2) LSA for each transit broadcast or NBMA network in an area
    Includes list of attached routers on the transit link
    Includes subnet mask of link
  Advertised by the DR of the broadcast network
  Floods within its area only; does not cross ABR

## Slide 12: LSA Type 3: Summary LSA
  Type 3 LSAs are used to flood network information to areas outside the originating area (interarea)
    Describes network number and mask of link.
  Advertised by the ABR of originating area.
  Regenerated by subsequent ABRs to flood throughout the autonomous system.
  By default, routes are not summarized, and type 3 LSA is advertised for every subnet.

## Slide 13: LSA Type 4: Summary LSA
  Summary (type 4) LSAs are used to advertise an ASBR to all other areas in the autonomous system.
  They are generated by the ABR of the originating area.
  They are regenerated by all subsequent ABRs to flood throughout the autonomous system.
  Type 4 LSAs contain the router ID of the ASBR.

## Slide 14: LSA Type 5: External LSA
  External (type 5) LSAs are used to advertise networks from other autonomous systems.
  Type 5 LSAs are advertised and owned by the originating ASBR.
  Type 5 LSAs flood throughout the entire autonomous system.
  The advertising router ID (ASBR) is unchanged throughout the autonomous system.
  Type 4 LSA is needed to find the ASBR.
  By default, routes are not summarized.

## Slide 15: Interpreting the OSPF Database
RouterA#show ip ospf database
OSPF Router with ID (10.0.0.11) (Process ID 1)
Router Link States (Area 0)
Link ID ADV Router Age Seq# Checksum Link count
10.0.0.11 10.0.0.11 548 0x80000002 0x00401A 1
10.0.0.12 10.0.0.12 549 0x80000004 0x003A1B 1
100.100.100.100 100.100.100.100 548 0x800002D7 0x00EEA9 2
Net Link States (Area 0)
Link ID ADV Router Age Seq# Checksum
172.31.1.3 100.100.100.100 549 0x80000001 0x004EC9
Summary Net Link States (Area 0)
Link ID ADV Router Age Seq# Checksum
10.1.0.0 10.0.0.11 654 0x80000001 0x00FB11
10.1.0.0 10.0.0.12 601 0x80000001 0x00F516
<output omitted>
Notes: <number>

## Slide 16: Interpreting the Routing Table: Types of Routes
Router Designator |  | Description
O | OSPF intra-area (router LSA) and network LSA | Networks from within the area of the router Advertised by way of router LSAs and network LSA
O IA | OSPF interarea (summary LSA) | Networks from outside the area of the router, but within the OSPF autonomous system Advertised by way of summary LSAs
O E1 | Type 1 external routes | Networks outside of the autonomous system of the router Advertised by way of external LSAs
O E2 | Type 2 external routes | 
Notes: <number>

## Slide 17: Calculating Costs for E1 and E2 Routes
Notes: <number>

## Slide 18: The show ip route Command
RouterB>show ip route
Codes: C - connected, S - static, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2
i - IS-IS, su - IS-IS summary, L1 - IS-IS level-1, L2 - IS-IS level-2
ia - IS-IS inter area, * - candidate default, U - per-user static route
o - ODR, P - periodic downloaded static route
Gateway of last resort is not set
172.31.0.0/24 is subnetted, 2 subnets
O IA 172.31.2.0 [110/1563] via 10.1.1.1, 00:12:35, FastEthernet0/0
O IA 172.31.1.0 [110/782] via 10.1.1.1, 00:12:35, FastEthernet0/0
10.0.0.0/8 is variably subnetted, 6 subnets, 2 masks
C 10.200.200.13/32 is directly connected, Loopback0
C 10.1.3.0/24 is directly connected, Serial0/0/0
O 10.1.2.0/24 [110/782] via 10.1.3.4, 00:12:35, Serial0/0/0
C 10.1.1.0/24 is directly connected, FastEthernet0/0
O 10.1.0.0/24 [110/782] via 10.1.1.1, 00:12:37, FastEthernet0/0
O E2 10.254.0.0/24 [110/50] via 10.1.1.1, 00:12:37, FastEthernet0/0
Notes: <number>

## Slide 19: OSPF LSDB Overload Protection
  Excessive LSAs generated by other routers can drain local router resources.
  This feature can limit the processing of non-self-generated LSAs for a defined OSPF process.
max-lsa maximum-number [threshold-percentage] [warning-only] [ignore-time minutes] [ignore-count count-number] [reset-time minutes]
Router(config-router)#

## Slide 20: Changing the Cost Metric
ip ospf cost interface-cost
Overrides the default cost calculation. Values from 1 to 65535 can be defined.
auto-cost reference-bandwidth ref-bw
Sets the reference bandwidth to values other than 100 Mbps (legal values range from 1 to 4,294,967 in megabits per second).
Dijkstra’s algorithm determines the best path by adding all link costs along a path.
The cost, or metric, is an indication of the overhead to send packets over an interface. Default = (100 Mbps) / (bandwidth in Mbps).
RouterA(config-if)#
RouterA(config-router)#

## Slide 21: Summary
  There are four OSPF router types: internal routers, backbone routers, ABRs, and ASBRs.
  A virtual link allows discontiguous area 0’ to be connected, or a disconnected area to be connected to area 0, via a transit area. Virtual links should be used only for temporary connections or backup after a failure, not as a primary backbone design feature.
  There are 11 OSPF LSA types. The first five are the most commonly used:
    Type 1 router
    Type 2 network
    Type 3 and 4 summary
    Type 5 external
Notes: <number>

## Slide 22: Summary (Cont.)
  In the IP routing table, OSPF routes are classified as either intra-area, interarea, or external; external routes are subdivided into E1 and E2.
  OSPF LSDB overload protection limits the processing of non-self-generated LSAs.
  The OSPF cost defaults to (100 Mbps) / (bandwidth in megabits per second). The cost can be changed on a per-interface basis, and the reference bandwidth (100 Mbps) can also be changed.
Notes: <number>