## Slide 1: Configuring OSPF
OSPF Route Summarization

## Slide 2: Benefits of Route Summarization
  Minimizes number of routing table entries
  Localizes impact of a topology change
  Reduces LSA type 3 and 5 flooding and saves CPU resources

## Slide 3: Using Route Summarization
  Interarea summary link carries mask.
  One or more entries can represent several subnets.

## Slide 4: Configuring Route Summarization
area area-id range address mask [advertise | not-advertise] [cost cost]
Router(config-router)#
Consolidates interarea routes on an ABR
summary-address ip-address mask [not-advertise] [tag tag]
Router(config-router)#
Consolidates external routes, usually on an ASBR

## Slide 5: Route Summarization Configuration Example at ABR
Notes: <number>

## Slide 6: Route Summarization Configuration Example at ASBR

## Slide 7: Default Routes in OSPF
  A default route is injected into OSPF as an external LSA type 5.
  Default route distribution is not on by default; use the default-information originate command under the OSPF routing process.

## Slide 8: Configuring OSPF Default Routes
Normally, this command advertises a 0.0.0.0 default into the OSPF network only if the default route already exists in the routing table.
The always keyword allows the 0.0.0.0 default to be advertised even when the default route does not exist in the routing table.
default-information originate [always] [metric metric-value] [metric-type type-value] [route-map map-name]
Router(config-router)#

## Slide 9: Default Route Configuration Example
Notes: <number>

## Slide 10: Summary
  Route summarization improves CPU utilization, reduces LSA flooding, and reduces routing table sizes.
  The area range command is used to summarize at the ABR. The summary-address command is used to summarize at the ASBR.
  Default routes can be used in OSPF to prevent the need for a specific route to all destination networks. The benefits include a much smaller routing table and LSDB, with complete reachability.
  OSPF uses the default-information originate command to inject a default route.
Notes: <number>