## Slide 1: Configuring OSPF
Configuring OSPF Special Area Types

## Slide 2: Types of Areas
Notes: <number>

## Slide 3: Stub and Totally Stub Area Rules
  An area can be stub or totally stub if:
  There is a single ABR, or if there is more than one ABR, suboptimal routing paths to other areas or external autonomous systems are acceptable.
  All routers in the area are configured as stub routers.
  There is no ASBR in the area.
  The area is not area 0.
  No virtual links go through the area.

## Slide 4: Using Stub Areas
  External LSAs are stopped.
  Default route is advertised into stub area by the ABR.
  All routers in area 50 must be configured as stub.
Notes: <number>

## Slide 5: Stub Area Configuration
area area-id stub [no-summary]
This command turns on stub area networking.
All routers in a stub area must use the stub command.
RouterA(config-router)#
area area-id default-cost cost
This command defines the cost of a default route sent into the stub area.
The default cost is 1.
RouterA(config-router)#

## Slide 6: OSPF Stub Area Configuration Example
Notes: <number>

## Slide 7: Using Totally Stubby Areas
  External LSAs are stopped.
  Summary LSAs are stopped.
  Routing table is reduced to a minimum.
  All routers must be configured as stub.
  ABR must be configured as totally stubby.
  This is a Cisco proprietary feature.
Notes: <number>

## Slide 8: Totally Stubby Configuration
area area-id stub no-summary
The addition of no-summary on the ABR creates a totally stubby area and prevents all summary LSAs from entering the stub area.
RouterA(config-router)#

## Slide 9: Totally Stubby Configuration Example
Notes: <number>

## Slide 10: Routing Table in a Standard Area
P1R3#sh ip route
<output omitted>
Gateway of last resort is not set
172.31.0.0/32 is subnetted, 4 subnets
O IA 172.31.22.4 [110/782] via 10.1.1.1, 00:02:44, FastEthernet0/0
O IA 172.31.11.1 [110/1] via 10.1.1.1, 00:02:44, FastEthernet0/0
O IA 172.31.11.2 [110/782] via 10.1.3.4, 00:02:52, Serial0/0/0
[110/782] via 10.1.1.1, 00:02:52, FastEthernet0/0
O IA 172.31.11.4 [110/782] via 10.1.1.1, 00:02:44, FastEthernet0/0
10.0.0.0/8 is variably subnetted, 7 subnets, 2 masks
O 10.11.0.0/24 [110/782] via 10.1.1.1, 00:03:22, FastEthernet0/0
C 10.200.200.13/32 is directly connected, Loopback0
C 10.1.3.0/24 is directly connected, Serial0/0/0
O 10.1.2.0/24 [110/782] via 10.1.3.4, 00:03:23, Serial0/0/0
C 10.1.1.0/24 is directly connected, FastEthernet0/0
O 10.1.0.0/24 [110/782] via 10.1.1.1, 00:03:23, FastEthernet0/0
O E2 10.254.0.0/24 [110/50] via 10.1.1.1, 00:02:39, FastEthernet0/0
P1R3#
Notes: <number>

## Slide 11: Routing Table in a Stub Area
P1R3#sh ip route
<output omitted>
Gateway of last resort is 10.1.1.1 to network 0.0.0.0
172.31.0.0/32 is subnetted, 4 subnets
O IA 172.31.22.4 [110/782] via 10.1.1.1, 00:01:49, FastEthernet0/0
O IA 172.31.11.1 [110/1] via 10.1.1.1, 00:01:49, FastEthernet0/0
O IA 172.31.11.2 [110/782] via 10.1.3.4, 00:01:49, Serial0/0/0
[110/782] via 10.1.1.1, 00:01:49, FastEthernet0/0
O IA 172.31.11.4 [110/782] via 10.1.1.1, 00:01:49, FastEthernet0/0
10.0.0.0/8 is variably subnetted, 6 subnets, 2 masks
O 10.11.0.0/24 [110/782] via 10.1.1.1, 00:01:50, FastEthernet0/0
C 10.200.200.13/32 is directly connected, Loopback0
C 10.1.3.0/24 is directly connected, Serial0/0/0
O 10.1.2.0/24 [110/782] via 10.1.3.4, 00:01:50, Serial0/0/0
C 10.1.1.0/24 is directly connected, FastEthernet0/0
O 10.1.0.0/24 [110/782] via 10.1.1.1, 00:01:50, FastEthernet0/0
O*IA 0.0.0.0/0 [110/2] via 10.1.1.1, 00:01:51, FastEthernet0/0
P1R3#
Notes: <number>

## Slide 12: Routing Table in a Stub Area with Summarization
P1R3#sh ip route
<output omitted>
Gateway of last resort is 10.1.1.1 to network 0.0.0.0
172.31.0.0/16 is variably subnetted, 2 subnets, 2 masks
O IA 172.31.22.4/32 [110/782] via 10.1.1.1, 00:13:08, FastEthernet0/0
O IA 172.31.11.0/24 [110/1] via 10.1.1.1, 00:02:39, FastEthernet0/0
10.0.0.0/8 is variably subnetted, 6 subnets, 2 masks
O 10.11.0.0/24 [110/782] via 10.1.1.1, 00:13:08, FastEthernet0/0
C 10.200.200.13/32 is directly connected, Loopback0
C 10.1.3.0/24 is directly connected, Serial0/0/0
O 10.1.2.0/24 [110/782] via 10.1.3.4, 00:13:09, Serial0/0/0
C 10.1.1.0/24 is directly connected, FastEthernet0/0
O 10.1.0.0/24 [110/782] via 10.1.1.1, 00:13:09, FastEthernet0/0
O*IA 0.0.0.0/0 [110/2] via 10.1.1.1, 00:13:09, FastEthernet0/0
P1R3#
Notes: <number>

## Slide 13: Routing Table in a Totally Stubby Area
P1R3#sh ip route
<output omitted>
Gateway of last resort is 10.1.1.1 to network 0.0.0.0
10.0.0.0/8 is variably subnetted, 6 subnets, 2 masks
O 10.11.0.0/24 [110/782] via 10.1.1.1, 00:16:53, FastEthernet0/0
C 10.200.200.13/32 is directly connected, Loopback0
C 10.1.3.0/24 is directly connected, Serial0/0/0
O 10.1.2.0/24 [110/782] via 10.1.3.4, 00:16:53, Serial0/0/0
C 10.1.1.0/24 is directly connected, FastEthernet0/0
O 10.1.0.0/24 [110/782] via 10.1.1.1, 00:16:53, FastEthernet0/0
O*IA 0.0.0.0/0 [110/2] via 10.1.1.1, 00:00:48, FastEthernet0/0
P1R3#
Notes: <number>

## Slide 14: Not-So-Stubby Areas
  NSSA breaks stub area rules.
  ASBR (R1) is allowed in NSSA.
  Special LSA type 7 defined, sent by ASBR.
  ABR (R2) converts LSA type 7 to LSA type 5.
  ABR sends default route into NSSA instead of external routes from other ASBRs.
  NSSA is an RFC addendum.
Notes: <number>

## Slide 15: NSSA Configuration
area area-id nssa [no-redistribution] [default-information-originate [metric metric-value] [metric-type type-value]] [no-summary]
Use this command instead of the area stub command to define the area as NSSA.
The no-summary keyword creates an NSSA totally stubby area; this is a Cisco proprietary feature.
RouterA(config-router)#

## Slide 16: Example: NSSA Configuration
Notes: <number>

## Slide 17: NSSA Totally Stubby Configuration
NSSA totally stubby area is a Cisco proprietary feature.
Notes: <number>

## Slide 18: show Commands for Stub and NSSA
show ip ospf
Displays which areas are normal, stub, or NSSA
show ip ospf database
Displays details of LSAs
show ip ospf database nssa-external
Displays specific details of each LSA type 7 update in database
show ip route
Displays all routes
RouterA#
RouterA#
RouterA#
RouterA#

## Slide 19: Summary
  There are several OSPF area types: standard, backbone, stub, totally stubby, and NSSA.
  Use the area area-id stub command to define an area as stubby.
  Use the area area-id stub command with the no-summary keyword on the ABR only to define an area as totally stubby.
  For stub areas, external routes are not visible in the routing table, but are accessible via the intra-area default route. For totally stubby areas, interarea and external routes are not visible in the routing table, but are accessible via the intra-area default route.
  Use the area area-id nssa command to define an area as NSSA.
  Use show ip ospf, show ip ospf database, show ip route commands to verify all types of stub areas. Use the show ip ospf database nssa-external command to display details of type 7 LSAs.
Notes: <number>