## Slide 1: Configuring OSPF
Configuring OSPF Authentication

## Slide 2: OSPF Authentication Types
  OSPF supports 2 types of authentication:
    Simple password (or plain text) authentication
    MD5 authentication
  Router generates and checks every OSPF packet. Router authenticates the source of each routing update packet that it receives.
  Configure a “key” (password); each participating neighbor must have same key configured.

## Slide 3: Configuring OSPF Simple Password Authentication
ip ospf authentication-key password
Router(config-if)#
Assigns a password to be used with neighboring routers
Router(config-if)#
ip ospf authentication [message-digest | null]
Specifies the authentication type for an interface (since Cisco IOS software 12.0)
Router(config-router)#
area area-id authentication [message-digest]
Specifies the authentication type for an area (was in Cisco IOS software before 12.0)

## Slide 4: Example Simple Password Authentication Configuration
Loopback 0
10.2.2.2
Notes: <number>

## Slide 5: R2 Configuration for Simple Password Authentication
<output omitted>
interface Loopback0
ip address 10.2.2.2 255.255.255.0
<output omitted>
interface Serial0/0/1
ip address 192.168.1.102 255.255.255.224
ip ospf authentication
ip ospf authentication-key plainpas
<output omitted>
router ospf 10
log-adjacency-changes
network 10.2.2.2 0.0.0.0 area 0
network 192.168.1.0 0.0.0.255 area 0
Notes: <number>

## Slide 6: Verifying Simple Password Authentication
R1#sh ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
10.2.2.2 0 FULL/ - 00:00:32 192.168.1.102 Serial0/0/1
R1#show ip route
<output omitted>
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 2 subnets, 2 masks
O 10.2.2.2/32 [110/782] via 192.168.1.102, 00:01:17, Serial0/0/1
C 10.1.1.0/24 is directly connected, Loopback0
192.168.1.0/27 is subnetted, 1 subnets
C 192.168.1.96 is directly connected, Serial0/0/1
R1#ping 10.2.2.2
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.2.2.2, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 28/29/32 ms

## Slide 7: Configuring OSPF MD5 Authentication
ip ospf message-digest-key key-id md5 key
Router(config-if)#
Assigns a key ID and key to be used with neighboring routers
Router(config-if)#
ip ospf authentication [message-digest | null]
Specifies the authentication type for an interface (since Cisco IOS software 12.0)
Router(config-router)#
area area-id authentication [message-digest]
Specifies the authentication type for an area (was in Cisco IOS software before 12.0)

## Slide 8: Example MD5 Authentication Configuration
Notes: <number>

## Slide 9: R2 Configuration for MD5 Authentication
<output omitted>
interface Loopback0
ip address 10.2.2.2 255.255.255.0
<output omitted>
interface Serial0/0/1
ip address 192.168.1.102 255.255.255.224
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 secretpass
<output omitted>
router ospf 10
log-adjacency-changes
network 10.2.2.2 0.0.0.0 area 0
network 192.168.1.0 0.0.0.255 area 0
Notes: <number>

## Slide 10: Verifying MD5 Authentication
R1#sho ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
10.2.2.2 0 FULL/ - 00:00:31 192.168.1.102 Serial0/0/1
R1#show ip route
<output omitted>
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 2 subnets, 2 masks
O 10.2.2.2/32 [110/782] via 192.168.1.102, 00:00:37, Serial0/0/1
C 10.1.1.0/24 is directly connected, Loopback0
192.168.1.0/27 is subnetted, 1 subnets
C 192.168.1.96 is directly connected, Serial0/0/1
R1#ping 10.2.2.2
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.2.2.2, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 28/28/32 ms

## Slide 11: Troubleshooting Simple Password Authentication
R1#debug ip ospf adj
OSPF adjacency events debugging is on
R1#
<output omitted>
*Feb 17 18:42:01.250: OSPF: 2 Way Communication to 10.2.2.2 on Serial0/0/1, state 2WAY
*Feb 17 18:42:01.250: OSPF: Send DBD to 10.2.2.2 on Serial0/0/1 seq 0x9B6 opt 0x52 flag 0x7 len 32
*Feb 17 18:42:01.262: OSPF: Rcv DBD from 10.2.2.2 on Serial0/0/1 seq 0x23ED opt0x52 flag 0x7 len 32 mtu 1500 state EXSTART
*Feb 17 18:42:01.262: OSPF: NBR Negotiation Done. We are the SLAVE
*Feb 17 18:42:01.262: OSPF: Send DBD to 10.2.2.2 on Serial0/0/1 seq 0x23ED opt 0x52 flag 0x2 len 72
<output omitted>
R1#show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
10.2.2.2 0 FULL/ - 00:00:34 192.168.1.102 Serial0/0/1
debug ip ospf adj
Router#
Displays the OSPF adjacency-related events

## Slide 12: Troubleshooting Simple Password Authentication Problems
R1#
*Feb 17 18:51:31.242: OSPF: Rcv pkt from 192.168.1.102, Serial0/0/1 : Mismatch Authentication type. Input packet specified type 0, we use type 1
R2#
*Feb 17 18:50:43.046: OSPF: Rcv pkt from 192.168.1.101, Serial0/0/1 : Mismatch Authentication type. Input packet specified type 1, we use type 0
Simple authentication on R1, no authentication on R2
R1#
*Feb 17 18:54:01.238: OSPF: Rcv pkt from 192.168.1.102, Serial0/0/1 : Mismatch Authentication Key - Clear Text
R2#
*Feb 17 18:53:13.050: OSPF: Rcv pkt from 192.168.1.101, Serial0/0/1 : Mismatch Authentication Key - Clear Text
Simple authentication on R1 and R2, but different
passwords

## Slide 13: Troubleshooting MD5 Authentication
R1#debug ip ospf adj
OSPF adjacency events debugging is on
<output omitted>
*Feb 17 17:14:06.530: OSPF: Send with youngest Key 1
*Feb 17 17:14:06.546: OSPF: 2 Way Communication to 10.2.2.2 on Serial0/0/1, state 2WAY
*Feb 17 17:14:06.546: OSPF: Send DBD to 10.2.2.2 on Serial0/0/1 seq 0xB37 opt 0x52 flag 0x7 len 32
*Feb 17 17:14:06.546: OSPF: Send with youngest Key 1
*Feb 17 17:14:06.562: OSPF: Rcv DBD from 10.2.2.2 on Serial0/0/1 seq 0x32F opt 0x52 flag 0x7 len 32 mtu 1500 state EXSTART
*Feb 17 17:14:06.562: OSPF: NBR Negotiation Done. We are the SLAVE
*Feb 17 17:14:06.562: OSPF: Send DBD to 10.2.2.2 on Serial0/0/1 seq 0x32F opt 0x52 flag 0x2 len 72
*Feb 17 17:14:06.562: OSPF: Send with youngest Key 1
<output omitted>
R1#show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
10.2.2.2 0 FULL/ - 00:00:35 192.168.1.102 Serial0/0/1

## Slide 14: Troubleshooting MD5 Authentication Problems
R1#
*Feb 17 17:56:16.530: OSPF: Send with youngest Key 1
*Feb 17 17:56:26.502: OSPF: Rcv pkt from 192.168.1.102, Serial0/0/1 : Mismatch Authentication Key - No message digest key 2 on interface
*Feb 17 17:56:26.530: OSPF: Send with youngest Key 1
R2#
*Feb 17 17:55:28.226: OSPF: Send with youngest Key 2
*Feb 17 17:55:28.286: OSPF: Rcv pkt from 192.168.1.101, Serial0/0/1 : Mismatch Authentication Key - No message digest key 1 on interface
*Feb 17 17:55:38.226: OSPF: Send with youngest Key 2
MD5 authentication on both R1 and R2, but R1 has key 1 and R2 has key 2, both with the same passwords:

## Slide 15: Summary
  When authentication is configured, the router generates and checks every OSPF packet and authenticates the source of each routing update packet that it receives. OSPF supports two types of authentication:
    Simple password (or plain text) authentication: The router sends an OSPF packet and key.
    MD5 authentication: The router generates a message digest, or hash, of the key, key ID, and message. The message digest is sent with the packet; the key is not sent.
  To configure simple password authentication, use the ip ospf authentication-key password command and the ip ospf authentication command.
Notes: <number>

## Slide 16: Summary (Cont.)
  To configure MD5 authentication, use the ip ospf message-digest-key key-id md5 key command and the ip ospf authentication message-digest command.
  Use show ip ospf neighbor, show ip route, and debug ip ospf adj to verify and troubleshoot both types of authentication.
  With MD5 authentication, the debug ip ospf adj command output indicates the key ID sent.
Notes: <number>