## Slide 1: Module Summary
  OSPF is an open-standard link-state routing protocol, offering quick convergence and the ability to scale large networks.
  There are five OSPF packet types: hello, DBD, LSU, LSR, and LSAck.
  Configuration of OSPF is a two-step process:
    Enter OSPF configuration with the router ospf command.
    Use the network command to describe which interfaces will run OSPF in which area.
  OSPF defines three types of networks: point-to-point, broadcast, and NBMA. On NBMA networks, OSPF mode options include nonbroadcast, broadcast, point-to-multipoint, point-to-multipoint nonbroadcast, and point-to-point.
Notes: <number>
<footer>
<header>
<date/time>
Lesson Aim
  <Enter lesson aim here.>

## Slide 2: Module Summary (Cont.)
  LSAs are the building blocks of the LSDB. There are 11 types of OSPF LSAs.
  Route summarization reduces OSPF LSA flooding and routing table size, which reduces memory and CPU utilization on routers.
  Stub area techniques improve OSPF performance by reducing the LSA flooding.
  OSPF supports two types of authentication:
    Simple password (or plain text) authentication
    MD5 authentication
Notes: <number>
<footer>
<header>
<date/time>
Lesson Aim
  <Enter lesson aim here.>