## Slide 1: The IS-IS Protocol
Introducing IS-IS and Integrated IS-IS Routing

## Slide 2: Uses for IS-IS Routing
Large ISPs
  Stable protocol
  Originally deployed by ISPs because U.S. government mandated Internet support of OSI and IP

## Slide 3: IS-IS Routing
  IS = router.
  IS-IS was originally designed as the IGP for the Connectionless Network Service (CLNS), part of the OSI protocol suite.
  The OSI protocol suite layer 3 protocol is the Connectionless Network Protocol (CLNP).
  IS-IS uses CLNS addresses to identify routers and build the LSDB.

## Slide 4: IS-IS Features
  Link-state routing protocol
  Supports VLSM
  Uses Dijkstra’s SPF algorithm; has fast convergence
  Uses hellos to establish adjacencies and LSPs to exchange link-state information
  Efficient use of bandwidth, memory, and processor
  Supports two routing levels:
    Level 1: Builds common topology of system IDs in local area and routes within area using lowest cost path.
    Level 2: Exchanges prefix information (area addresses) between areas. Routes traffic to area using lowest-cost path.

## Slide 5: IS-IS Link-State Operation
Routers are identified as Level 1, Level 2, or Level 1-2:
  Level 1 routers use LSPs to build topology for local area.
  Level 2 routers use LSPs to build topology between different areas.
  Level 1-2 routers act as border routers between Level 1 and Level 2 routing domains.
Notes: <number>

## Slide 6: Integrated (or Dual) IS-IS Routing
  Integrated IS-IS is IS-IS for multiple protocols:
    For IP, CLNS, or both
  Uses its own PDUs to transport IP routing information; updates not sent in IP packets
  Requires CLNS addresses, even if only routing for IP

## Slide 7: Integrated IS-IS Design Principles
  IP and CLNP addresses must be planned.
  Use two-level hierarchy for scalability:
    Limits LSP flooding
    Provides opportunity for summarization
  Summarization:
    Limits update traffic
    Minimizes router memory and CPU usage
Notes: <number>

## Slide 8: Issues with Integrated IS-IS
  Default narrow metrics are limited to 6-bit interface and 10-bit path metric
    In Cisco IOS Software Relase 12.0, wide metrics allow 24-bit interface and 32-bit path metric.
  Cisco IOS software has default metric of 10 on all interfaces.

## Slide 9: End System-to-Intermediate System
  ES-IS forms adjacencies between ESs and routers (ISs).
    IP end-systems do not use ES-IS.
  ESs transmit ESHs to announce their presence to ISs.
  ISs transmit ISHs to announce their presence to ESs.
  ISs transmit IIHs to other ISs.
Notes: <number>

## Slide 10: Four OSI Routing Levels
Notes: <number>

## Slide 11: Similarities Between IS-IS and OSPF
  Integrated IS-IS and OSPF are both open standard link-state protocols with the following similar features:
    Link-state representation, aging timers, and LSDB synchronization
    SPF algorithms
    Update, decision, and flooding processes
    VLSM support
  Scalability of link-state protocols has been proven (used in ISP backbones).
  They both converge quickly after changes.

## Slide 12: Integrated IS-IS vs. OSPF: Area Design
OSPF is based on a central backbone with all other areas attached to it.
  In OSPF the border is inside routers (ABRs).
  Each link belongs to one area.

## Slide 13: Integrated IS-IS vs. OSPF: Area Design (Cont.)
In IS-IS the area borders lie on links
  Each IS-IS router belongs to exactly one area.
  IS-IS is more flexible when extending the backbone.

## Slide 14: Advantages of Integrated IS-IS
  Supports CLNP and IP
  More extensible through TLV design

## Slide 15: Advantages of OSPF
  OSPF has more features, including:
    Has three area types: normal, stub, and NSSA
    Defaults to scaled metric (IS-IS always 10)
  OSPF is supported by many vendors.
  Information, examples, and experienced engineers are easier to find.

## Slide 16: Summary
  IS-IS is a popular routing protocol in the ISP industry.
  IS-IS is a stable, fast-converging IGP that is positioned to route IPv4, CLNS, or IPv6.
  All IS-IS interfaces have a default metric of 10.
  ES-IS (for CLNS routing only) provides discovery between host and routers using hello packets to form adjacencies. Hosts send ESHs, while routers send ISHs.
  OSI defines routing levels 0 through 3. Level 0 is between ES and IS. Levels 1 and 2 are between IS and IS to support intradomain routing. Level 3 supports interdomain routing.
    Level 1 is intra-area
    Level 2 is interarea.
  IS-IS and OSPF are both open-standard link-state routing protocols that support VLSM, scalability, and quick convergence.
Notes: <number>