## Slide 1: The IS-IS Protocol
Performing IS-IS Routing Operations

## Slide 2: OSI Addresses
  OSI network layer addressing is implemented with NSAP addresses.
  An NSAP address identifies a system in the OSI network; an address represents an entire node, not an interface.
  Various NSAP formats are used in various systems, because different protocols may use different representations of NSAP.
  NSAP addresses are a maximum of 20 bytes:
    Higher-order bits identify the interarea structure.
    Lower-order bits identify systems within area.

## Slide 3
Integrated IS-IS NSAP Address Structure
  The Cisco implementation of Integrated IS-IS distinguishes only the following three fields in the NSAP address:
    Area address: Variable-length field (1 to 13 octets) composed of the higher-order NSAP octets, excluding system ID and NSEL.
    System ID: ES or IS identifier in an area; fixed length of six octets in Cisco IOS software.
    NSEL: One octet NSAP selector, service identifier.
  Total length of NSAP is from 8 (minimum) to 20 octets (maximum).
Notes: <number>

## Slide 4: Typical NSAP Address Structure
The simplest NSAP format used by most companies running IS-IS as their IGP is as follows:
  Area address (must be at least 1 byte)
    AFI set to 49
      Locally administered; thus, you can assign your own addresses.
    Area ID
      The octets of the area address after the AFI.
  System ID
    Cisco routers require a 6-byte system ID.
  NSEL
    Always set to 0 for a router.

## Slide 5: Identifying Systems in IS-IS: Area Address
The area address uniquely identifies the routing area, and the system ID identifies each node.
  All routers within an area must use the same area address.
  An ES may be adjacent to a router only if they share a common area address.
  Area address is used in Level 2 routing.
Notes: <number>

## Slide 6: Identifying Systems in IS-IS: System ID
  System ID in the address used to identify the IS; it is not just an interface. Cisco supports only a 6-byte system ID.
  System ID is used in Level 1 routing and has to be unique within an area.
  System ID has to be unique within Level 2 routers that form the routing domain.
  General recommendation: use domain-wide unique system ID.
    This may be MAC (for example, 0000.0c12.3456) or IP address (for example, 1921.6800.0001) taken from an interface.

## Slide 7: OSI Addressing: NET Addresses
  NSAP address includes NSEL field (process or port number)
  NET: NSAP with a NSEL field of 0
    Refers to the device itself (equivalent to the Layer 3 OSI address of the device)
    Used in routers because they implement the network layer only (base for SPF calculation)

## Slide 8: Subnetwork Point of Attachment (SNPA) and Circuit
SNPA is equivalent to Layer 2 address; for example:
  Virtual circuit ID (DLCI on Frame Relay)
  MAC address on LAN interfaces
Interfaces uniquely identified by circuit ID:
  On point-to-point interfaces, SNPA is used.
  On LANs, circuit ID concatenated with six-octet system ID of a designated IS to form seven-octet LAN ID (for example, 1921.6800.0001.01) is used.
  Cisco routers use host name instead of system ID (for example, “R1.01”).

## Slide 9: Level 1, Level 2, and Level 1-2 Routers
Level 1 (like OSPF internal nonbackbone routers):
  Intra-area routing enables ESs to communicate.
  Level 1 area is a collection of Level 1 and Level 1-2 routers.
  Level 1 IS keeps copy of the Level 1 area LSDB.
Level 1-2 (like OSPF ABR):
  Intra-area and interarea routing.
  Level 1-2 IS keeps separate Level 1 and Level 2 LSDBs and advertises default route to Level 1 routers.
Level 2 (like OSPF backbone routers):
  Interarea routing.
  Level 2 (backbone) area is a contiguous set of Level 1-2 and Level 2 routers.
  Level 2 IS keeps a copy of the Level 2 area LSDB.

## Slide 10: Addressing and Routing
  Area address is used to route between areas; system ID is not considered.
  System ID is used to route within an area; area address is not considered.

## Slide 11: OSI IS-IS Routing Logic
Level 1 router: For a destination address, compare the area address to this area.
  If not equal, pass to nearest Level 1-2 router.
  If equal, use Level 1 database to route by system ID.
Level 1-2 router: For a destination address, compare the area address to this area.
  If not equal, use Level 2 database to route by area address.
  If equal, use Level 1 database to route by system ID.

## Slide 12: Example: Identifying Systems: OSI Addressing in Networks
Notes: <number>

## Slide 13: Example: OSI Area Routing
Notes: <number>

## Slide 14: Route Leaking
  Available since Cisco IOS Sofware Release 12.0
  Helps reduce suboptimal routing by allowing Level 2 information to be leaked into Level 1
  Uses up/down bit in Type, Length, and Value (TLV) field

## Slide 15: OSI PDUs
PDUs between peers:
  Network PDU = datagram, packet
  Data-link PDU = frame
  Examples:
Notes: <number>

## Slide 16: IS-IS PDUs
  IS-IS PDUs are encapsulated directly into a data-link frame. There is no CLNP or IP header in a PDU.
  IS-IS PDUs are as follows:
    Hello (ESH, ISH, IIH)
    LSP
    PSNP (partial sequence number PDU)
    CSNP (complete sequence number PDU)

## Slide 17: A Link-State Packet Represents Router
LSP Header
IS Neighbors
ES Neighbors
…………..
  Router describes itself with an LSP
  LSP header contents include:
    PDU type, length, LSP ID, sequence number, remaining lifetime
  TLV variable-length fields:
    IS neighbors
    ES neighbors
    Authentication information
    ....
TLV
TLV
TLV
Notes: <number>

## Slide 18: LSP Header
LSPs are sequenced to prevent duplication of LSPs.
  Assists with synchronization.
  Sequence numbers begin at 1.
  Sequence numbers are increased to indicate the newest LSP.
LSPs in LSDB have a remaining lifetime.
  Allows synchronization.
  Decreasing timer.
Notes: <number>

## Slide 19: LSP TLV Examples
TLV | Type Code | Length Field | Value Variable Length
Area address | 1 | Area ID length + 1 | Areas
Intermediate system neighbors | 2 | Neighbor count + 1 | IS neighbors
IP internal reachability | 128 | Number of connected prefixes | Connected IP prefixes — 4-byte metric, 4-byte prefix, 4-byte mask
IP external reachability | 130 | Number of redistributed prefixes | Redistributed IP prefixes — 4-byte metric, 4-byte prefix, 4-byte mask
Each set of information, called a “tuple,” includes a type code, length field, and value.
Notes: <number>

## Slide 20: IS-IS Network Representation
  Generally, physical links can be placed in the following two groups:
    Broadcast: Multiaccess subnetworks that support addressing of a group of attached systems
    Point-to-point: Permanent or dynamically established links
  Only two link-state representations are available in IS-IS:
    Broadcast for LANs and multipoint WANs
    Point-to-point for all other topologies
  IS-IS has no concept of NBMA networks.
Notes: <number>

## Slide 21: Implementing Network Types in NBMA
When implementing IS-IS in NBMA (such as Frame Relay or ATM):
  Broadcast mode assumes fully meshed connectivity.
  In broadcast mode, you must enable CLNS mapping and include the broadcast keyword, in addition to creating IP maps with the broadcast keyword.
  Point-to-point mode is highly recommended (using subinterfaces).

## Slide 22: Broadcast Mode
  Used for LAN and multipoint WAN interfaces.
  Adjacency is recognized through hellos; separate adjacencies for Level 1 and Level 2.
  Designated IS (DIS) creates a pseudonode and represents LAN.
  DIS for Level 1 and Level 2 may be different.
  DIS is elected based on these criteria:
    Only routers with adjacencies are eligible.
    Highest interface priority.
    Highest SNPA (MAC) breaks ties.
  There is no backup DIS.

## Slide 23: LSP Representing Routers: LAN Representation
Notes: <number>

## Slide 24: Level 1 and Level 2 LSPs and IIHs
  The two-level nature of IS-IS requires separate types of LSPs: Level 1 and Level 2 LSPs.
  DIS is representative of LAN:
    DIS sends pseudo-Level 1 and pseudo-Level 2 LSPs for LAN.
    Separate DIS for Level 1 and Level 2.
  LSPs are sent as unicast on point-to-point networks.
  LSPs are sent as multicast on broadcast networks.
  LAN uses separate Level 1 and Level 2 IIHs; sent as multicast.
  Point-to-point uses a common IIH format; sent as unicast.

## Slide 25: Comparing Broadcast and Point-to-Point Topologies
 | Broadcast | Point-to-Point
Usage | LAN, full-mesh WAN | PPP, HDLC, partial-mesh WAN
Hello timer | 3.3 sec for DIS else 10 sec | 10 sec
Adjacencies | n (n-1) / 2 | n-1
Uses DIS | Yes | No
IIH type | Level 1 IIH, Level 2 IIH | Point-to-point IIH
Notes: <number>

## Slide 26: LSP Flooding
  Single procedure for flooding, aging, and updating of LSPs.
  Level 1 LSPs are flooded within an area.
  Level 2 LSPs are flooded throughout the Level 2 backbone.
  Large PDUs are divided into fragments that are independently flooded.
    Each PDU is assigned an LSP fragment number, starting at 0 and incrementing by 1.
  Separate LSDBs are maintained for Level 1 and Level 2 LSPs.

## Slide 27: LSDB Synchronization
  SNP packets are used to ensure synchronization and reliability.
    Contents are LSP descriptions
  PSNP is used for the following:
    For acknowledgment of LSPs on point-to-point links
    To request missing pieces of LSDB
  CSNP is used for the following:
    Periodically by DIS on LAN to ensure LSDB accuracy
    On point-to-point link when the link comes up

## Slide 28: LSDB Synchronization: LAN
Notes: <number>

## Slide 29: LSDB Synchronization: Point-to-Point
Notes: <number>

## Slide 30: LAN Adjacencies
Adjacencies are established based on the area address announced in the incoming IIHs and the type of the router.
Notes: <number>

## Slide 31: Example: WAN Adjacencies
Notes: <number>

## Slide 32: Summary
  An NSAP is the OSI network-layer address. Cisco uses the area address (comprising the AFI and area ID), system ID, and NSEL fields. The system ID must be 6 bytes.
  A NET address is an NSAP with an NSEL value of 0 and is used to identify the device itself.
  IS-IS defines three types of routers: Level 1, Level 2, and Level 1-2.
  The area address is used to route between areas; the system ID is used to route within an area.
  The four types of IS-IS PDUs are hello, LSP, PSNP, and CSNP.
Notes: <number>

## Slide 33: Summary (Cont.)
  LSPs are used by routers to describe their characteristics. LSPs contain a header and TLV fields. The header ensures unique sequenced packets; the TLV fields include information about the network and stations attached to the router.
  IS-IS recognizes two topology types: point-to-point and broadcast.
  Broadcast networks are LAN interfaces or multipoint WAN interfaces.
  The two-level nature of IS-IS requires separate types of LSPs: Level 1 and Level 2.
  Level 1 LSPs are flooded within an area; Level 2 LSPs are flooded throughout the Level 2 backbone.
Notes: <number>