## Slide 1: The IS-IS Protocol
Configuring Basic Integrated IS-IS

## Slide 2: Integrated IS-IS: Requires NET Addresses
  Common CLNS parameters (NET) and area planning are still required even in an IP environment.
  Even when Integrated IS-IS is used for IP routing only, routers still establish CLNS adjacencies and use CLNS packets.

## Slide 3: OSI Area Routing: Building an OSI Forwarding Database (Routing Table)
  When databases are synchronized, Dijkstra’s algorithm (SPF) is run on the LSDB to calculate the SPF tree.
  The shortest path to the destination is the lowest total sum of metrics.
  Separate route calculations are made for Level 1 and Level 2 routes in Level 1-2 routers.
  Best paths are placed in the OSI forwarding database (CLNS routing table).

## Slide 4: Building an IP Routing Table
Partial route calculation (PRC) is run to calculate IP reachability.
  Because IP and ES are represented as leaf objects, they do not participate in SPF.
Best paths are placed in the IP routing table following IP preferential rules.
  They appear as Level 1 or Level 2 IP routes.

## Slide 5: Integrated IS-IS Configuration Steps
Define areas, prepare addressing plan (NETs) for routers, and determine interfaces.
Enable IS-IS on the router.
Configure the NET.
Enable Integrated IS-IS on the appropriate interfaces. Do not forget interfaces to stub IP networks, such as loopback interfaces (although there are no CLNS neighbors there).

## Slide 6: Step 1: Define Area and Addressing
  Area determined by NET prefix
    Assign to support two-level hierarchy.
  Addressing
    IP: Plan to support summarization.
    CLNS: Prefix denotes area. System ID must be unique.

## Slide 7: Step 2: Enable IS-IS on the Router
router isis [area-tag]
router(config)#
  Enables the IS-IS routing protocol
    area-tag—name for a process
  When routing of CLNS packets is also needed, use the clns routing command.

## Slide 8: Step 3: Configure the NET
net network-entity-title
Router(config-router)#
Configures an IS-IS NET address for the routing process

## Slide 9: Step 4: Enable Integrated IS-IS
ip router isis [area-tag]
router(config-if)#
Includes an interface in an IS-IS routing process

## Slide 10: Simple Integrated IS-IS Example
interface FastEthernet0/0
ip address 10.1.1.2 255.255.255.0
ip router isis
!
interface Serial 0/0/1
ip address 10.2.2.2 255.255.255.0
ip router isis
!
<output omitted>
router isis
net 49.0001.0000.0000.0002.00
The configured router acts as an IP-only Level 1-2 router.

## Slide 11: Change IS-IS Router Level
is-type {level-1 | level-1-2 | level-2-only}
Router(config-router)#
Configures the IS-IS level globally on a router; the default is Level 1-2.

## Slide 12: Change IS-IS Interface Level
isis circuit-type {level-1 | level-1-2 | level-2-only}
Router(config-if)#
Configures the type of adjacency on an interface; the default is Level 1-2.

## Slide 13: Change IS-IS Metric
isis metric metric [delay-metric [expense-metric [error-metric]]] {level-1 | level-2}
Router(config-if)#
Configures the metric for an interface; the default is 10.
Metric value is from 1 to 63.
Router(config-router)#
metric default-value {level-1 | level-2}
Alternately, configures the metric globally for all interfaces

## Slide 14: Example: Tuning IS-IS Configuration
  Change router type on R1 and R3.
  Change interface levels on R2.
  Change metric on S0/0/1.

## Slide 15: IP Summarization
summary-address address mask [level-1 | level-2 | level-1-2]
[tag tag-number] [metric metric-value]
Router(config-router)#
P3R1(config-router)# summary-address 10.3.2.0 255.255.254.0 level-1-2
Creates summary
Default is Level 2
Example
Summarizes 10.3.2.0/23 into Level 1-2

## Slide 16: Example: Is Integrated IS-IS Running?
R2#show ip protocols
Routing Protocol is "isis"
Invalid after 0 seconds, hold down 0, flushed after 0
Outgoing update filter list for all interfaces is not set
Incoming update filter list for all interfaces is not set
Redistributing: isis
Address Summarization:
None
Maximum path: 4
Routing for Networks:
FastEthernet0/0
Loopback0
Serial0/0/1
Routing Information Sources:
Gateway Distance Last Update
10.10.10.10 115 00:00:02
10.30.30.30 115 00:00:03
Distance: (default is 115)
R2#
Displays the parameters and current state of the active routing protocol processes
Router#
show ip protocols

## Slide 17: Example: Are There Any IP Routes?
R2#show ip route isis
10.0.0.0/24 is subnetted, 5 subnets
i L2 10.30.30.0 [115/45] via 10.2.2.3, Serial0/0/1
i L1 10.10.10.0 [115/20] via 10.1.1.1, FastEthernet0/0
R2#
Displays the current state of the routing table
show ip route [address [mask]] | [protocol [process-id]]
router#

## Slide 18: Troubleshooting Commands: CLNS
show clns
Router#
Displays information about the CLNS network
show clns [area-tag] protocol
Router#
Lists the protocol-specific information
show clns interface [type number]
Router#
Lists the CLNS-specific information about each interface
show clns [area-tag] neighbors [type number] [detail]
Router#
Displays both ES and IS neighbors

## Slide 19: Troubleshooting Commands: CLNS and IS-IS
show isis [area-tag] route
Router#
Displays IS-IS Level 1 routing table (system IDs) (requires that CLNS routing be enabled)
show clns route [nsap]
Router#
Displays IS-IS routing table (areas)
show isis [area-tag] database
Router#
Displays the IS-IS LSDB
show isis [area-tag] topology
Displays IS-IS least-cost paths to destinations
Router#

## Slide 20: Example: OSI Intra-Area and Interarea Routing
Routing in a Two-Level Area Structure
Notes: <number>

## Slide 21: Level 1 and Level 2 Topology Table
R1#show isis topology
IS-IS paths to level-1 routers
System Id Metric Next-Hop Interface SNPA
R1 --
R2 10 R2 Fa0/0 0016.4650.c470
R2#show isis topology
IS-IS paths to level-1 routers
System Id Metric Next-Hop Interface SNPA
R1 10 R1 Fa0/0 0016.4610.fdb0
R2 --
IS-IS paths to level-2 routers
System Id Metric Next-Hop Interface SNPA
R1 **
R2 --
R3 35 R3 Se0/0/1 *HDLC*

## Slide 22: Simple Troubleshooting: What About CLNS Protocol?
R2# show clns protocol
IS-IS Router: <Null Tag>
System Id: 0000.0000.0002.00 IS-Type: level-1-2
Manual area address(es):
49.0001
Routing for area address(es):
49.0001
Interfaces supported by IS-IS:
Loopback0 - IP
Serial0/0/1 - IP
FastEthernet0/0 - IP
Redistribute:
static (on by default)
Distance for L2 CLNS routes: 110
RRR level: none
Generate narrow metrics: level-1-2
Accept narrow metrics: level-1-2
Generate wide metrics: none
Accept wide metrics: none

## Slide 23: Are Adjacencies Established?
R2# show clns neighbors
System Id Interface SNPA State Holdtime Type Protocol
R3 Se0/0/1 *HDLC* Up 28 L2 IS-IS
R1 Fa0/0 0016.4610.fdb0 Up 23 L1 IS-IS
R2#show clns interface s0/0/1
Serial0/0/1 is up, line protocol is up
Checksums enabled, MTU 1500, Encapsulation HDLC
ERPDUs enabled, min. interval 10 msec.
CLNS fast switching enabled
CLNS SSE switching disabled
DEC compatibility mode OFF for this interface
Next ESH/ISH in 45 seconds
Routing Protocol: IS-IS
Circuit Type: level-2
Interface number 0x1, local circuit ID 0x100
Neighbor System-ID: R3
Level-2 Metric: 35, Priority: 64, Circuit ID: R2.00
Level-2 IPv6 Metric: 10
Number of active level-2 adjacencies: 1
Next IS-IS Hello in 5 seconds
if state UP

## Slide 24: Summary
  Integrated IS-IS routing for IP uses CLNS and therefore requires CLNS addresses, that is, NET addresses.
  Integrated IS-IS requires planning the addresses, enabling the router, defining the router NET, and enabling the appropriate interfaces.
  IS-IS can be optimized by adjusting adjacency levels and changing the default metric cost.
  IS-IS summarization can be configured with the summary-address command.
  The show ip protocols and show ip route commands verify the IS-IS configuration and IP functionality.
  Various show commands are used to troubleshoot CLNS IS-IS structures and Integrated IS-IS networks
Notes: <number>