## Slide 1: Module Summary
  IS-IS is a proven and extensible IP routing protocol that converges quickly and supports VLSM.
  Unlike IP addresses, CLNS addresses apply to entire nodes and not to interfaces. IS-IS runs directly on the data-link layer and does not use IP or CLNS as a network protocol.
  Even when IS-IS is installed to support IP exclusively, network devices must also be configured with NET addresses. Default settings for IS-IS may result in the inefficient use of router and network resources and suboptimal routing.
Notes: <number>
<footer>
<header>
<date/time>
Lesson Aim
  <Enter lesson aim here.>