## Slide 1: Manipulating Routing Updates
Implementing Advanced Cisco IOS Features: Configuring DHCP

## Slide 2: DHCP in an Enterprise Network

## Slide 3: Dynamic Host Configuration Protocol
Notes: Lesson Aim
  <Enter lesson aim here.>

## Slide 4: Configuring a DHCP Server
Router(config)#ip dhcp pool [pool name]
Enables a DHCP pool for use by hosts
Router(config-dhcp)#import all
Imports DNS and WINS information from IPCP
Router(config-dhcp)#default-router [host address]
Specifies the default router for the pool to use
Router(config-dhcp)#network [network address][subnet mask]
Specifies the network and subnet mask of the pool
Notes: Purpose: This figure shows the commands used to allocate the number of channels (timeslots) to a PRI group, specify which serial port will be the D channel, and allow analog calls to terminate on internal modems.
Emphasize: The serial interface slot/port or unit number will be the slot/port or unit number of the T1/E1 controller. The isdn incoming-voice modem command allows analog calls over a PRI to terminate on internal modems. The router uses the bearer capability field in the ISDN Q.931 message to indicate whether the call is analog (voice) or digital, and then switches it appropriately.
Transition: The next figure shows an example ISDN PRI configuration.

## Slide 5: DHCP Server Configuration Example
ipdhcp database ftp://user:passwords@172.16.4.253/router-dhcp write-delay 120
ip dhcp excluded-address 172.16.1.100 172.16.1.103
ip dhcp excluded-address 172.16.2.100 172.16.2.103
ip dhcp pool 0
network 172.16.0.0/16
domain-name global.com
dns-server 172.16.1.102 172.16.2.102
netbios-name-server 172.16.2.103 172.16.2.103
default-router 172.16.1.100
Notes: Purpose: This figure shows an example ISDN PRI configuration.
Emphasize: Review the commands.
Transition: The next figure shows the lab configuration topology.

## Slide 6: Importing and Autoconfiguration

## Slide 7: DHCP Client
Router (config-if)#
ip address dhcp
Enables a Cisco IOS device to obtain an IP address dynamically
from a DHCP server
Notes: Purpose: This figure shows an example ISDN PRI configuration.
Emphasize: Review the commands.
Transition: The next figure shows the lab configuration topology.

## Slide 8: Helper Addressing Overview
  Routers do not forward broadcasts, by default.
  Helper address provides selective connectivity.

## Slide 9: Why Use a Helper Address?
  Sometimes clients do not know the server address.
  Helpers change broadcast to unicast to reach server.

## Slide 10: IP Helper Address Commands
  Specifies which protocols will be forwarded
Router(config)#
ip forward-protocol { udp [ port ] }
Enables forwarding and specifies destination address for main UDP broadcast packets
Changes destination address from broadcast to unicast or directed broadcast address
Router(config-if)#
ip helper-address address

## Slide 11: Multiple Servers: Remote Networks

## Slide 12: Relay Agent Option Support

## Slide 13: DHCP Verification Commands
show ip dhcp database
router#
Displays recent activity on the DHCP database
show ip dhcp server statistics
router#
Shows count information about statistics and messages sent and received
show ip route dhcp
router#
Displays routes added to the routing table by DHCP
debug ip dhcp server {events | packets | linkage}
router#
Enables debugging on the DHCP server

## Slide 14: Summary
  DHCP functions may be configured with Cisco IOS software.
  DHCP server can be configured.
  DHCP options can be configured.
  DHCP client can be configured.
  The IP helper address activates the DHCP relay agent in the Cisco IOS device.
  DHCP relay services are supported.