## Slide 1: Implementing BGP
Selecting a BGP Path

## Slide 2: BGP Path Attributes
  BGP metrics are called path attributes.
  Characteristics of path attributes include:
    Well-known versus optional
    Mandatory versus discretionary
    Transitive versus nontransitive
    Partial

## Slide 3: Well-Known Attributes
  Well-known attributes
    Must be recognized by all compliant BGP implementations
    Are propagated to other neighbors
  Well-known mandatory attributes
    Must be present in all update messages
  Well-known discretionary attributes
    May be present in update messages

## Slide 4: Optional Attributes
  Optional attributes
    They are recognized by some implementations (could be private); but expected not to be recognized by all BGP routers.
    Recognized optional attributes are propagated to other neighbors based on their meaning.
  Optional transitive attributes
    If not recognized, marked as partial and propagated to other neighbors
  Optional nontransitive attributes
    Discarded if not recognized

## Slide 5: BGP Attributes
BGP attributes include the following:
  AS path *
  Next-hop *
  Origin *
  Local preference
  MED
  Others
* Well-known mandatory attribute

## Slide 6: AS Path Attribute
  A list of autonomous systems that a route has traversed:
    For example, on router B, the path to 192.168.1.0 is the AS sequence (65500, 64520).
  The AS path attribute is well-known, mandatory.
Notes: <number>

## Slide 7: Next-Hop Attribute
The IP address of the next AS to reach a given network:
  Router A advertises network 172.16.0.0 to router B in EBGP, with a next hop of 10.10.10.3.
  Router B advertises 172.16.0.0 in IBGP to router C, keeping 10.10.10.3 as the next-hop address.
The next-hop attribute is well-known, mandatory.
Notes: <number>

## Slide 8: Origin Attribute
  IGP (i)
    network command
  EGP (e)
    Redistributed from EGP
  Incomplete (?)
    Redistributed from IGP or static
The origin attribute informs all autonomous systems in the internetwork how the prefixes were introduced into BGP.
The origin attribute is well-known, mandatory.

## Slide 9: Example: Origin Attribute
RouterA# show ip bgp
BGP table version is 14, local router ID is 172.31.11.1
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal, r RIB-failure, S Stale
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*> 10.1.0.0/24 0.0.0.0 0 32768 i
* i 10.1.0.2 0 100 0 i
*> 10.1.1.0/24 0.0.0.0 0 32768 i
*>i10.1.2.0/24 10.1.0.2 0 100 0 i
*> 10.97.97.0/24 172.31.1.3 0 64998 64997 i
* 172.31.11.4 0 64999 64997 i
* i 172.31.11.4 0 100 0 64999 64997 i
*> 10.254.0.0/24 172.31.1.3 0 0 64998 i
* 172.31.11.4 0 64999 64998 i
* i 172.31.1.3 0 100 0 64998 i
r> 172.31.1.0/24 172.31.1.3 0 0 64998 i
r 172.31.11.4 0 64999 64998 i
r i 172.31.1.3 0 100 0 64998 i
*> 172.31.2.0/24 172.31.1.3 0 0 64998 i
<output omitted>

## Slide 10: Local Preference Attribute
Paths with highest local preference value are preferred:
  Local preference is used to advertise to IBGP neighbors about how to leave their AS.
  The local preference is sent to IBGP neighbors only (that is, within the AS only).
  The local preference attribute is well-known and discretionary.
  Default value is 100.
Notes: <number>

## Slide 11: MED Attribute
  The paths with the lowest MED (also called the metric) value are the most desirable:
    MED is used to advertise to EBGP neighbors how to exit their AS to reach networks owned by this AS.
  The MED attribute is optional and nontransitive.
Notes: <number>

## Slide 12: Weight Attribute (Cisco Only)
Paths with the highest weight value are preferred
  Weight not sent to any BGP neighbors; local to this router only
Notes: <number>

## Slide 13: BGP Path Selection
  The BGP forwarding table usually has multiple paths from which to choose for each network.
  BGP is not designed to perform load balancing:
    Paths are chosen because of policy.
    Paths are not chosen based on bandwidth.
  The BGP selection process eliminates any multiple paths through attrition until a single best path is left.
  That best path is submitted to the routing table manager process and evaluated against the methods of other routing protocols for reaching that network (using administrative distance).
  The route from the source with the lowest administrative distance is installed in the routing table.

## Slide 14: Route Selection Decision Process
Consider only (synchronized) routes with no AS loops and a valid next hop, and then:
  Prefer highest weight (local to router).
  Prefer highest local preference (global within AS).
  Prefer route originated by the local router (next hop = 0.0.0.0).
  Prefer shortest AS path.
  Prefer lowest origin code (IGP < EGP < incomplete).
  Prefer lowest MED (exchanged between autonomous systems).
  Prefer EBGP path over IBGP path.
  Prefer the path through the closest IGP neighbor.
  Prefer oldest route for EBGP paths.
  Prefer the path with the lowest neighbor BGP router ID.
  Prefer the path with the lowest neighbor IP address.

## Slide 15: Summary
  BGP metrics are called path attributes and describe the paths to reach each network. These attributes are categorized as well-known mandatory, well-known discretionary, optional transitive, and optional nontransitive.
  The AS path attribute is a well-known mandatory attribute that lists the AS numbers that a route has traversed to reach a destination.
  The BGP next-hop attribute is a well-known mandatory attribute that indicates the next-hop IP address to use to reach a destination.
  The origin attribute is a well-known mandatory attribute that defines the origin of the path information.
  The local preference attribute is a well-known discretionary attribute that provides an indication to routers in the AS about which path is preferred to exit the AS.
Notes: <number>

## Slide 16: Summary (Cont.)
  The MED attribute, also called the metric, is an optional nontransitive attribute that is an indication to EBGP neighbors about the preferred path into an AS. The MED is sent to EBGP peers; those routers propagate the MED within their AS. The routers within the AS use the MED, but do not pass it on to the next AS.
  The weight attribute is an attribute that Cisco defines for the path selection process. Routes with a higher weight are preferred when multiple routes exist to the same destination.
  Paths for a network that are determined not to be the best are eliminated from the selection criteria but are still kept in the BGP forwarding table in case the best path becomes inaccessible.
  BGP follows a multiple-step process when selecting the best route to reach a destination.
Notes: <number>