## Slide 1: Implementing BGP
Using Route Maps to Manipulate Basic BGP Paths

## Slide 2: BGP Is Designed to Implement Policy Routing
BGP is designed for manipulating routing paths.
Notes: <number>

## Slide 3: Changing BGP Local Preference For All Routes
bgp default local-preference value
Router(config-router)#
  This command changes the default local preference value.
  All routes advertised to an IBGP neighbor have the local preference set to the value specified.
Local preference is used in these ways:
  Within an AS between IBGP speakers
  To determine the best path to exit the AS to reach an outside network
  Set to 100 by default; higher values preferred

## Slide 4: Local Preference Case Study
What is the best path for router C to 65003, 65004, and 65005?
Notes: <number>

## Slide 5: Router C BGP Table with Default Settings
RouterC# show ip bgp
BGP table version is 7, local router ID is 3.3.3.3
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal, r RIB-failure, S Stale
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
* i172.16.0.0 172.20.50.1 100 0 65005 65004 65003 i
*>i 192.168.28.1 100 0 65002 65003 i
*>i172.24.0.0 172.20.50.1 100 0 65005 i
* i 192.168.28.1 100 0 65002 65003 65004 65005 i
*>i172.30.0.0 172.20.50.1 100 0 65005 65004 i
* i 192.168.28.1 100 0 65002 65003 65004i
  By default, BGP selects the shortest AS path as the best (>) path.
  In AS 65001, the percentage of traffic going to 172.24.0.0 is 30%, 172.30.0.0 is 20%, and 172.16.0.0 is 10%.
  50% of all traffic will go to the next hop of 172.20.50.1 (AS 65005), and 10% of all traffic will go to the next hop of 192.168.28.1 (AS 65002).
  Make traffic to 172.30.0.0 select the next hop of 192.168.28.1 to achieve load sharing where both external links get approximately 30% of the load.

## Slide 6: Route Map for Router A
router bgp 65001
neighbor 2.2.2.2 remote-as 65001
neighbor 3.3.3.3 remote-as 65001
neighbor 2.2.2.2 remote-as 65001 update-source loopback0
neighbor 3.3.3.3 remote-as 65001 update-source loopback0
neighbor 192.168.28.1 remote-as 65002
neighbor 192.168.28.1 route-map local_pref in
!
access-list 65 permit 172.30.0.0 0.0.255.255
!
route-map local_pref permit 10
match ip address 65
set local-preference 400
!
route-map local_pref permit 20
  Router A configuration

## Slide 7: Router C BGP Table with Local Preference Learned
RouterC# show ip bgp
BGP table version is 7, local router ID is 3.3.3.3
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal, r RIB-failure, S Stale
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
* i172.16.0.0 172.20.50.1 100 0 65005 65004 65003 i
*>i 192.168.28.1 100 0 65002 65003 i
*>i172.24.0.0 172.20.50.1 100 0 65005 i
* i 192.168.28.1 100 0 65002 65003 65004 65005 i
* i172.30.0.0 172.20.50.1 100 0 65005 65004 i
*>i 192.168.28.1 400 0 65002 65003 65004i
  Best (>) paths for networks 172.16.0.0/16 and 172.24.0.0/16 have not changed.
  Best (>) path for network 172.30.0.0 has changed to a new next hop of 192.168.28.1 because the next hop of 192.168.28.1 has a higher local preference, 400.
  In AS 65001, the percentage of traffic going to 172.24.0.0 is 30%, 172.30.0.0 is 20%, and 172.16.0.0 is 10%.
  30% of all traffic will go to the next hop of 172.20.50.1 (AS 65005), and 30% of all traffic will go to the next hop of 192.168.28.1 (AS 65002).

## Slide 8: Changing BGP MED for All Routes
default-metric number
Router(config-router)#
  MED is considered the metric of BGP.
  All routes that are advertised to an EBGP neighbor are set to the value specified using this command.
  MED is used when multiple paths exist between two autonomous systems.
  A lower MED value is preferred.
  The default setting for Cisco is MED = 0.
  The metric is an optional, nontransitive attribute.
  Usually, MED is shared only between two autonomous systems that have multiple EBGP connections with each other.

## Slide 9: BGP Using Route Maps and the MED
Notes: <number>

## Slide 10: Route Map for Router A
  Router A’s Configuration:
  router bgp 65001
  neighbor 2.2.2.2 remote-as 65001
  neighbor 3.3.3.3 remote-as 65001
  neighbor 2.2.2.2 update-source loopback0
  neighbor 3.3.3.3 update-source loopback0
  neighbor 192.168.28.1 remote-as 65004
  neighbor 192.168.28.1 route-map med_65004 out
  !
  access-list 66 permit 192.168.25.0.0 0.0.0.255
  access-list 66 permit 192.168.26.0.0 0.0.0.255
  !
  route-map med_65004 permit 10
  match ip address 66
  set metric 100
  !
  route-map med_65004 permit 100
  set metric 200

## Slide 11: Route Map for Router B
  Router B’s Configuration:
  router bgp 65001 neighbor 1.1.1.1 remote-as 65001
  neighbor 3.3.3.3 remote-as 65001
  neighbor 1.1.1.1 update-source loopback0
  neighbor 3.3.3.3 update-source loopback0
  neighbor 172.20.50.1 remote-as 65004
  neighbor 172.20.50.1 route-map med_65004 out
  !
  access-list 66 permit 192.168.24.0.0 0.0.0.255
  !
  route-map med_65004 permit 10
  match ip address 66
  set metric 100
  !
  route-map med_65004 permit 100
  set metric 200

## Slide 12: MED Learned by Router Z
RouterZ# show ip bgp
BGP table version is 7, local router ID is 122.30.1.1
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal, r RIB-failure, S Stale
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
*>i192.168.24.0 172.20.50.2 100 100 0 65001 i
* i 192.168.28.2 200 100 0 65001 i
* i192.168.25.0 172.20.50.2 200 100 0 65001 i
*>i 192.168.28.2 100 100 0 65001 i
* i192.168.26.0 172.20.50.2 200 100 0 65001 i
*>i 192.168.28.2 100 100 0 65001 i
  Examine the networks that have been learned from AS 65001 on Router Z in AS 65004.
  For all networks: Weight is equal (0); local preference is equal (100); routes are not originated in this AS; AS path is equal (65001); origin code is equal (i).
  192.168.24.0 has a lower metric (MED) through 172.20.50.2 (100) than 192.168.28.2 (200).
  192.168.25.0 has a lower metric (MED) through 192.168.28.2 (100) than 172.20.50.2 (200).
  192.168.26.0 has a lower metric (MED) through 192.168.28.2 (100) than 172.20.50.2 (200).

## Slide 13
BGP in an Enterprise

## Slide 14: Summary
  The BGP local preference attribute can be changed to manipulate the best-path decision process, either for all routes or for selected routes using route maps.
    Higher local preference values are preferred.
    Local preference is used only between IBGP speakers within the same AS.
  The MED values can be changed to manipulate packets returning to an AS, either for all routes or for selected routes, using route maps.
    Lower MED values are preferred.
    The MED is sent to EBGP neighbors; those routers propagate the MED within their AS. The routers within the AS use the MED but do not pass it on to the next AS.
  Routers in a typical enterprise BGP implementation multihome to two ISPs and pass default routes to other routers within the enterprise.
Notes: <number>