## Slide 1: Implementing Multicast
IGMP and Layer 2 Issues
Notes: Need title page

## Slide 2: IGMPv2
RFC 2236
  Group-specific query
    Router sends group-specific query to make sure that there are no members present before ceasing to forward data for the group for that subnet.
  Leave group message
    Host sends leave message if it leaves the group and is the last member (reduces leave latency in comparison to v1).
Notes: IGMPv2
  As a result of some of the limitations discovered in IGMPv1, work was begun on IGMPv2 in an attempt to remove these limitations. Most of the changes between IGMPv1 and IGMPv2 are primarily to address the issues of Leave and Join latencies as well as address ambiguities in the original protocol specification. (IGMPv2 is almost to standard status.)
  The following sections define some of the more significant changes.
Group Specific Queries
  A Group Specific query was added in v2 to allow the router to only query membership in a single group instead of all groups. This is an optimized way to quickly find out if any members are left in a group without asking all groups for a report.
  The difference between the Group Specific query and the General Query is that a General Query is multicast to the “All-Hosts” (224.0.0.1) address while a Group Specific query for Group “G”, is multicast to the Group “G” multicast address.
Leave Group message
  A Leave Group message was also added in IGMPv2. This allows end systems to tell the router they are leaving the group which reduces the leave latency for the group on the segment when the member leaving is the last member of the group.
  The standard is loosely written on when leave group messages should and must be sent. This is an important consideration when discussing CGMP.

## Slide 3: IGMPv2—Joining a Group
Notes: IGMP State in “rtr-a”
  Group 224.1.1.1 is active on Ethernet 0 and
    Has been active on this interface for 6 days and 17 hours.
    It expires (and will be deleted) in 2 minutes and 31 seconds if an IGMP Host Membership report for this group is not heard in that time.
    The last Host to report membership was 1.1.1.11 (H2).

## Slide 4: IGMPv2—Leaving a Group
H2 sends a leave message.
Router sends group-specific query.
A remaining member host sends report, so group remains active.
Notes: IGMPv2 Leaves
  In IGMPv1, hosts would leave passively - i.e.. they do not explicitly say they are leaving - they just stop reporting. However, IGMPv2 has explicit “Leave Group” messages.
  When the IGMPv2 Query router receives a “Leave Message”, it responds by sending a “Group Specific Query” for the associated group to see if there are still other hosts wishing to receive traffic for the group. This process helps to reduce overall “Leave Latency”.
  When CGMP is in use, the IGMPv2 “Leave Message” mechanism also helps the router to better manage the CGMP state in the switch. This also improves the leave latency for the specific host at layer 2.
  (Note: Due to the wording of the current IGMPv2 draft specification, hosts may chose to NOT send Leave messages if they are not the last host to leave the group. This can adversely affect CGMP performance.)
Example :
  H2 and H3 are members of group 224.1.1.1
  #1 - H2 leaves
  #2 - Router sends group specific query to see if any other group members are present.
  #3 - H3 hasn’t left yet so it responds with a Report message.
  Router keeps sending multicast for 224.1.1.1 since there is >= 1 member present

## Slide 5: IGMPv2—Leaving a Group (Cont.)
Notes: IGMPv2 Leaves
  At this point, the group is still active. However, the router shows that Host 3 is the last host to send an IGMP Group Membership Report.

## Slide 6: IGMPv2—Leaving a Group (Cont.)
Notes: IGMPv2 Leaves
  At this point, all hosts have left the 224.1.1.1 group on Ethernet0. This is indicated by “rtr-a” above.in the output of the show ip igmp group command.

## Slide 7: IGMPv3—Joining a Group
Joining member sends IGMPv3 report to 224.0.0.22 immediately upon joining.
Notes: Asynchronous Joins
  Members joining a group do not have to waited for a query to join; they send in an unsolicited IGMPv3 Membership Report indicating their interest. This reduces join latency for the end system joining if no other members are present.
    In the example above, Host 2 is joining multicast group 224.1.1.1 and is willing to receive any and all sources in this group.

## Slide 8: IGMPv3—Maintaining State
  Reports contain multiple group state records.
Router sends periodic queries:
All IGMPv3 members respond.
Notes: Query-Response Process
  The router multicasts periodic Membership Queries to the “All-Hosts” (224.0.0.1) group address.
  All hosts on the wire respond by sending back an IGMPv3 Membership Report that contains their complete IGMP Group state for the interface.

## Slide 9: Determining IGMP Version Running
Determining which IGMP version is running on an interface
rtr-a>show ip igmp interface e0
Ethernet0 is up, line protocol is up
Internet address is 1.1.1.1, subnet mask is 255.255.255.0
IGMP is enabled on interface
Current IGMP version is 2
CGMP is disabled on interface
IGMP query interval is 60 seconds
IGMP querier timeout is 120 seconds
IGMP max query response time is 10 seconds
Inbound IGMP access group is not set
Multicast routing is enabled on interface
Multicast TTL threshold is 0
Multicast designated router (DR) is 1.1.1.1 (this system)
IGMP querying router is 1.1.1.1 (this system)
Multicast groups joined: 224.0.1.40 224.2.127.254
Notes: Verifying the IGMP Version on an Interface
  Use the “show ip igmp interface” command to determine which version of IGMP is currently active on an interface.
  This is indicated by the line in the above example that says
    Current IGMP version is 2

## Slide 10: Layer 2 Multicast Frame Switching
Problem: Layer 2 flooding of multicast frames
  Typical Layer 2 switches treat multicast traffic as unknown or broadcast and must flood the frame to every port (in VLAN).
  Static entries may sometimes be set to specify which ports must receive which groups of multicast traffic.
  Dynamic configuration of these entries may reduce administration.
Notes: L2 Multicast Switching
  For most L2 Switches, Multicast traffic is normally treated like an unknown MAC address or Broadcast frame which causes the frame to be flooded out every port within a VLAN at rates of over 1 Mbps. This is fine for unknowns and broadcasts but as we have seen earlier, IP Multicast hosts may join and be interested in only specific multicast groups. Again, on most L2 Switches, all this traffic is forwarded out all ports resulting in wasted bandwidth on both the segments and on the end stations. One way around this on Catalyst Switches is using the Command Line Interface to program the switch manually to associate a multicast MAC address with say ports 5,6,7 so only ports 5,6,and 7 receive the multicast traffic destined for the multicast group. This works fine but again we know IP Multicast hosts dynamically join and leave groups using IGMP to signal to the Multicast Router. This static way of entering the multicast information is not very scaleable. Dynamic configuration of the Switches’ forwarding tables would be a better idea, and cut down on user administration.

## Slide 11: Layer 2 Multicast Switching Solutions
Cisco Group Management Protocol (CGMP): Simple, proprietary; routers and switches
IGMP snooping: Complex, standardized, proprietary implementations; switches only
Notes: Multicast Forwarding
  Routers must know packet origin, rather than destination (opposite of unicast)
    ... origination IP address denotes known source
    ... destination IP address denotes unknown group of receivers
  Multicast routing utilizes Reverse Path Forwarding (RPF)
    ... Broadcast: floods packets out all interfaces except incoming from source; initially assuming every host on network is part of multicast group
    ... Prune: eliminates tree branches without multicast group members; cuts off transmission to LANs without interested receivers
    ... Selective Forwarding: requires its own integrated unicast routing protocol

## Slide 12: Layer 2 Multicast Frame Switching CGMP
Solution 1: CGMP
  Runs on switches and routers.
  CGMP packets sent by routers to switches at the CGMP multicast MAC address
    0100.0cdd.dddd
  CGMP packet contains:
    Type field: join or leave
    MAC address of the IGMP client
    Multicast MAC address of the group
  Switch uses CGMP packet information to add or remove an entry for a particular multicast MAC address.
Notes: Solution 2: CGMP
  CGMP is based on a client server model where the router can be considered a CGMP server and the switch taking on the client role. There are software components running on both devices, with the router translating IGMP messages into CGMP commands which are then executed on the Catalyst 5000 NMP and used to program the EARL’s forwarding tables with the correct Multicast entries. Since the hosts and routers use well-known IP Multicast Addresses, the EARL can be preprogrammed to direct IGMP Control packets both to the router and the NMP. We will see the NMPs use of these IGMP control packets in a later slide. The basis of CGMP is that the IP Multicast router sees all IGMP packets and therefore can inform the switch when specific hosts join or leave Multicast groups. The switch then uses this information to program it’s forwarding table. When the router sees an IGMP control packet it creates a CGMP packet that contains the request type (Join or Leave), the Layer 2 Multicast MAC Address, and the actual MAC address of the client. This packet is sent to a well known address which all CGMP switches listen on. It is then interpreted and the proper entries created in the switch’s CAM Table to constrain the forwarding of multicast traffic for this group.

## Slide 13: Layer 2 Multicast Frame Switching IGMP Snooping
Solution 2: IGMP snooping
  Switches become IGMPaware.
  IGMP packets are intercepted by the CPU or by special hardware ASICs.
  The switch must examine contents of IGMP messages to determine which ports want what traffic:
    IGMP membership reports
    IGMP leave messages
  Effect on switch:
    Must process all Layer 2 multicast packets
    Administration load increased with multicast traffic load
    Requires special hardware to maintain throughput
Notes: Solution 1: IGMP Snooping
  As its name implies, switch become IGMP “aware” and listen in on the IGMP conversations between hosts and routers.
  This requires the processor in the switch to identify and intercept a copy of all IGMP packets flowing between router and hosts and vice versa. This includes:
    IGMP Membership Reports
    IGMP Leaves
  If care is not taken as to how IGMP Snooping is implemented, a switch may have to intercept ALL layer 2 multicast packets in order to identify IGMP packets.
    This can have a significant impact on the switch’s performance.
    Proper designs require special hardware to avoid this problem. This can directly affect the overall cost of the switch.

## Slide 14: Summary
  IGMPv2 is a protocol used by multicast clients to join a multicast group.
  IGMPv3 allows a receiver to specify a source.
  If controls such as CGMP and IGMP snooping are not added at the Ethernet switching level, all multicast frames are flooded.
  CGMP is a Cisco proprietary protocol used to implement multicast efficiently.
  IGMP snooping is a standard protocol that has a function similar to CGMP.