## Slide 1: Implementing Multicast
Explaining Multicast Routing Protocols

## Slide 2: Multicast Protocol Basics
Types of multicast distribution trees
  Source-rooted; also called shortest path trees (SPTs)
  Rooted at a meeting point in the network; shared trees
    Rendezvous point (RP)
    Core
Types of multicast protocols
  Dense mode protocols
  Sparse mode protocols
Notes: Multicast Distribution Trees
  Defines the path down which traffic flows from source to receiver(s).
Multicast Forwarding
  Unlike unicast forwarding which uses the “destination” address to make it’s forwarding decision, multicast forwarding uses the “source” address to make it’s forwarding decision.
Type of Multicast Protocols
  Dense Mode Protocols
  Spares Mode Protocols

## Slide 3: Shortest-Path Trees
Shortest-Path or Source Distribution Tree
Notes: Shortest Path Trees — aka Source Trees
  A Shortest path or source distribution tree is a minimal spanning tree with the lowest cost from the source to all leaves of the tree.
  We forward packets on the Shortest Path Tree according to both the Source Address that the packets originated from and the Group address G that the packets are addressed to. For this reason we refer to the forwarding state on the SPT by the notation (S,G) (pronounced “S comma G”).
  where:
    “S” is the IP address of the source.
    “G” is the multicast group address
  Example 1:
    The shortest path between Source 1 and Receiver 1 is via Routers A and C, and shortest path to Receiver 2 is one additional hop via Router E.

## Slide 4: Shortest-Path Trees (Cont.)
Shortest-Path or Source Distribution Tree
Notes: Shortest Path Trees — aka Source Trees
  A Shortest path or source distribution tree is a minimal spanning tree with the lowest cost from the source to all leaves of the tree.
  We forward packets on the Shortest Path Tree according to both the Source Address that the packets originated from and the Group address G that the packets are addressed to. For this reason we refer to the forwarding state on the SPT by the notation (S,G) (pronounced “S comma G”).
  where:
    “S” is the IP address of the source.
    “G” is the multicast group address
  Example 1:
    The shortest path between Source 1 and Receiver 1 is via Routers A and C, and shortest path to Receiver 2 is one additional hop via Router E.

## Slide 5: Shared Distribution Trees
Shared Distribution Tree
Notes: Shortest Path Trees — aka Source Trees
  A Shortest path or source distribution tree is a minimal spanning tree with the lowest cost from the source to all leaves of the tree.
  We forward packets on the Shortest Path Tree according to both the Source Address that the packets originated from and the Group address G that the packets are addressed to. For this reason we refer to the forwarding state on the SPT by the notation (S,G) (pronounced “S comma G”).
  where:
    “S” is the IP address of the source.
    “G” is the multicast group address
  Example 1:
    The shortest path between Source 1 and Receiver 1 is via Routers A and C, and shortest path to Receiver 2 is one additional hop via Router E.

## Slide 6: Shared Distribution Trees (Cont.)
Shared Distribution Tree
Notes: Shortest Path Trees — aka Source Trees
  A Shortest path or source distribution tree is a minimal spanning tree with the lowest cost from the source to all leaves of the tree.
  We forward packets on the Shortest Path Tree according to both the Source Address that the packets originated from and the Group address G that the packets are addressed to. For this reason we refer to the forwarding state on the SPT by the notation (S,G) (pronounced “S comma G”).
  where:
    “S” is the IP address of the source.
    “G” is the multicast group address
  Example 1:
    The shortest path between Source 1 and Receiver 1 is via Routers A and C, and shortest path to Receiver 2 is one additional hop via Router E.

## Slide 7: Multicast Distribution Trees Identification
(S,G) entries
  For this particular source sending to this particular group
  Traffic forwarded via the shortest path from the source
(*,G) entries
  For any (*) source sending to this group
  Traffic forwarded via a meeting point for this group
Notes: Source or Shortest Path Tree Characteristics
  Provides optimal path (shortest distance and minimized delay) from source to all receivers, but requires more memory to maintain
Shared Tree Characteristics
  Provides sub-optimal path (may not be shortest distance and may introduce extra delay) from source to all receivers, but requires less memory to maintain

## Slide 8: Multicast Forwarding
Multicast routing operation is the opposite of unicast routing.
  Unicast routing is concerned with where the packet is going.
  Multicast routing is concerned with where the packet comes from.
Multicast routing uses Reverse Path Forwarding to prevent forwarding loops.
Notes: Multicast Forwarding
  Routers must know packet origin, rather than destination (opposite of unicast)
    ... origination IP address denotes known source
    ... destination IP address denotes unknown group of receivers
  Multicast routing utilizes Reverse Path Forwarding (RPF)
    ... Broadcast: floods packets out all interfaces except incoming from source; initially assuming every host on network is part of multicast group
    ... Prune: eliminates tree branches without multicast group members; cuts off transmission to LANs without interested receivers
    ... Selective Forwarding: requires its own integrated unicast routing protocol

## Slide 9: PIM-DM Flood and Prune
Initial Flooding
Notes: PIM-DM Initial Flooding
  PIM-DM is similar to DVMRP in that it initially floods multicast traffic to all parts of the network.
  However unlike DVMRP, which pre-builds a “Truncated Broadcast Tree” that is used for initial flooding, PIM-DM initially floods traffic out ALL non RPF interfaces where there is:
    Another PIM-DM neighbor or
    A directly connected member of the group
  The reason that PIM-DM does not use “Truncated Broadcast Trees” to pre-build a spanning tree for each source network is that this would require running a separate routing protocol as does DVMRP. (At the very least, some sort of Poison-Reverse messages would have to be sent to build the TBT.) Instead, PIM-DM uses other mechanisms to prune back the traffic flows and build Source Trees.
Initial Flooding Example
  In this example, multicast traffic being sent by the source is flooded throughout the entire network.
  As each router receives the multicast traffic via its RPF interface (the interface in the direction of the source), it forwards the multicast traffic to all of its PIM-DM neighbors.
  Note that this results in some traffic arriving via a non-RPF interface such as the case of the two routers in the center of the drawing. (Packets arriving via the non-RPF interface are discarded.) These non-RPF flows are normal for the initial flooding of data and will be corrected by the normal PIM-DM pruning mechanism.

## Slide 10: PIM-DM Flood and Prune (Cont.)
Notes: PIM-DM Initial Flooding
  PIM-DM is similar to DVMRP in that it initially floods multicast traffic to all parts of the network.
  However unlike DVMRP, which pre-builds a “Truncated Broadcast Tree” that is used for initial flooding, PIM-DM initially floods traffic out ALL non RPF interfaces where there is:
    Another PIM-DM neighbor or
    A directly connected member of the group
  The reason that PIM-DM does not use “Truncated Broadcast Trees” to pre-build a spanning tree for each source network is that this would require running a separate routing protocol as does DVMRP. (At the very least, some sort of Poison-Reverse messages would have to be sent to build the TBT.) Instead, PIM-DM uses other mechanisms to prune back the traffic flows and build Source Trees.
Initial Flooding Example
  In this example, multicast traffic being sent by the source is flooded throughout the entire network.
  As each router receives the multicast traffic via its RPF interface (the interface in the direction of the source), it forwards the multicast traffic to all of its PIM-DM neighbors.
  Note that this results in some traffic arriving via a non-RPF interface such as the case of the two routers in the center of the drawing. (Packets arriving via the non-RPF interface are discarded.) These non-RPF flows are normal for the initial flooding of data and will be corrected by the normal PIM-DM pruning mechanism.

## Slide 11: PIM-DM Flood and Prune (Cont.)
Results After Pruning
Notes: PIM-DM Initial Flooding
  PIM-DM is similar to DVMRP in that it initially floods multicast traffic to all parts of the network.
  However unlike DVMRP, which pre-builds a “Truncated Broadcast Tree” that is used for initial flooding, PIM-DM initially floods traffic out ALL non RPF interfaces where there is:
    Another PIM-DM neighbor or
    A directly connected member of the group
  The reason that PIM-DM does not use “Truncated Broadcast Trees” to pre-build a spanning tree for each source network is that this would require running a separate routing protocol as does DVMRP. (At the very least, some sort of Poison-Reverse messages would have to be sent to build the TBT.) Instead, PIM-DM uses other mechanisms to prune back the traffic flows and build Source Trees.
Initial Flooding Example
  In this example, multicast traffic being sent by the source is flooded throughout the entire network.
  As each router receives the multicast traffic via its RPF interface (the interface in the direction of the source), it forwards the multicast traffic to all of its PIM-DM neighbors.
  Note that this results in some traffic arriving via a non-RPF interface such as the case of the two routers in the center of the drawing. (Packets arriving via the non-RPF interface are discarded.) These non-RPF flows are normal for the initial flooding of data and will be corrected by the normal PIM-DM pruning mechanism.

## Slide 12: PIM Sparse Mode
  Protocol independent: works with any of the underlying unicast routing protocols
  Supports both source and shared trees
  Based on an explicit pull model
  Uses an RP
    Senders and receivers “meet each other.”
      Senders are registered with RP by their first-hop router.
      Receivers are joined to the shared tree (rooted at the RP) by their local DR.
Notes: Protocol Independent Multicast (PIM) Sparse-mode (RFC 2362)
  Utilizes a rendezvous point (RP) to coordinate forwarding from source to receivers
    Regardless of location/number of receivers, senders register with RP and send a single copy of multicast data through it to registered receivers
    Regardless of location/number of sources, group members register to receive data and always receive it through the RP
  Appropriate for
    Wide scale deployment for both densely and sparsely populated groups in the Enterprise
    Optimal choice for all production networks regardless of size and membership density.

## Slide 13: PIM-SM Shared Tree Join
Notes: PIM-SM Shared Tree Joins
  In this example, there is an active receiver (attached to leaf router at the bottom of the drawing) has joined multicast group “G”.
  The leaf router knows the IP address of the Rendezvous Point (RP) for group G and when it sends a (*,G) Join for this group towards the RP.
  This (*, G) Join travels hop-by-hop to the RP building a branch of the Shared Tree that extends from the RP to the last-hop router directly connected to the receiver.
  At this point, group “G” traffic can flow down the Shared Tree to the receiver.

## Slide 14: Multiple RPs with Auto RP
Shared Distribution Tree
Notes: PIM-SM Shared Tree Joins
  In this example, there is an active receiver (attached to leaf router at the bottom of the drawing) has joined multicast group “G”.
  The leaf router knows the IP address of the Rendezvous Point (RP) for group G and when it sends a (*,G) Join for this group towards the RP.
  This (*, G) Join travels hop-by-hop to the RP building a branch of the Shared Tree that extends from the RP to the last-hop router directly connected to the receiver.
  At this point, group “G” traffic can flow down the Shared Tree to the receiver.

## Slide 15: Summary
  IP multicast requires multiple protocols and processes for proper packet forwarding.
  Source and shared trees may be used to define multicast packet flows to group members.
  Multicast routing utilizes the distribution trees for proper packet forwarding.
  PIM is the routing protocol for multicast.
  PIM-DM uses flood and prune.
  PIM-SM uses less device and bandwidth resources and is typically chosen to implement multicast. PIM sparse-dense mode is the recommended methodology for maximum efficiency in IP multicast.