## Slide 1: Implementing Multicast
Multicast Configuration and Verification

## Slide 2: PIM-SM Configuration Commands
ip multicast-routing
router(config)#
Enables multicast routing.
ip pim { sparse-mode | sparse-dense-mode }
router(config-if)#
Enables PIM SM on an interface; the sparse-dense-mode option enables mixed sparse-dense groups.
ip pim send-rp-announce {interface type} scope {ttl} group-list {acl}
ip pim send-rp-discovery {interface type} scope {ttl}
router(config)#
Configures the ability of a group of routers to be and discover RPs dynamically.

## Slide 3: Inspecting Multicast Routing Table
Displays the contents of the IP multicast routing table
  summary: Displays a one-line, abbreviated summary of each entry in the IP multicast routing table.
  count: Displays statistics about the group and source, including number of packets, packets per second, average packet size, and bits per second.
  active: Displays the rate at which active sources are sending to multicast groups. Active sources are those sending at a rate specified in the kbps argument or higher. The kbps argument defaults to 4 kbps.
show ip mroute [group-address] [summary] [count] [active kbps]
router#
Notes: The show ip mroute command is the most useful command in determining the state of multicast sources and groups as seen from the selected router perspective. The output of the command generally represents a part of the multicast distribution tree with incoming interface ald list of outgoing interfaces.

## Slide 4: show ip mroute
NA-1#sh ip mroute
IP Multicast Routing Table
Flags: D - Dense, S - Sparse, B - Bidir Group, s - SSM Group, C - Connected
L - Local, P - Pruned, R - RP-bit set, F - Register flag,
T - SPT-bit set, J - Join SPT, M - MSDP created entry,
X - Proxy Join Timer Running, A - Advertised via MSDP, U - URD,
I - Received Source Specific Host Report
Outgoing interface flags: H - Hardware switched
Timers: Uptime/Expires
Interface state: Interface, Next-Hop or VCD, State/Mode
(*, 224.1.1.1), 00:07:54/00:02:59, RP 10.127.0.7, flags: S
Incoming interface: Null, RPF nbr 0.0.0.0
Outgoing interface list:
Serial1/3, Forward/Sparse, 00:07:54/00:02:32
(172.16.8.1, 224.1.1.1), 00:01:29/00:02:08, flags: TA
Incoming interface: Serial1/4, RPF nbr 10.139.16.130
Outgoing interface list:
Serial1/3, Forward/Sparse, 00:00:57/00:02:02
Notes: Partial output taken from a production router in Cisco’s network for more interesting output.
This is a generic multicast routing table.
Note the:
  (*,G) and (S,G) entries
  Incoming interface
  Outgoing interface list (OIF)
  RP (if any)
  Flags
  Timers - how long the entry has been in the table and when it will expire

## Slide 5: Finding PIM Neighbors
show ip pim interface [type number] [count]
router#
Displays information about interfaces configured for PIM
show ip pim neighbor [type number]
router#
Lists the PIM neighbors discovered by the Cisco IOS software
mrinfo [hosthanme | address]
router#
Queries which neighboring multicast routers are peering with the local router or router specified
Notes: When PIM Dense Mode is configured, the first step to check for proper operation is to determine the PIM neighbors. The following commands do this:
  show ip pim interface
  show ip pim neighbor
  mrinfo

## Slide 6: show ip pim interface
NA-2#show ip pim interface
Address Interface Ver/ Nbr Query DR DR
Mode Count Intvl Prior
10.139.16.133 Serial0/0 v2/S 1 30 1 0.0.0.0
10.127.0.170 Serial1/2 v2/S 1 30 1 0.0.0.0
10.127.0.242 Serial1/3 v2/S 1 30 1 0.0.0.0
Notes: Nbr Count = number of neighbors on this link
DR = 0.0.0.0 in this example, because p2p links do not have DRs

## Slide 7: show ip pim neighbor
NA-2#show ip pim neighbor
PIM Neighbor Table
Neighbor Interface Uptime/Expires Ver DR
Address Priority
10.139.16.134 Serial0/0 00:01:46/00:01:28 v2 None
10.127.0.169 Serial1/2 00:01:05/00:01:40 v2 1 (BD)
10.127.0.241 Serial1/3 00:01:56/00:01:18 v2 1 (BD)
Notes: Uptime—indicates how long the neighbor adjacency has existed
Expires—indicates when the adjacency will timeout and be removed - PIM hellos maintain this adjacency
Mode—indicates what mode the interface is running in

## Slide 8: Checking RP Information
  Displays active RPs that are cached with associated multicast routing entries
    Mapping—displays all group-to-RP mappings that the router is aware of
show ip pim rp [group-name | group-address | mapping]
router(config)#
  Displays how IP multicast routing does Reverse Path Forwarding (RPF)
    Address—IP address of a source of an RP
show ip rpf {address | name }
router(config)#

## Slide 9: show ip pim rp
P4-2#show ip pim rp
Group: 224.1.2.3, RP: 10.127.0.7, uptime 00:00:20, expires never
P4-2#show ip pim rp mapping
PIM Group-to-RP Mappings
Group(s) 224.0.1.39/32
RP 10.127.0.7 (NA-1), v1
Info source: local, via Auto-RP
Uptime: 00:00:21, expires: never
Group(s) 224.0.1.40/32
RP 10.127.0.7 (NA-1), v1
Info source: local, via Auto-RP
Uptime: 00:00:21, expires: never
Group(s): 224.0.0.0/4, Static
RP: 10.127.0.7 (NA-1)
Notes: This command lists the RPs - they can be learned statically or dynamically.
Note that there can be multiple RPs in the network each supporting a different multicast address range.

## Slide 10: show ip rpf
(towards the RP)
NA-2#show ip rpf 10.127.0.7
RPF information for NA-1 (10.127.0.7)
RPF interface: Serial1/3
RPF neighbor: ? (10.127.0.241)
RPF route/mask: 10.127.0.7/32
RPF type: unicast (ospf 1)
RPF recursion count: 0
Doing distance-preferred lookups across tables
(towards the source)
NA-2#show ip rpf 10.139.17.126
RPF information for ? (10.139.17.126)
RPF interface: Serial0/0
RPF neighbor: ? (10.139.16.134)
RPF route/mask: 10.139.17.0/25
RPF type: unicast (ospf 1)
RPF recursion count: 0
Doing distance-preferred lookups across tables
Notes: This command lists the RPs - they can be learned statically or dynamically.
Note that there can be multiple RPs in the network each supporting a different multicast address range.

## Slide 11: Checking the Group State
show ip igmp interface [type number]
router#
Displays multicast-related information about an interface
show ip igmp groups [group-address | type number]
router#
Displays the multicast groups that are directly connected to the router and that were learned via IGMP
Notes: If traffic is not flowing to receivers, the IGMP group membership has to be checked in local routers. The command show ip igmp interface shows various information on the selected interface and show ip igmp groups lists the local groups known to the router.

## Slide 12: show ip igmp interface
rtr-a>show ip igmp interface e0
Ethernet0 is up, line protocol is up
Internet address is 1.1.1.1, subnet mask is 255.255.255.0
IGMP is enabled on interface
Current IGMP version is 2
CGMP is disabled on interface
IGMP query interval is 60 seconds
IGMP querier timeout is 120 seconds
IGMP max query response time is 10 seconds
Inbound IGMP access group is not set
Multicast routing is enabled on interface
Multicast TTL threshold is 0
Multicast designated router (DR) is 1.1.1.1 (this system)
IGMP querying router is 1.1.1.1 (this system)
Multicast groups joined: 224.0.1.40 224.2.127.254
Notes: Verifying the state of multicast groups on the router:
  Use the “show ip igmp interface” command to determine which router is the IGMPv2 Querier on the multiaccess network.
  Note that the “Designated Router” is a different function and is listed separately in the display above.
  Note also that the router itself joined two groups (224.0.1.40 – Auto-RP, which was joined automatically, and 224.2.127.254 – SDR, which was joined by configuring ip sdr listen on the interface).

## Slide 13: show ip igmp groups
rtr-a>sh ip igmp groups
IGMP Connected Group Membership
Group Address Interface Uptime Expires Last Reporter
224.1.1.1 Ethernet0 6d17h 00:01:47 1.1.1.12
224.0.1.40 Ethernet0 6d17h never 1.1.1.17
Notes: IGMP State in “rtr-a”:
  Group 224.1.1.1 is active on Ethernet 0 and
    Has been active on this interface for six days and 17 hours.
    It expires (and will be deleted) in two minutes and 31 seconds if an IGMP Host Membership report for this group is not heard in that time.
    The last Host to report membership was 1.1.1.11 (H2).
Group 224.0.1.40 (Auto-RP) is automatically joined by Cisco routers and thus its expiration shows never.

## Slide 14: Verifying IGMP Snooping
  Displays information about multicast groups.
  If igmp keyword is used, only IGMP-learned information is shown.
show multicast group [igmp] [mac_addr] [vlan_id]
switch>
  Displays information on dynamically learned and manually configured multicast router ports.
  If igmp keyword is used, only IGMP-learned information is shown.
show multicast router [igmp] [mod_num/port_num] [vlan_id]
switch>
Notes: Use the show multicast group command to display the multicast group configuration.
Use the show multicast router command to display the information about dynamically learned and manually configured multicast router ports. IGMP keyword specifies to display only the configuration information learned through IGMP.

## Slide 15: Verifying IGMP Snooping—Example
Notes: In the example above we have IGMP enabled multicast router with the IP address 10.0.0.1 and a multicast receiver with the IP address 10.0.0.2 connected to the router via switch that has IGMP Snooping enabled over ports 4/1 and 4/2 respectively. Both ports are in a vlan 10. The IGMP router with the MAC address 00-10-11-7e-74-8d is a member of multicast group 224.0.1.40 and the multicast receiver with the MAC address 00-90-5f-69-a0-21 is receiving mulicast traffic from multicast group 224.1.2.3.

## Slide 16: Verifying IGMP Snooping—Example (Cont.)
Switch> show igmp statistics 10
IGMP enabled
IGMP statistics for vlan 10:
IGMP statistics for vlan 10:
Transmit:
General Queries: 0
Group Specific Queries: 0
Reports: 0
Leaves: 0
Receive:
General Queries: 1
Group Specific Queries: 0
Reports: 2
Leaves: 0
Total Valid pkts: 4
Total Invalid pkts: 0
Other pkts: 1
MAC-Based General Queries: 0
Failures to add GDA to EARL: 0
Topology Notifications: 0
Notes: The output of show igmp statistics shows sample statistics for VLAN 10. The number of Group Specific Queries and General Queries is shown along with the number of Host Memebrship Report and Group Leave messages.
The statistics are split into Receive and Transmit parts.

## Slide 17: Verifying IGMP Snooping—Example (Cont.)
Switch> show multicast router igmp
Port Vlan
---------- ----------------
4/1 10
Total Number of Entries = 1
'*' - Configured
'+' - RGMP-capable
Switch> show multicast group igmp
VLAN Dest MAC/Route Des [CoS] Destination Ports or VCs / [Protocol Type]
---- ---------------------------------------------------------------------
10 01-00-5e-00-01-28 4/1
10 01-00-5e-01-02-03 4/1-2
Total Number of Entries = 2
Notes: The show multicast router command displays the information about IGMP router port and VLAN configuration on a switch.
The show multicast group igmp command list the information about the VLAN, multicast group and ports that are joined to that multicast group on a switch.

## Slide 18: Summary
  Configuring a simple multicast network requires a global multicast command, a multicast command for each interface, and the specification of an RP discovery method.
  Effective methods for verifying a multicast network include checking the multicast routing table and checking PIM neighbors.
  Configuring IGMP snooping on an Ethernet switch avoids the problem of multicast frame flooding.