## Slide 1: Implementing IPv6
Introducing IPv6

## Slide 2: Why Do We Need a Larger Address Space?
  Internet population
    Approximately 973 million users in November 2005
    Emerging population and geopolitical and address space
  Mobile users
    PDA, pen-tablet, notepad, and so on
    Approximately 20 million in 2004
  Mobile phones
    Already 1 billion mobile phones delivered by the industry
  Transportation
    1 billion automobiles forecast for 2008
    Internet access in planes – Example: Lufthansa
  Consumer devices
    Sony mandated that all its products be IPv6-enabled by 2005
    Billions of home and industrial appliances

## Slide 3: IPv6 Advanced Features
Larger address space
  Global reachability and flexibility
  Aggregation
  Multihoming
  Autoconfiguration
  Plug-and-play
  End to end without NAT
  Renumbering
Simpler header
  Routing efficiency
  Performance and forwarding rate scalability
  No broadcasts
  No checksums
  Extension headers
  Flow labels

## Slide 4: IPv6 Advanced Features (Cont.)
Mobility and security
  Mobile IP RFC-compliant
  IPsec mandatory (or native) for IPv6
Transition richness
  Dual stack
  6to4 tunnels
  Translation

## Slide 5: Larger Address Space
IPv4
  32 bits or 4 bytes long
    4,200,000,000 possible addressable nodes
IPv6
  128 bits or 16 bytes: four times the bits of IPv4
    3.4 * 1038 possible addressable nodes
    340,282,366,920,938,463,374,607,432,768,211,456
    5 * 1028 addresses per person
~ =
~ =
~ =
~ =

## Slide 6: Larger Address Space Enables Address Aggregation
  Aggregation of prefixes announced in the global routing table
  Efficient and scalable routing
  Improved bandwidth and functionality for user traffic

## Slide 7: Summary
  IPv6 is a powerful enhancement to IPv4. Features that offer functional improvement include a larger address space, simplified header, and mobility and security.
  IPv6 increases the number of address bits by a factor of four, from 32 to 128.