## Slide 1: Implementing IPv6
Defining IPv6 Addressing

## Slide 2: Simple and Efficient Header
A simpler and more efficient header means:
  64-bit aligned fields and fewer fields
  Hardware-based, efficient processing
  Improved routing efficiency and performance
  Faster forwarding rate with better scalability

## Slide 3: IPv4 and IPv6 Header Comparison

## Slide 4: IPv6 Extension Headers
Simpler and more efficient header means:
  IPv6 has extension headers.
  It handles the options more efficiently.
  It enables faster forwarding rate and end nodes processing.

## Slide 5: IPv6 Address Representation
Format:
  x:x:x:x:x:x:x:x, where x is a 16-bit hexadecimal field
    Case-insensitive for hexadecimal A, B, C, D, E, and F
  Leading zeros in a field are optional:
    2031:0:130F:0:0:9C0:876A:130B
  Successive fields of 0 can be represented as ::, but only once per address.
  Examples:
    2031:0000:130F:0000:0000:09C0:876A:130B
    2031:0:130f::9c0:876a:130b
    2031::130f::9c0:876a:130b—incorrect
    FF01:0:0:0:0:0:0:1 FF01::1
    0:0:0:0:0:0:0:1 ::1
    0:0:0:0:0:0:0:0 ::

## Slide 6: IPv6 Address Types
IPv6 uses:
  Unicast
    Address is for a single interface.
    IPv6 has several types (for example, global and IPv4 mapped).
  Multicast
    One-to-many
    Enables more efficient use of the network
    Uses a larger address range
  Anycast
    One-to-nearest (allocated from unicast address space).
    Multiple devices share the same address.
    All anycast nodes should provide uniform service.
    Source devices send packets to anycast address.
    Routers decide on closest device to reach that destination.
    Suitable for load balancing and content delivery services.

## Slide 7: IPv6 Global Unicast (and Anycast) Addresses
IPv6 has same address format for global unicast and for anycast.
  Uses a global routing prefix—a structure that enables aggregation upward, eventually to the ISP.
  A single interface may be assigned multiple addresses of any type (unicast, anycast, multicast).
  Every IPv6-enabled interface must contain at least one loopback (::1/128) and one link-local address.
  Optionally, every interface can have multiple unique local and global addresses.
  Anycast address is a global unicast address assigned to a set of interfaces (typically on different nodes).
  IPv6 anycast is used for a network multihomed to several ISPs that have multiple connections to each other.

## Slide 8: IPv6 Unicast Addressing
  IPv6 addressing rules are covered by multiple RFCs.
    Architecture defined by RFC 4291.
  Unicast: One to one
    Global
    Link local (FE80::/10)
  A single interface may be assigned multiple IPv6 addresses of any type: unicast, anycast, or multicast.

## Slide 9: Summary
  The IPv6 header has 40 octets and is simpler and more efficient than the IPv4 header.
  IPv6 addresses use 16-bit hexadecimal number fields separated by colons (:) to represent the 128-bit addressing format.
  The three types of IPv6 addresses are unicast, multicast, and anycast.