## Slide 1: Implementing IPv6
Implementing Dynamic IPv6 Addresses

## Slide 2: Aggregatable Global Unicast Addresses
  Cisco uses the extended universal identifier (EUI)-64 format to do stateless autoconfiguration.
  This format expands the 48-bit MAC address to 64 bits by inserting “FFFE” into the middle 16 bits.
  To make sure that the chosen address is from a unique Ethernet MAC address, the universal/local (U/L bit) is set to 1 for global scope (0 for local scope).

## Slide 3: Link-Local Address
  Link-local addresses have a scope limited to the link and are dynamically created on all IPv6 interfaces by using a specific link-local prefix FE80::/10 and a 64-bit interface identifier.
  Link-local addresses are used for automatic address configuration, neighbor discovery, and router discovery. Link-local addresses are also used by many routing protocols.
  Link-local addresses can serve as a way to connect devices on the same local network without needing global addresses.
  When communicating with a link-local address, you must specify the outgoing interface because every interface is connected to FE80::/10.

## Slide 4: EUI-64 to IPv6 Interface Identifier
A modified EUI-64 address is formed by inserting “FFFE” and “complementing” a bit identifying the uniqueness of the MAC address.
Notes: EUI-64 to IPv6 Interface Identifier
The interface identifier for stateless auto-configuration in an Ethernet environment uses the modified EUI-64 format. This format expands the 48-bit Ethernet MAC address format to a 64-bit version by inserting "FFFE" in the middle of the 48 bits. This creates a 64-bit version.
The 7th bit (starting with the leftmost bit as “1”) in an IPv6 interface identifier is referred to as the Universal/Local bit, or U/L bit. This bit identifies whether this interface identifier is locally unique on the link or that it is universally unique. In the case where the interface identifier is created from an Ethernet MAC address, it is assumed that the MAC address is universally unique and, therefore, the interface identifier is universally unique.
The rationale of the U/L bit is for future use of the upper-layer protocols to uniquely identify a connection, even in the context of a change in the leftmost part of the address. However, this is not yet used.
The 8th bit (starting with leftmost bit as “1”), also known as the “G” bit, is a group/individual bit for managing groups.
Note to Graphic Designer:
Animation is needed for this slide.
Stage 1: Show Ethernet MAC address (top address on slide) and two FF and FE blocks.
Stage 2: Show the FF and FE blocks going in-between blocks 27 and 17 of Ethernet address. Change label of address to Ethernet MAC address (64 bits). Also Show the U/L bit coming out of the OO block with the where U = information.
Stage 3: Show final Modified EUI-64 address.
Instructor Note
Discuss the transformative process for EUI-64 to IPv6 interface identifier.

## Slide 5: EUI-64 to IPv6 Interface Identifier (Cont.)
  A modified EUI-64 address is formed by inserting “FFFE” and “complementing” a bit identifying the uniqueness of the MAC address.
Notes: EUI-64 to IPv6 Interface Identifier
The interface identifier for stateless auto-configuration in an Ethernet environment uses the modified EUI-64 format. This format expands the 48-bit Ethernet MAC address format to a 64-bit version by inserting "FFFE" in the middle of the 48 bits. This creates a 64-bit version.
The 7th bit (starting with the leftmost bit as “1”) in an IPv6 interface identifier is referred to as the Universal/Local bit, or U/L bit. This bit identifies whether this interface identifier is locally unique on the link or that it is universally unique. In the case where the interface identifier is created from an Ethernet MAC address, it is assumed that the MAC address is universally unique and, therefore, the interface identifier is universally unique.
The rationale of the U/L bit is for future use of the upper-layer protocols to uniquely identify a connection, even in the context of a change in the leftmost part of the address. However, this is not yet used.
The 8th bit (starting with leftmost bit as “1”), also known as the “G” bit, is a group/individual bit for managing groups.
Note to Graphic Designer:
Animation is needed for this slide.
Stage 1: Show Ethernet MAC address (top address on slide) and two FF and FE blocks.
Stage 2: Show the FF and FE blocks going in-between blocks 27 and 17 of Ethernet address. Change label of address to Ethernet MAC address (64 bits). Also Show the U/L bit coming out of the OO block with the where U = information.
Stage 3: Show final Modified EUI-64 address.
Instructor Note
Discuss the transformative process for EUI-64 to IPv6 interface identifier.

## Slide 6: EUI-64 to IPv6 Interface Identifier (Cont.)
  A modified EUI-64 address is formed by inserting “FFFE” and “complementing” a bit identifying the uniqueness of the MAC address.
Notes: EUI-64 to IPv6 Interface Identifier
The interface identifier for stateless auto-configuration in an Ethernet environment uses the modified EUI-64 format. This format expands the 48-bit Ethernet MAC address format to a 64-bit version by inserting "FFFE" in the middle of the 48 bits. This creates a 64-bit version.
The 7th bit (starting with the leftmost bit as “1”) in an IPv6 interface identifier is referred to as the Universal/Local bit, or U/L bit. This bit identifies whether this interface identifier is locally unique on the link or that it is universally unique. In the case where the interface identifier is created from an Ethernet MAC address, it is assumed that the MAC address is universally unique and, therefore, the interface identifier is universally unique.
The rationale of the U/L bit is for future use of the upper-layer protocols to uniquely identify a connection, even in the context of a change in the leftmost part of the address. However, this is not yet used.
The 8th bit (starting with leftmost bit as “1”), also known as the “G” bit, is a group/individual bit for managing groups.
Note to Graphic Designer:
Animation is needed for this slide.
Stage 1: Show Ethernet MAC address (top address on slide) and two FF and FE blocks.
Stage 2: Show the FF and FE blocks going in-between blocks 27 and 17 of Ethernet address. Change label of address to Ethernet MAC address (64 bits). Also Show the U/L bit coming out of the OO block with the where U = information.
Stage 3: Show final Modified EUI-64 address.
Instructor Note
Discuss the transformative process for EUI-64 to IPv6 interface identifier.

## Slide 7: Multicasting

## Slide 8: Examples of Permanent Multicast Addresses

## Slide 9: Anycast
  An IPv6 anycast address is a global unicast address that is assigned to more than one interface.

## Slide 10: Stateless Autoconfiguration

## Slide 11: A Standard Stateless Autoconfiguration
  Stage 1: The PC sends a router solicitation to request a prefix for stateless autoconfiguration.

## Slide 12: A Standard Stateless Autoconfiguration (Cont.)
  Stage 2: The router replies with a router advertisement.

## Slide 13: IPv6 Mobility

## Slide 14: Summary
  The MAC address may form a portion of the IPv6 system ID.
  IPv6 multicast addresses are defined by the prefix FF00::/8. Multicast is frequently used in IPv6 and replaces broadcast.
  IPv6 provides an efficient means to implement mobile IP, which has not been possible with IPv4.