## Slide 1: Implementing IPv6
Using IPv6 with OSPF and Other Routing Protocols

## Slide 2: IPv6 Routing Protocols
  IPv6 routing types
    Static
    RIPng (RFC 2080)
    OSPFv3 (RFC 2740)
    IS-IS for IPv6
    MP-BGP4 (RFC 2545/2858)
    EIGRP for IPv6
  The ipv6 unicast-routing command is required to enable IPv6 before any routing protocol configured.

## Slide 3: RIPng
Same as IPv4
  Distance vector, radius of 15 hops, split horizon, and poison reverse
  Based on RIPv2
Updated features for IPv6
  IPv6 prefix, next-hop IPv6 address
  Uses the multicast group FF02::9, the all-rip-routers multicast group, as the destination address for RIP updates
  Uses IPv6 for transport
  Named RIPng

## Slide 4: OSPF Version 3 (OSPFv3) (RFC 2740)
Similar to IPv4
  Same mechanisms, but a major rewrite of the internals of the protocol
Updated features for IPv6
  Every IPv4-specific semantic removed
  Carry IPv6 addresses
  Link-local addresses used as source
  IPv6 transport
  OSPF for IPv6 currently an IETF proposed standard
Notes: Cisco IOS does not support OSPF for IPv6 yet.

## Slide 5: Integrated Intermediate System-to-Intermediate System (IS-IS)
  Same as for IPv4
  Extensions for IPv6:
    Two new Type, Length, Value (TLV) attributes:
      IPv6 reachability (with 128-bit prefix)
      IPv6 interface address (with 128 bits)
    New protocol identifier
    Not yet an IETF standard
Notes: Cisco IOS does not support IS-IS for IPv6 yet.

## Slide 6: Multiprotocol Border Gateway Protocol (MP-BGP) (RFC 2858)
Multiprotocol extensions for BGP4:
  Enables protocols other than IPv4
  New identifier for the address family
IPv6 specific extensions:
  Scoped addresses: NEXT_HOP contains a global IPv6 address and potentially a link-local address (only when there is a link-local reachability with the peer).
  NEXT_HOP and Network Layer Reachability Information (NLRI) are expressed as IPv6 addresses and prefix in the multiprotocol attributes.

## Slide 7: OSPFv3—Hierarchical Structure
  Topology of an area is invisible from outside of the area:
    LSA flooding is bounded by area.
    SPF calculation is performed separately for each area.
  Backbones must be contiguous.
  All areas must have a connection to the backbone:
    Otherwise a virtual link must be used to connect to the backbone.

## Slide 8: OSPFv3—Similarities with OSPFv2
  OSPFv3 is OSPF for IPv6 (RFC 2740)
    Based on OSPFv2, with enhancements
    Distributes IPv6 prefixes
    Runs directly over IPv6
  OSPFv3 and OSPFv2 can be run concurrently, because each address family has a separate SPF (ships in the night).
  OSPFv3 uses the same basic packet types as OSPFv2:
    Hello
    Database description (DBD)
    Link state request (LSR)
    Link state update (LSU)
    Link state acknowledgment (ACK)
Notes: Although most of the algorithms of OSPFv2 are the same in OSPFv3, some changes have been made in OSPFv3, particularly to handle the increased address size in IPv6 and the fact that OSPF runs directly over IP. Because OSPFv2 is heavily dependent on the IPv4 address for its operation, changes were necessary in OSPFv3 protocol to support IPv6, as outlined in RFC 2740 OSPF for IPv6. Some of the notable changes include platform-independent implementation, protocol processing per-link rather than per-node processing, explicit support for multiple instances per link, and changes in authentication and packet format.
IPv6 OSPF is now an IETF proposed standard. Like RIPng, IPv6 OSPFv3 uses IPv6 for transport and uses link-local addresses as source address.
Runs directly over IPv6 : ATM aal5 mux, tunneling : configured tunnel
All of OSPF for IPv4's optional capabilities, including on-demand circuit support, NSSA areas, and the multicast extensions to OSPF (MOSPF) are also supported in OSPF for IPv6.

## Slide 9: OSPFv3—Similarities with OSPFv2
  Neighbor discovery and adjacency formation mechanism are identical.
  RFC-compliant NBMA and point-to-multipoint topology modes are supported. Also supports other modes from Cisco, such as point-to-point and broadcast, including the interface.
  LSA flooding and aging mechanisms are identical.
Notes: Although most of the algorithms of OSPFv2 are the same in OSPFv3, some changes have been made in OSPFv3, particularly to handle the increased address size in IPv6 and the fact that OSPF runs directly over IP. Because OSPFv2 is heavily dependent on the IPv4 address for its operation, changes were necessary in OSPFv3 protocol to support IPv6, as outlined in RFC 2740 OSPF for IPv6. Some of the notable changes include platform-independent implementation, protocol processing per-link rather than per-node processing, explicit support for multiple instances per link, and changes in authentication and packet format.
IPv6 OSPF is now an IETF proposed standard. Like RIPng, IPv6 OSPFv3 uses IPv6 for transport and uses link-local addresses as source address.
Runs directly over IPv6 : ATM aal5 mux, tunneling : configured tunnel
All of OSPF for IPv4's optional capabilities, including on-demand circuit support, NSSA areas, and the multicast extensions to OSPF (MOSPF) are also supported in OSPF for IPv6.

## Slide 10: Enhanced Routing Protocol Support Differences from OSPFv2
  OSPF packet type
    OSPFv3 has the same five packet types, but some fields have been changed.
  All OSPFv3 packets have a 16-byte header vs. the 24-byte header in OSPFv2.
Notes: OSPFv2 was primarily concerned with the subnet on which it was operating, whereas OSPFv3 is concerned with the links to which the router is connected.
OSPFv2 did not define or allow for multiple instance per link, although similar functionality could made by other mechanisms such as sub-interfaces. OSPFv3 has explicit support for instances through the instance field.
Authentication no more on OSPF - It's now the job of IPv6 to make sure the right level of authentication is in use.
stub
External networks, such as those redistributed from other protocols into OSPF, are not allowed to be flooded into a stub area. Routing from these areas to the outside world is based on a default route. Configuring a stub area reduces the topological database size inside an area and reduces the memory requirements of routers inside that area.
An area could be qualified a stub when there is a single exit point from that area or if routing to outside of the area does not have to take an optimal path.
An extension to stub areas is what is called "totally stubby areas". Cisco indicates this by adding a "no-summary" keyword to the stub area configuration. A totally stubby area is one that blocks external routes and summary routes (inter-area routes) from going into the area. This way, intra-area routes and the default of 0.0.0.0 are the only routes injected into that area.

## Slide 11: OSPFv3 Differences from OSPFv2
OSPFv3 protocol processing is per link, not per subnet
  IPv6 connects interfaces to links.
  Multiple IPv6 subnets can be assigned to a single link.
  Two nodes can talk directly over a single link, even though they do not share a common subnet.
  The terms “network” and “subnet” are being replaced with “link.”
  An OSPF interface now connects to a link instead of to a subnet.

## Slide 12: OSPFv3 Differences from OSPFv2 (Cont.)
Multiple OSPFv3 protocol instances can now run over a single link
  This structure allows separate autonomous systems, each running OSPF, to use a common link. A single link could belong to multiple areas.
  Instance ID is a new field that is used to allow multiple OSPFv3 protocol instances per link.
  In order to have two instances talk to each other, they need to have the same instance ID. By default, it is 0, and for any additional instance it is increased.

## Slide 13: OSPFv3 Differences from OSPFv2 (Cont.)
Multicast addresses:
  FF02::5—Represents all SPF routers on the link-local scope; equivalent to 224.0.0.5 in OSPFv2
  FF02::6—Represents all DR routers on the link-local scope; equivalent to 224.0.0.6 in OSPFv2
Removal of address semantics
  IPv6 addresses are no longer present in OSPF packet header (part of payload information).
  Router LSA and network LSA do not carry IPv6 addresses.
  Router ID, area ID, and link-state ID remain at 32 bits.
  DR and BDR are now identified by their router ID and not by their IP address.
Security
  OSPFv3 uses IPv6 AH and ESP extension headers instead of variety of the mechanisms defined in OSPFv2.
Notes: Router ID is a 4 byte field used to identify the router, originating OSPF packet.
Link ID depends on the type of link (pt-to-pt, broadcast)

## Slide 14: LSA Overview
 | LSA Function Code | LSA Type
Router LSA | 1 | 0x2001
Network LSA | 2 | 0x2002
Interarea prefix LSA | 3 | 0x2003
Interarea router LSA | 4 | 0x2004
AS external LSA | 5 | 0x2005
Group membership LSA | 6 | 0x2006
Type 7 LSA | 7 | 0x2007
Link-LSA | 8 | 0x2008
Intra-area prefix LSA | 9 | 0x2009
Notes: RFC's A4.2.1

## Slide 15: Larger Address Space Enables Address Aggregation
  Aggregation of prefixes announced in the global routing table
  Efficient and scalable routing
  Improved bandwidth and functionality for user traffic

## Slide 16: Configuring OSPFv3 in Cisco IOS Software
  Similar to OSPFv2
    Prefixes existing interface and EXEC mode commands with “ipv6”
  Interfaces configured directly
    Replaces network command
  “Native” IPv6 router mode
    Not a submode of router ospf command

## Slide 17: Enabling OSPFv3 Globally
ipv6 unicast-routing
!
ipv6 router ospf 1
router-id 2.2.2.2

## Slide 18: Enabling OSPFv3 on an Interface
interface Ethernet0/0
ipv6 address 3FFE:FFFF:1::1/64
ipv6 ospf 1 area 0
ipv6 ospf priority 20
ipv6 ospf cost 20

## Slide 19: Cisco IOS OSPFv3-Specific Attributes
  Configuring area range:
    area area-id range prefix/prefix length [advertise | not-advertise] [cost cost]
  Showing new LSAs:
    show ipv6 ospf [process-id] database link
    show ipv6 ospf [process-id] database prefix

## Slide 20: OSPFv3 Configuration Example
Router1#
interface S1/1
ipv6 address 2001:410:FFFF:1::1/64
ipv6 ospf 100 area 0
interface S2/0
ipv6 address 3FFE:B00:FFFF:1::2/64
ipv6 ospf 100 area 1
ipv6 router ospf 100
router-id 10.1.1.3
Router2#
interface S3/0
ipv6 address 3FFE:B00:FFFF:1::1/64
ipv6 ospf 100 area 1
ipv6 router ospf 100
router-id 10.1.1.4

## Slide 21: Verifying Cisco IOS OSPFv3
Router2#show ipv6 ospf int s 3/0
S3/0 is up, line protocol is up
Link Local Address 3FFE:B00:FFFF:1::1, Interface ID 7
Area 1, Process ID 100, Instance ID 0, Router ID 10.1.1.4
Network Type POINT_TO_POINT, Cost: 1
Transmit Delay is 1 sec, State POINT_TO_POINT,
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
Hello due in 00:00:02
Index 1/1/1, flood queue length 0
Next 0x0(0)/0x0(0)/0x0(0)
Last flood scan length is 3, maximum is 3
Last flood scan time is 0 msec, maximum is 0 msec
Neighbor Count is 1, Adjacent neighbor count is 1
Adjacent with neighbor 10.1.1.3
Suppress hello for 0 neighbor(s)

## Slide 22: show ipv6 ospf
R7#show ipv6 ospf
Routing Process “ospfv3 1” with ID 75.0.7.1
It is an area border and autonomous system boundary router
Redistributing External Routes from, connected
SPF schedule delay 5 secs, Hold time between two SPFs 10 secs
Minimum LSA interval 5 secs. Minimum LSA arrival 1 secs
LSA group pacing timer 240 secs
Interface floor pacing timer 33 msecs
Retransmission pacing timer 33 msecs
Number of external LSA 3. Checksum Sum 0x12B75

## Slide 23: show ipv6 ospf (Cont.)
  Number of areas in this router is 2. 1 normal 0 stub 1 nssa
  Area BACKBONE(0)
  Number of interfaces in this area is 1
  SPF algorithm executed 23 times
  Number of LSA 14. Checksum Sum 0x760AA
  Number of DCbitless LSA 0
  Number of Indication LSA 0
  Number of DoNotAge LSA 0
  Flood list length 0
  Area 2
  Number of interfaces in this area is 1
  It is a NSSA area
  Perform type-7/type-5 LSA translation
  SPF algorithm executed 17 times
  Number of LSA 25. Checksum Sum 0xE3BF0
  Number of DCbitless LSA 0
  Number of Indication LSA 0
  Number of DoNotAge LSA 0
  Flood list length 0

## Slide 24: show ipv6 ospf neighbor detail
Router2#show ipv6 ospf neighbor detail
Neighbor 10.1.1.3
In the area 0 via interface S2/0
Neighbor: interface-id 14, link-local address 3FFE:B00:FFFF:1::2
Neighbor priority is 1, State is FULL, 6 state changes
Options is 0x63AD1B0D
Dead timer due in 00:00:33
Neighbor is up for 00:48:56
Index 1/1/1, retransmission queue length 0, number of retransmission 1
First 0x0(0)/0x0(0)/0x0(0) Next 0x0(0)/0x0(0)/0x0(0)
Last retransmission scan length is 1, maximum is 1
Last retransmission scan time is 0 msec, maximum is 0 msec

## Slide 25: show ipv6 ospf database
Router Link States (Area 1)
ADV Router Age Seq# Fragment ID Link count Bits
26.50.0.1 1812 0x80000048 0 1 None
26.50.0.2 1901 0x80000006 0 1 B
Inter-Area Router Link States (Area 1)
Net Link States (Area 1)
Inter-Area Prefix Link States (Area 1)
ADV Router Age Seq# Link ID Rtr count
26.50.0.1 57 0x8000003B 3 4
ADV Router Age Seq# Prefix
26.50.0.2 139 0x80000003 3FFE:FFFF:26::/64
26.50.0.2 719 0x80000001 3FFE:FFF:26::/64
ADV Router Age Seq# Link ID Dest RtrID
26.50.0.2 772 0x80000001 1207959556 72.0.0.4
26.50.0.4 5 0x80000003 1258292993 75.0.7.1

## Slide 26: show ipv6 ospf database (Cont.)
Link (Type-8) Link States (Area 1)
ADV Router Age Seq# Link ID Interface
26.50.0.1 1412 0x80000031 3 Fa0/0
26.50.0.2 238 0x80000003 3 Fa0/0
Intra-Area Prefix Link States (Area 1)
Type-5 AS External Link States
ADV Router Age Seq# Link ID Ref-Istype Ref-LSID
26.50.0.1 1691 0x8000002E 0 0x2001 0
26.50.0.1 702 0x80000031 1003 0x2002 3
26.50.0.2 1797 0x80000002 0 0x2001 0
ADV Router Age Seq# Prefix
72.0.0.4 287 0x80000028 3FFE:FFFF:A::/64
72.0.0.4 38 0x80000027 3FFE:FFFF:78::/64
75.0.7.1 162 0x80000007 3FFE:FFFF:8::/64

## Slide 27: show ipv6 ospf database database-summary
R3#show ipv6 ospf database database-summary
Area 0 database summary
LSA Type Count Delete Maxage
Router 3 0 0
Network 0 0 0
Link 3 0 0
Prefix 3 0 0
Inter-area Prefix 6 0 0
Inter-area Router 0 0 0
Type-7 External 0 0 0
Subtotal 15 0 0
Process 1 database summary
LSA Type Count Delete Maxage
Router 7 0 0
Network 1 0 0
Link 7 0 0
Prefix 8 0 0
Inter-area Prefix 14 0 0
Inter-area Router 2 0 0
Type-7 External 0 0 0
Type-5 Ext 3 0 0
Total 42 0 0

## Slide 28: Summary
  RIP, EIGRP, IS-IS, BGP, and OSPF all have new versions to support IPv6.
  OSPFv3 is OSPF for IPv6.
  Most of the algorithms of OSPFv2 are the same in OSPFv3. Some changes have been made in OSPFv3, particularly to handle the increased address size in IPv6 the fact that OSPF runs directly over IP and all of the OSPF for IPv4 optional capabilities, including on-demand circuit support and NSSA areas. The multicast extensions to OSPF (MOSPF) are also supported in OSPF for IPv6.

## Slide 29: Summary (Cont.)
  There are two new LSAs in IPv6: LSA type 8 and LSA type 9. The router LSA and the network LSA do not carry IPv6 addresses.
  Configuring OSPFv3 requires a good background understanding of IPv6.
  There are Cisco IOS software configuration commands for OSPFv3 to support all of the new and old capabilities of OSPFv3.
  Numerous OSPFv3 IOS show commands support the verification of OSPFv3 configurations.