## Slide 1: Implementing IPv6
Using IPv6 with IPv4

## Slide 2: IPv4-to-IPv6 Transition
Transition richness means:
    No fixed day to convert; no need to convert all at once.
    Different transition mechanisms are available:
      Smooth integration of IPv4 and IPv6.
      Use of dual stack or 6to4 tunnels.
    Different compatibility mechanisms:
      IPv4 and IPv6 nodes can communicate.

## Slide 3: Cisco IOS Software Is IPV6-Ready: Cisco IOS Dual Stack
  If both IPv4 and IPv6 are configured on an interface, this interface is dual-stacked.

## Slide 4: Dual Stack
  Dual stack is an integration method where a node has implementation and connectivity to both an IPv4 and IPv6 network.

## Slide 5: Cisco IOS Software Is IPv6-Ready: Overlay Tunnels
  Tunneling encapsulates the IPv6 packet in the IPv4 packet.

## Slide 6: Tunneling
Tunneling is an integration method where an IPv6 packet is encapsulated within another protocol, such as IPv4. This method of encapsulation is IPv4 protocol 41:
  This method includes a 20-byte IPv4 header with no options and an IPv6 header and payload.
  This method is considered dual stacking.

## Slide 7: “Isolated” Dual-Stack Host
Encapsulation can be done by edge routers between hosts or between a host and a router.

## Slide 8: Cisco IOS Software Is IPv6-Ready: Configured Tunnel
Configured tunnels require:
  Dual-stack endpoints
  IPv4 and IPv6 addresses configured at each end

## Slide 9: Example: Cisco IOS Tunnel Configuration

## Slide 10: Cisco IOS Software Is IPv6-Ready: 6to4 Tunneling
6to4
  Is an automatic tunnel method
  Gives a prefix to the attached IPv6 network

## Slide 11: Translation—NAT-PT
NAT-Protocol Translation (NAT-PT) is a translation mechanism that sits between an IPv6 network and an IPv4 network.
The job of the translator is to translate IPv6 packets into IPv4 packets and vice versa.

## Slide 12: Summary
  The two most common techniques to make the transition from IPv4 to IPv6 are dual stack and IPv6-to-IPv4 (6-to-4) tunnels.
  Tunneling IPv6 traffic over an IPv4 network requires one edge router to encapsulate the IPv6 packet inside an IPv4 packet and another router to decapsulate it. Transition methods from IPv4 to IPv6 include dual-stack operation, protocol translation, and 6to4 tunnels.