## Slide 1: 计算机网络层协议与设备应用
第八章

## Slide 2: 内容回顾
交换机的工作原理
交换机的基本配置和维护

## Slide 3: 课程目标
理解网络层的各个协议
  IP子网的划分
  ARP/RARP、ICMP的概念，原理
路由器的基本操作
在路由器上配置静态路由和默认路由

## Slide 4: 网络层的功能
定义了基于某个协议的逻辑地址
选择数据通过网络的最佳路径
连接不同的媒介类型

## Slide 5: 封装数据的过程
Transport
Data Link
Physical
Network
Upper Layer Data
Upper Layer Data
TCP Header
Data
IP Header
Data
LLC Header
0101110101001000010
Data
MAC Header
Presentation
Application
Session
Segment
Packet
Bits
Frame
PDU
FCS
FCS
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: 解封装数据的过程
Upper Layer Data
LLC Hdr + IP + TCP + Upper Layer Data
MAC Header
IP + TCP + Upper Layer Data
LLC Header
TCP+ Upper Layer Data
IP Header
Upper Layer Data
TCP Header
0101110101001000010
Transport
Data Link
Physical
Network
Presentation
Application
Session
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: IP包头的格式
Version (4)
Destination IP Address (32)
Options (0 or 32 if any)
Data (varies if any)
1
Bit 0
Bit 15
Bit 16
Bit 31
Header Length (4)
Priority & Type of Service (8)
Total Length (16)
Identification (16)
Flags (3)
Fragment offset (13)
Time to live (8)
Protocol (8)
Header checksum (16)
Source IP Address (32)
20 Bytes
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: IP地址的作用
192.168.1.0
192.168.3.0
192.168.1.100
192.168.2.101
192.168.2.100
192.168.3.100
192.168.2.0
192.168.1.100
IP
Address
Host ID
Network ID

## Slide 9: IP地址的组成
点分十进制
最大值
10101100
二进制
十进制例子
二进制例子
255
255
255
255
Network
Host
128 64 32 16 8 4 2 1
11111111
11111111
11111111
11111111
00010000
01111010
11001100
172
16
122
1
8
9
16
17
24
25
32
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
32bits
202
255
10101100

## Slide 10: IP地址的分类
1
Class A:
Bits:
0NNNNNNN
Host
Host
Host
8
9
16
17
24
25
32
Range (1-126)
1
Class B:
Bits:
10NNNNNN
Network
Host
Host
8
9
16
17
24
25
32
Range (128-191)
1
Class C:
Bits:
110NNNNN
Network
Network
Host
8
9
16
17
24
25
32
Range (192-223)
1
Class D:
Bits:
1110MMMM
Multicast Group
Multicast Group
Multicast Group
8
9
16
17
24
25
32
Range (224-239)

## Slide 11: 子网掩码的使用
IP
Address
Host ID
Network ID
192.168.
2.200
Subnet
Mask
255.255.
0.0
192.168.
IP
Address
10.
50.100.200
Subnet
Mask
255.
0.0.0
Network
ID
10.
0.0.0
IP
Address
10.50.
100.200
Subnet
Mask
255.255.
0.0
Network
ID
10.50.
0.0
IP
Address
10.50.100.
200
Subnet
Mask
255.255.255.
0
Network
ID
10.50.100.
0

## Slide 12: 未划分子网的IP地址
Network 172.16.0.0
172.16.0.0
172.16.0.1
172.16.0.2
172.16.0.3
…...
172.16.255.253
172.16.255.254
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: 划分子网后的IP地址
Network 172.16.0.0
172.16.1.0
172.16.2.0
172.16.3.0
172.16.4.0
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: 变长子网掩码及子网规划
IP Host Address: 172.16.2.121
Subnet Mask: 255.255.255.0
Subnet Address = 172.16.2.0
Host Addresses = 172.16.2.1–172.16.2.254
Broadcast Address = 172.16.2.255
Eight bits of subnetting
Network
Subnet
Host
10101100
00010000
00000010
11111111
172.16.2.121:
255.255.255.0:
10101100
11111111
Subnet:
10101100
00010000
00010000
11111111
00000010
00000010
11111111
01111001
00000000
00000000
Broadcast:
Network
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: 子网规划
Other
subnets
192.168.5.16
192.168.5.32
192.168.5.48
20 subnets
5 hosts per subnet
Class C address:
192.168.5.0
应该用什么的子网掩码呢?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: ARP协议
IP地址解析为MAC地址
① 检查ARP缓存
B
C
A
ARP
Cache
2
1
4
6
5
ARP
Cache
3
② 发送ARP请求
③ 添加ARP缓存条目
④ 发送ARP回应
⑤ 添加ARP缓存条目
⑥ 发送IP数据包

## Slide 17: ARP协议的工作过程
172.16.3.1
172.16.3.2
IP: 172.16.3.2 = ???
I need the Ethernet address of 176.16.3.2.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: ARP协议的工作过程
172.16.3.1
172.16.3.2
IP: 172.16.3.2 = ???
I heard that broadcast. The message is for me. Here is my Ethernet address.
I need the Ethernet address of 176.16.3.2.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: ARP协议的工作过程
172.16.3.1
IP: 172.16.3.2
Ethernet: 0800.0020.1111
172.16.3.2
IP: 172.16.3.2 = ???
I heard that broadcast. The message is for me. Here is my Ethernet address.
I need the Ethernet address of 176.16.3.2.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: ARP协议的工作过程
Map IP Ethernet
Local ARP
172.16.3.1
IP: 172.16.3.2
Ethernet: 0800.0020.1111
172.16.3.2
IP: 172.16.3.2 = ???
I heard that broadcast. The message is for me. Here is my Ethernet address.
I need the Ethernet address of 176.16.3.2.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: RARP协议的工作过程
Ethernet: 0800.0020.1111 IP = ???
What is my IP address?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: RARP协议的工作过程
Ethernet: 0800.0020.1111 IP = ???
What is my IP address?
I heard that broadcast. Your IP address is 172.16.3.25.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: RARP协议的工作过程
Ethernet: 0800.0020.1111
IP: 172.16.3.25
Ethernet: 0800.0020.1111 IP = ???
What is my IP address?
I heard that broadcast. Your IP address is 172.16.3.25.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: RARP协议的工作过程
Map Ethernet IP
Ethernet: 0800.0020.1111
IP: 172.16.3.25
Ethernet: 0800.0020.1111 IP = ???
What is my IP address?
I heard that broadcast. Your IP address is 172.16.3.25.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: ICMP协议
ICMP消息通过IP数据报传送，被用来发送错误和控制信息。
ICMP定义了很多信息类型，例如：
  目的地不可达
  TTL 超时
  信息请求
  信息应答
  地址请求
  地址应答

## Slide 26: ICMP协议的应用
在一台计算机上向远程主机发起ping连接时，可能收到的ICMP信息有：
  连接建立成功
  目标主机不可达
  请求时间超时
  未知主机名

## Slide 27: 路由器工作原理
Routing Table
NET
INT
Metric
1
2
4
S0
S0
E0
1
0
0
1.0
4.0
1.3
E0
4.3
S0
2.2
E0
2.1
S0
4.1
4.2
1.1
1.2
Routing Table
NET
INT
Metric
1
2
4
E0
S0
S0
0
0
1
Router1
Router2

## Slide 28: 从主机1.1到4.2的数据传送过程
数据包从1.1出发传给缺省网关1.3
Router1从E0口接收到数据后，查看数据包的目的地址是4.2，并查找路由表是否有4.0网段的路由条目。
Router1在路由表中找到相应路由条目，并把数据包转到接口S0。
数据包从S0端口转发到Router2的S0端口
Router2从S0端口接收到数据后，查看数据包的目的地址是4.2，并查找路由表看是否有4.0网段的路由条目。
Router2在路由表中找到相应路由条目，并把数据包转到接口E0。
数据包从E0端口出发直接到达主机4.2

## Slide 29: 路由的基本概念
路由：跨越从源主机到目标主机的一个互联网络来转发数据包的过程。
路由器：是专门设计用于路由的设备，不能运行应用程序。如Cisco公司的1600、2500系列路由器，3COM公司的系列路由器
路由表：在路由器中维护的路由条目，路由器根据路由表做路径选择。
路由发现：路由器学习路由条目的过程。
路由选择：路由器根据路由表选择到达目标网络的最佳路径。
路由维护：路由器根据拓朴结构的变化对路由条目进行重配置。

## Slide 30: 静态路由
静态路由是由管理员手工配置的，是单向的。
RouterA(config)#ip route 192.168.1.0 255.255.255.0 192.168.2.1
192.168.2.1
SO
192.168.1.0
B
192.168.2.2
Network
A
B

## Slide 31: 默认路由
当路由器在路由表中找不到目标网络的路由条目时，路由器把请求转发到默认路由接口。
Stub Network-末节网络
RouterB(config)#ip route 0.0.0.0 0.0.0.0 192.168.2.2
192.168.2.1
SO
192.168.1.0
B
192.168.2.2
Network
A
B

## Slide 32: 动态路由
在路由器上运行路由协议，使路由器可以自动根据网络拓朴结构的变化调整路由条目。
在路由器之间利用路由协议进行路由交换。
无需管理员手工维护，减轻了管理员的工作负担。
在广域网上使用。

## Slide 33: 路由和交换对比
路由工作在网络层
路由是路由器根据自己的路由表进行的，其间经过了路由选择和路由转发的过程，从路由器的一个接口“路由”到的另外一个接口。
交换工作在数据链路层
交换是交换机根据自己的MAC地址表在交换机的不同端口之间进行的，从交换机的一个端口“交换”到另外一个端口。

## Slide 34: 路由器的硬件组成

## Slide 35: 路由器的启动过程
RAM
ROM
Bootstrap
装载引导代码
TFTP Server
Flash
ROM
Cisco
Internetwork
Operating
System
发现和装载IOS软件
Console
TFTP Server
NVRAM
Configuration
File
发现和应用配置文件
或进入Setup模式
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: 路由器启动时在控制台上的输出内容
  没有配置文件与有配置文件的路由器启动对比
--- System Configuration Dialog ---
Continue with configuration dialog? [yes/no]:yes
At any point you may enter a question mark '?' for help. Use ctrl-c to abort configuration dialog at any prompt. Default settings are in square brackets '[ ]'.
Setup模式
Router con0 is now available
Press RETURN to get started.
用户模式
Router>
控制台
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: Setup: 初始配置对话框
Router#setup
--- System Configuration Dialog ---
Continue with configuration dialog? [yes/no]: y
At any point you may enter a question mark '?' for help.
Use ctrl-c to abort configuration dialog at any prompt.
Default settings are in square brackets '[]'.
Basic management setup configures only enough connectivity
for management of the system, extended setup will ask you
to configure each interface on the system
Would you like to enter basic management setup? [yes/no]: n
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: 路由器的配置模式

## Slide 39: IOS使用技巧
Router#
clok
Translating "CLOK"
% Unknown command or computer name, or unable to find computer address
Router#
cl?
clear clock
Router#
clock
% Incomplete command.
Router#
clock ?
set Set the time and date
Router#
clock set
% Incomplete command.
Router#
<Ctrl-P>clock set ?
hh:mm:ss Current Time
符号翻译
命令提示
调回上一命令
Notes: <number>
<footer>
<header>
<date/time>

## Slide 40: IOS使用技巧
Router# clok
Translating "CLOK"
% Unknown command or computer name, or unable to find computer address
Router#
clear clock
Router#
% Incomplete command.
Router#
set Set the time and date
Router#
% Incomplete command.
Router#
hh:mm:ss Current Time
Router#
clock set 19:56:00
% Incomplete command.
Router#
clock set 19:56:00 ?
<1-31> Day of the month
MONTH Month of the year
Router#
clock set 19:56:00 04 8
^
% Invalid input detected at the '^' marker
Router#
clock set 19:56:00 04 August
% Incomplete command.
Router#
clock set 19:56:00 04 August ?
<1993-2035> Year
命令提示
语法检查
命令提示
Notes: <number>
<footer>
<header>
<date/time>
Slide 2 of 2

## Slide 41: Cisco 2600路由器的基本操作
从用户模式进入特权模式
Router>enable
Router#
从特权模式进入全局配置模式
Router#config terminal
Router(config)#
为路由器配置主机名
Router(config)#hostname teacher
teacher(config)#
进入路由器的以太口配置模式
teacher(config)#interface fastethernet 0/0
teacher(config_if)#

## Slide 42: Cisco 2600路由器的基本操作
配置路由器的banner信息
tercher(config)#banner motd $This is Aptech
company’s Router! Please don’t change the
configuration without permission! $
配置路由器接口的描述信息
teacher(config)#interface fastethernet 0/0
teacher(config_if)#description This is a fast ethernet
port used to connecting the company’s intranet!

## Slide 43: 为Cisco 2600路由器配置密码
配置控制台密码
teacher(config)#line console 0
teacher(config_line)#login
teacher(config_line)#password cisco
配置特权模式密码
配置安全的加密密码
teacher(config)#enable secret 1234
teacher(config)#enable password cisco
对所有密码进行加密
teacher(config)#service password-encryption

## Slide 44: 配置路由器的控制台会话
配置控制台会话时间
teacher(config)#line console 0
teacher(config_line)#exec-timeout 0 0
配置控制台输出日志同步
teacher(config)#line console 0
teacher(config_line)#logging synchronous

## Slide 45: 为Cisco 2600路由器配置串口
进入路由器的串口配置模式
teacher(config)#interface serial 0/0
teacher(config_if)#
查看路由器串口的物理状态
teacher#show controllers serial 0/0
HD unit 0,idb=0x122c04,driver structure at 0x127098
buffer size 1524 HD unit 0，V.35 DCE ，no clock
设置串口的时钟频率（仅在DCE端口）
teacher(config)#interface serial 0/0
teacher(config_if)#clock rate 64000
设置串口的带宽
teacher(config)#interface serial 0/0
teacher(config_if)#bandwidth 64

## Slide 46: 为Cisco 2600路由器配置串口
启用路由器的串口
teacher(config)#interface serial 0/0
teacher(config_if)#no shutdown
%LINK-3-UPDOWN: Interface Seria0/0, changed state to up
%LINEPROTO-5-UPDOWN: Line Protocol on Interface Serial0/0,
changed state to up
禁用路由器的串口
teacher(config)#interface serial 0/0
teacher(config_if)#shutdown
%LINK-3-UPDOWN: Interface Seria0/0, changed state to
administratively down
%LINEPROTO-5-UPDOWN: Line Protocol on Interface Serial0/0,
changed state to down

## Slide 47: 查看Cisco 2600路由器的串口状态
teacher(config)#show interface serial 0/0
serial 0/0 is up ，line protocol is up
可操作状态………serial 0/0 is up ，line protocol is up
连接问题…………serial 0/0 is up ，line protocol is down
接口问题…………serial 0/0 is down ，line protocol is down
禁用状态…………serial 0/0 is administratively down ，line protocol is down

## Slide 48: 为Cisco 2600路由器配置接口IP地址
配置路由器以太口IP地址
teacher(config)#interface fastethernet 0/0
teacher(config_if)#ip address 192.168.1.1 255.255.255.0
配置路由器串口IP地址
teacher(config)#interface serial 0/0
teacher(config_if)#ip address 192.168.2.1 255.255.255.0

## Slide 49: 查看路由器配置—show version
Router#show version
Cisco Internetwork Operating System Software
IOS (tm) 2600 Software (C2600-JS-L), Version 12.0(3), RELEASE SOFTWARE (fc1)
Copyright (c) 1986-1999 by cisco Systems, Inc.
Compiled Mon 08-Feb-99 18:18 by phanguye
Image text-base: 0x03050C84, data-base: 0x00001000
ROM: System Bootstrap, Version 11.0(10c), SOFTWARE
BOOTFLASH: 3000 Bootstrap Software (IGS-BOOT-R), Version 11.0(10c), RELEASE SOFTWARE(fc1)
wg_ro_a uptime is 20 minutes
System restarted by reload
System image file is "flash:c2600-js-l_120-3.bin"
(output omitted)
--More--
Configuration register is 0x2102

## Slide 50: 查看路由器配置—show running-config
Router#show running-config
Router#show running-config
Building configuration…
Current configuration:493bytes
!
!Last configuration change at 17:37:14 UTC Sat February
!
Version 12.1
Service timestamps debug uptime
Service timestamps log uptime
No service password-encryption
!
Hostname Router
!
!
!
--More--

## Slide 51: 查看路由器配置—show startup-config
删除路由器的配置
Router#erase startup-config
Router#show startup-config
Using 433 out of 29688 bytes
!
version 12.1
service timestamps debug uptime
service timestamps log uptime
no service password-encryption
!
hostname Router
!
memory-size iomem 10
ip subnet-zero
!
!
--More--

## Slide 52: 本章总结
网络层的基本功能
IP地址及子网规划
ARP及RARP协议的作用
ICMP协议作用
静态路由和默认路由的配置
动态路由
路由器的硬件组成
路由器的基本操作

## Slide 53: 实验目标
熟悉路由器的基本操作，能够根据指定的要求配置路由器。
在路由器上配置静态路由和默认路由，并对其进行检测。

## Slide 54: LAB1：路由器的基本操作

## Slide 55: 实验完成标准
按照实验拓朴结构图连接各设备
完成对路由器的各项配置，熟悉各命令的使用

## Slide 56: LAB2：静态路由和默认路由
Station A
IP:192.168.1.100/24
Gateway:192.168.1.1
Station B
IP:192.168.3.100/24
Gateway:192.168.3.1
RouterA
RouterB
Fa0/0:192.168.1.1/24
s0/0:192.168.2.1/24
Fa0/0:192.168.3.1/24
s0/0:192.168.2.2/24

## Slide 57: 实验完成标准
按照实验拓朴结构图连接各设备，并配置相关参数。
在路由器上配置静态路由，最终可以使stationA和stationB互相通讯。
在路由器上配置默认路由，最终可以使stationA和stationB互相通讯。
在路由器上利用show ip route命令查看路由条目