## Slide 1: HL-002 TCP-IP原理和子网规划
ISSUE 4.0
Notes: 此为封面页，需列出课程编码、课程名称和课程开发室名称。
要求：每个子课程（6位编码的课程）要求做一个这样的胶片，胶片文件命名为“课程编码 课程名称.ppt”。
此页胶片仅在授课时使用，胶片＋注释中不使用。
封面页按产品分为4个，各产品使用自己的封面，把其他封面直接删除即可。

## Slide 2: 学习目标
描述TCP/IP协议与OSI参考模型
描述TCP/IP协议栈各层次功能和原理
描述IP地址分类和应用
进行子网地址划分
学习完本课程，您应该能够：
Notes: 此页列出学习本课程需要达到的目标。
此页胶片仅在授课时使用，胶片＋注释中有单独的文字说明课程目标，不需要再使用该页胶片。

## Slide 3: 课程内容
第一章 TCP/IP协议
第二章 子网规划
Notes: 此页为了让学员和老师对课程安排有一个大致的了解。
此页列出本课程的主要培训标题，列出每章的名称即可。如果章下面的节不多，在此页可以一并列出。
此页胶片仅在授课时使用，胶片＋注释中有专门的目录和标题，不需要重复使用该页面。

## Slide 4: TCP/IP介绍
早期的协议族
全球范围
主机
Internet
TCP/IP
主机
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains the history of TCP/IP.
Emphasize: In the mid-1970s, DARPA established a packet-switched network to provide electronic communication between research institutions in the United States. DARPA and other government organizations understood the potential of packet-switched technology and were just beginning to face the problem virtually all companies with networks now have—how to establish communication between dissimilar computer systems.

## Slide 5: TCP/IP协议和OSI参考模型
TCP/IP协议栈具有简单的分层设计，与OSI参考模型有清晰的对应关系。
应用层
表示层
会话层
传输层
网络层
数据链路层
物理层
应 用 层
传输层
网络层
7
6
5
4
3
2
1
物理层
数据链路层
OSI参考模型
TCP/IP
Notes: 此页标题禁止有多级标题，更不要出现所在章节的名称。
此页标题要简练，能直接表达出本页的内容。
内容页可以除标题外的任何版式，如图、表等。
该页在授课和胶片＋注释中都要使用。

## Slide 6: TCP/IP协议栈
HTTP、Telnet、FTP、
TFTP、Ping、etc
TCP/UDP
ARP/RARP
IP
ICMP
Ethernet、802.3、PPP、
HDLC、FR、etc
接口和线缆
应用层
传输层
网络层
数据链路层
提供应用程序网络接口
建立端到端连接
寻址和路由选择
物理介质访问
二进制数据流传输
物理层

## Slide 7: TCP/IP协议数据封装
TELNET 23 | FTP 20/21 | SMTP 25 | TFTP 69
TCP/UDP 6/17 |  |  | 
IP PACKETS |  |  | 
FRAMES |  |  | 
BITS |  |  | 

## Slide 8: Data Flow
UDP
TCP
FTP
HTTP
IP
ICMP
IGMP
ARP
Ethernet
ATM
UDP
TCP
FTP
HTTP
IP
ICMP
IGMP
ARP
Ethernet
ATM
Data
Application
Data
FTP
HTTP
Transport
Data
UDP
TCP
FTP
HTTP
Internet
Data
UDP
TCP
IP
ICMP
IGMP
ARP
Preamble
Data
CRC
IP
ICMP
IGMP
ARP
Ethernet
ATM
Data
Ethernet
ATM
Data
Ethernet
ATM
Data
IP
ICMP
IGMP
ARP
Ethernet
ATM
Data
UDP
TCP
IP
ICMP
IGMP
ARP
Data
UDP
TCP
FTP
HTTP
Preamble
Internet
Transport
Application
Data
CRC
FTP
HTTP

## Slide 9: 应用层
文件传输
  FTP、TFTP
邮件服务
  SMTP、POP3
网络管理
  SNMP、Telnet、Ping、Tracert
网络服务
  HTTP、DNS、WINS

## Slide 10: 传输层协议概述
应用层
传输层
网络层
网络接入层
TCP
UDP

## Slide 11: TCP/UDP报文格式
0
8
16
24
31
16位源端口
16位目的端口
32位序列号
32位确认号
URG
ACK
PSH
RST
SYN
FIN
首部长度
保留(6位)
16位窗口大小
16位TCP校验和
16位紧急指针
选项
数据
0
8
16
24
31
16位源端口
16位目的端口
16位UDP校验和
数据
UDP报文格式
TCP报文格式
16位UDP长度

## Slide 12: 端口号
传输层协议用端口号来标识和区分各种上层应用程序。
HTTP
FTP
Telnet
SMTP
DNS
TFTP
SNMP
TCP
UDP
IP 数 据 包
套 接 字
80
20/21
23
25
53
69
161

## Slide 13: TCP 三次握手
发送 SYN
(seq=100 ctl=SYN)
接收 SYN
Host A
Host B
1
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 3:
Host A begins by sending a SYN segment indicating that host A will use sequence numbers starting with sequence number 100.
Emphasize: TCP is a simple protocol in terms of connection establishment. Some protocols have dozens of negotiation messages that are transmitted prior to session initialization.
TCP implements a strategy that is both necessary and sufficient.

## Slide 14: TCP 三次握手
发送 SYN
(seq=100 ctl=SYN)
接收 SYN
发送 SYN, ACK
(seq=300 ack=101 ctl=syn,ack)
Host A
Host B
接收 SYN
1
2
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 3:
Host B sends an ACK and acknowledges the SYN it received from host A. Host B also sends a SYN. Note that the acknowledgment field indicates host B is now expecting to hear sequence 101, acknowledging the SYN that occupied sequence 100.

## Slide 15: TCP 三次握手
发送 SYN
(seq=100 ctl=SYN)
接收 SYN
发送 SYN, ACK
(seq=300 ack=101 ctl=syn,ack)
建立会话
(seq=101 ack=301 ctl=ack)
Host A
Host B
1
2
3
接收 SYN
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 3:
In the next segment, host A sends some data. Note that the sequence number of the segment in step 3 is the same as as the ACK in step 2.
Emphasize: This sequence is like two people talking. The first person wants to talk to the second, so she says, “I would like to talk with you.” (SYN.) The second person responds, “Good. I want to talk with you.” (SYN, ACK.) The first person then says, “Fine—let us talk. Here is what I have to say.” (SYN, ACK, DATA.)
At this point either side can begin communicating and either side can break the connection. TCP is a peer-to-peer (balanced) communication method (no primary/secondary).
Note: This figure explains TCP connection establishment. For more information regarding the three-way handshake in establishing a TCP connection, refer to RFC 793.

## Slide 16: TCP连接
Internet
SYN(seq=a)
SYN(seq=b,ack=a+1)
SYN(seq=a+1,ack=b+1)
client
server

## Slide 17: TCP 简单确认
滑动窗口 = 1
发送方
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 7:
The window size is the number of messages transmitted before the sender must wait for an acknowledgment. Window size was presented earlier in the course, so this slide is a review.
The initial state, no messages being sent.

## Slide 18: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 7:
Data message 1 sent. (Send 1, Receive 1)

## Slide 19: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 7:
Acknowledgment message 2 sent. (Send ACK 2, Receive ACK 2)

## Slide 20: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
发送 2
接收 2
Notes: <number>
<footer>
<header>
<date/time>
Layer 4 of 7:
Data message 2 sent. (Send 2, Receive 2)

## Slide 21: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
发送 2
接收 2
接收 ACK 3
发送 ACK 3
Notes: <number>
<footer>
<header>
<date/time>
Layer 5 of 7:
ACK for message 2. (Send ACK 3, Receive ACK 3)

## Slide 22: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
发送 2
接收 2
接收 ACK 3
发送 ACK 3
发送 3
接收 3
Notes: <number>
<footer>
<header>
<date/time>
Layer 6 of 7:
Send 3, Receive 3.

## Slide 23: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
发送 2
接收 2
接收 ACK 3
发送 ACK 3
发送 3
接收 3
接收 ACK 4
发送 ACK 4
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 7:
ACK for message 3. (Send ACK 4, Receive ACK 4)
This sequence helps to convey the delay associated with a window size of one.
Note: TCP acknowledgments are expectational and are sometimes called forward referenced, which means that they refer to the segment they are expecting to receive, not the one just sent.
Acknowledgment field sizes can become an issue when transmitting data at FDDI and ATM speeds.

## Slide 24: 滑动窗口
需要修改窗口大小
发送数据太快了！
len 1024
win4096
len 1024
win4096
len 1024
win4096
ack 4097
win2048
len 1024
win4096
len 1024
win4096
ack 6145
win2048
len 1024
win4096
len 1024
win4096
len 1024
win4096

## Slide 25: TCP 窗 口
发送方
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 5:
This figure points out the benefit of a larger window size. Layer 1 is in the initial state, no messages being sent.

## Slide 26: TCP 窗 口
Window size = 3
Send 2
发送方
接收方
Window size = 3
Send 1
Window size = 3
Send 3
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 5:
Layer 2 illustrates how the sending device defines its window buffer as 3 and sends three bytes.

## Slide 27: TCP 窗 口
Window size = 3
Send 2
发送方
Window size = 3
Send 1
Window size = 3
Send 3
ACK 3
Window size = 2
数据 3 被丢弃
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 5:
In layer 3, the receiving device acknowledges the two first bytes, drops 3, and advertises its window size as 2.

## Slide 28: TCP 窗 口
Window size = 3
Send 2
发送方
Window size = 3
Send 1
Window size = 3
Send 3
ACK 3
Window size = 2
数据 3 被丢弃
Window size = 3
Send 4
Window size = 3
Send 3
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 4 of 5:
In layer 3 the sending device transmits 2 bytes but maintains a window size of 2.

## Slide 29: TCP 窗 口
Window size = 3
Send 2
发送方
Window size = 3
Send 1
Window size = 3
Send 3
ACK 3
Window size = 2
数据 3 被丢弃
Window size = 3
Send 4
Window size = 3
Send 3
ACK 5
Window size = 2
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 5 of 5:
In layer 5, the receiving device acknowledges the 2 bytes and still advertises its window size as 2.

## Slide 30: 网络层协议概述
网络接入层
应用层
传输层
网络层
IP
ARP
RARP
ICMP

## Slide 31: IP报文格式
版本
报文长度
服务类型
总 长 度
标 识 符
标志
片 偏 移
生存时间
协 议
报 头 校 验 和
源 IP 地 址
目 的 IP 地 址
IP 选 项

## Slide 32: ARP－地址解析协议
需要10.0.0.2的MAC地址？
IP:10.0.0.1/24
MAC:00-E0-FC-00-00-11
IP:10.0.0.2/24
MAC:00-E0-FC-00-00-12
ARP Request?
ARP Reply
10.0.0.2 对应的MAC：00-E0-FC-00-00-12

## Slide 33: RARP－反向地址解析协议
我的IP地址是什么？
无盘工作站
RARP Server
RARP Request?
RARP Reply
你的IP地址是10.0.0.1

## Slide 34: ICMP协议
B可达吗？
ICMP Echo Request
ICMP Echo Reply
我在。
A
B
Notes: 让发送者知道数据包传输过程中出现的问题

## Slide 35: 课程内容
第一章 TCP/IP协议
第二章 子网规划
Notes: 此页为了让学员和老师对课程安排有一个大致的了解。
此页列出本课程的主要培训标题，列出每章的名称即可。如果章下面的节不多，在此页可以一并列出。
此页胶片仅在授课时使用，胶片＋注释中有专门的目录和标题，不需要重复使用该页面。

## Slide 36: IP地址介绍
IP地址唯一标示一台网络设备
私有IP地址
10.110.192.111
20.130.188.144

## Slide 37: IP地址
逻辑地址，用于标识网络中的主机
32位二进制数
  点分4组,每组8位
  每8位一个字节（byte）
  169. 254. 0. 1
  10101001. 11111110. 00000000. 00000001

## Slide 38: Converting to Binary Format
8 Bits
Decimal Value 255
1
1
1
1
1
1
1
1
128
64
32
16
8
4
2
1
Binary Notation (Base 2)
27
26
25
24
23
22
21
20
Example
1
1
0
1
1
0
0
1
1*128
1*64
0*32
1*16
1*8
0*4
0*2
1*1
128
64
32
16
8
4
2
1
128
64
0
16
8
0
0
1
217

## Slide 39: 规定
Net ID 和Host ID
  二进制位不能全0 全1
  IP 10.0.0.1
  Net ID 10.0.0.0
  本地广播 10.255.255.255
  子网广播 255.255.255.255

## Slide 40: IP地址分类

## Slide 41: Class A
  0xxxxxxx . 00000000 . 00000000 . 00000000
  00000000 . 00000000 . 00000000
  01111110 .
  1 . 0 . 0 . 0 ~
  126 . 0 . 0 . 0
  网络号范围：
  00000001 . xxxxxxxx . xxxxxxxx . xxxxxxxx
  00000001 .
  00000001 .
  主机范围: 1 . 0 . 0 . 0
  1 . 0 . 0 . 1 ~
  1 . 255 . 255 . 254
00000001 .
  00000000 . 00000000 . 00000000
  00000000 . 00000000 . 00000001
  11111111 . 11111111 . 11111110

## Slide 42: Class B
  10xxxxxx . xxxxxxxx . 00000000 . 00000000
  . 00000000 . 00000000
  10111111 . 11111111
  128 . 0 . 0 . 0 ~
  191 . 255 . 0 . 0
  网络号范围：
  10000000 . 00000000 . xxxxxxxx . xxxxxxxx
  10000000 . 00000000 .
  10000000 . 00000000 .
  主机范围: 128 . 0 . 0 . 0
  128 . 0 . 0 . 1 ~
  128 . 0 . 255 . 254
10000000 . 00000000
  . 00000000 . 00000000
  00000000 . 00000001
  11111111 . 11111110

## Slide 43: Class C
  110xxxxx . xxxxxxxx . xxxxxxxx . 00000000
  . 00000000
  11011111 . 11111111 . 11111111
  192 . 0 . 0 . 0 ~
  223 . 255 . 255 . 0
  网络号范围：
  11000000 . 00000000 . 00000000 . xxxxxxxx
  11000000 . 00000000 . 00000000 .
  11000000 . 00000000 . 00000000 .
  主机范围: 192 . 0 . 0 . 0
  192 . 0 . 0 . 1 ~
  192 . 0 . 0 . 254
11000000 . 00000000 . 00000000
  . 00000000
  00000001
  11111110

## Slide 44: 计算可用的主机地址
11111111
172 16 0 0
10101100
00010000
00000000
00000000
16 15 14 13 12 11 10 9
8 7 6 5 4 3 2 1
网络
主机
00000000
00000001
11111111
11111111
11111111
11111110
...
...
00000000
00000011
11111101
1
2
3
65534
65535
65536
-
...
2
65534
N
2N-2 = 216-2 = 65534
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains how to calculate the number of available hosts in a network.
Emphasize: 2N-2 is the calculation to determine available hosts. N is the number of binary digits in the host field. Subtract 2 because a host cannot be all 0s or 1s.
The same principal applies when determining the number of available networks.

## Slide 45: IP
网络数 主机数
A类 27 - 2 224 – 2
B类 214 216 – 2
C类 221 28 – 2
D类 组播
E类 保留

## Slide 46: 特殊IP地址
网络部分
主机部分
地址类型
用 途
127
any
全“0”
全“1”
Any
全“0”
Any
全“1”
网络地址
代表一个网段
广播地址
特定网段的所有节点
环回地址
环回测试
广播地址
本网段所有节点
所有网络
华为Quidway路由器
用于指定默认路由

## Slide 47: 合法的主机IP?
0.0.0.0
1.1.1.1
12.0.1.0
12.0.1.255
127.0.0.4
131.107.0.255
222.0.0.255
225.0.0.1

## Slide 48: 无子网编址
无子网编址是指使用自然掩码，不对网段进行细分。比如B类网段172.16.0.0，采用255.255.0.0作为掩码。

## Slide 49: 带子网编址
B类网段172.16.0.0
172.16.8.1 ，255.255.255.0
172.16.4.1，255.255.255.0

## Slide 50: 子网掩码的作用
区分Network ID和Host ID
确定目标主机所在的网络
“与”运算
Default Subnet Mask
  Class A -- 255.0.0.0
  Class B -- 255.255.0.0
  Class C -- 255.255.255.0

## Slide 51: 确定目标网络的过程
TCP/IP初始化时
  本机IP “与”本机子网掩码=本网络号
发送数据时
  目标IP “与”本机子网掩码=目标网络号
目标网络号和本网络号比较
  相同,说明在本网络
  不相同,数据包发往 Gateway

## Slide 52: 子网划分
Subnetting IP子网 (Subnet)
  不同访问技术的网络处于不同子网
  减少网络
    拥塞
    广播
从Host ID高位起划分子网
借位连续
最少要借2个二进制位
子网ID不能全为0
子网ID不能全为1
Notes:     ?? 子网划分灵活,可以超过每个子网的最大主机数

## Slide 53: Subnet ID
  .xxxxxxxx.xxxxxxxx
  .00
  .01
  .10
  .11
  000000.00000000
  000000.00000000
  131.107.64.0
  131.107.128.0
  11111111.11111111.11000000.00000000
  10000011.01101011.
131.107
  Subnet Mask:
  255.255.192.0

## Slide 54: Subnet ID
  10000011.01101011.01000000.00000000
000000.00000001
111111.11111110
10000011.01101011.01
10000011.01101011.01
主机范围：
131.107.64.1
~ 131.107.127.254
子网1: 131.107.64.0
IP：
  11111111.11111111. 11000000.00000000
Mask：
255.255.192.0

## Slide 55: Subnet ID
  10000011.01101011.10000000.00000000
000000.00000001
111111.11111110
10000011.01101011.10
10000011.01101011.10
主机范围：
131.107.128.1
~ 131.107.191.254
子网2: 131.107.128.0
IP：
  11111111.11111111. 11000000.00000000
Mask：
255.255.192.0

## Slide 56: 子网规划
201.222.5.0
255.255.255.0
201.222.5.8
255.255.255.248
201.222.5.16
255.255.255.248
201.222.5.24
255.255.255.248
201.222.5.32
255.255.255.248
201.222.5.9
255.255.255.248
201.222.5.17
255.255.255.248
201.222.5.25
255.255.255.248
201.222.5.33
255.255.255.248

## Slide 57: B类子网规划实例
子网地址 | 172.16.2.0
主机地址 | 172.16.2.1－172.16.2.254
广播地址 | 172.16.2.255
IP主机地址 | 172.16.2.120
子网掩码 | 255.255.255.0

## Slide 58: C类子网规划实例
子网地址 | 192.168.5.120
主机地址 | 192.168.5.121-192.168.5.126
广播地址 | 192.168.5.127
IP主机地址 | 192.168.5.121
子网掩码 | 255.255.255.248

## Slide 59: 变长子网掩码（VLSM）
192.168.1.32/27
192.168.1.64/27
192.168.1.96/27
192.168.1.128/27
192.168.1.160/30
192.168.1.164/30
192.168.1.168/30
192.168.1.172/30
ISP
通告
192.168.1.0

## Slide 60: 无类域间路由（CIDR）
CIDR减少了路由表的规模，增了网络的可扩展性。
Internet
198.168.1.0
198.168.2.0
198.168.3.0
ISP
通告路由
198.168.0.0/16
Notes: Classless Inter-Domain Routing (CIDR)
  不再遵从A,B,C类地址的缺省子网掩码
10.0.0.0/16

## Slide 61: 地址耗尽问题
IPV4
IP地址耗尽
路由表的增长
Subneting 子网划分
VLSM 变长子网掩码
CIDR 无类别域间路由
Private IP 私有IP
IPV6 最终方案

## Slide 62: 本章总结
TCP/IP协议栈与OSI参考模型比较
TCP/IP协议栈各层主要协议介绍
IP子网规划原理
IP子网规划实例
Notes: 对于比较大的章，内容比较多，最好能在一章讲解完后对本章的课程内容、要达到的能力和注意事项等进行概要总结。
本页在胶片＋注释中同样要使用。

## Slide 63
华为3Com技术有限公司
华为3Com公司网址: www.huawei-3com.com
华为3Com技术论坛网址: forum.huawei-3com.com