## Slide 1: 华为认证教育
中国IT认证实验室
Notes: ChinaITLab.com是国内著名的IT教育门户网站，创建于2001年初，由深圳拓普思信息科技有限公司投资运营。 ChinaITLab自2001年成立以来，在互联网寒潮中以“寒冬腊梅傲雪开”的乐观精神和务实态度迎来了全新的发展春天。经历过3年的风雨洗礼，ChinaITlab更加生机勃勃，值得欣慰的是，ChinaITLab不负众望，现今已发展成为中国最大的IT教育门户网站。ChinaITLab日访问量高达270万人次，成为行业的中流砥柱，为全球华人提供优秀的学习资源和丰富的培训资讯，为IT培训机构和IT人才打造一个从IT培训品牌推广、培训战略咨询、IT职业发展规划到学习解决方案提供和实施的完整服务链。 媒体优势： ChinaITLab是国内唯一专业IT教育门户网站，日访问量已超270万人次以上，拥有最准确的客户群体，用户均是计算机软硬件的IT从业人员、公司部门的负责人，并具有高技能、高素质、高消费的特点，非常适合各类厂商公司、培训中心宣传产品形象，发布产品、培训信息。 网站坚持“争分夺秒报道IT技术、IT教育资讯”的媒体导向，成功策划众多的IT技术和认证专题，受到广大网友的好评，被誉为“IT认证指南针”。 通过ChinaITLab，学生可以了解到全国500多家知名IT培训机构的详细资料，以及近10000门的流行课程。客观的评测数据，公正的教学导向，让学生掌握就业市场的需求，准确定位，有的放矢的选择教育培训。 网校优势： ChinaITLab针对IT培训市场，根据企业和个人需求，开发各种热门在线培训课程，包括国际IT认证课程和企业培训课程，涵盖网络，通讯，数据库，安全，程序等中高端领域， 为企业员工和个人用户提供整体的学习解决方案。 ChinaITLab始终坚持“教育就是人性化的互动服务”宗旨，在国内远程教育尚未成熟的情况下，勇于创新，首家采用“课程直播系统”和“网络呼叫学习模式”，以引领式E-learnling学习模式为核心，为学员提供量身定做的“导师制”教学服务，开创E-learning培训新模式，受到客户及同行的推崇。
ChinaITLab理念：提升客户价值，把握时代潮流，追求不断创新，拥有开放的心态，永不轻言放弃！

## Slide 2: TCP/IP介绍
早期的协议族
全球范围
主机
Internet
TCP/IP
主机
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains the history of TCP/IP.
Emphasize: In the mid-1970s, DARPA established a packet-switched network to provide electronic communication between research institutions in the United States. DARPA and other government organizations understood the potential of packet-switched technology and were just beginning to face the problem virtually all companies with networks now have—how to establish communication between dissimilar computer systems.

## Slide 3: TCP/IP 协议族
7
6
5
4
3
2
5
4
3
2
应用层
表达层
会话层
传输层
网络层
数据链路层
物理层
1
应用层
传输层
Internet层
数据链路层
物理层
1
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure shows the protocol layers and compares them with the layers of the OSI reference model.
Emphasize: This figure shows the TCP/IP conceptual layer titles. The protocol stack is used several times in this chapter, and the lower two layers may be sometimes called the network interface layer.
The terms “packet” and “datagram” are nearly interchangeable. However, a datagram is a unit of data, while a packet is a physical entity that appears on a network. In most cases, a packet contains a datagram. In some protocols, though, a datagram is divided into a number of packets to accommodate a requirement for smaller transmittable pieces.
Note: Creation and documentation of the Internet protocols closely resembles an academic research project. The protocols are specified in documents called RFCs. RFCs are published, reviewed, and analyzed by the Internet community.

## Slide 4: 应用层概述
* 路由器使用
应用层
传输层
Internet层
数据链路层
物理层
文件传输
- TFTP *
- FTP *
- NFS
E-Mail
- SMTP
远程登陆
- Telnet *
- rlogin *
网络管理
- SNMP *
名称管理
- DNS*
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure discusses application-layer protocols.
Emphasize: The common network applications today include file transfer, remote login, network management, and e-mail.
We focus on TCP/IP in this course for several reasons:
  TCP/IP is a universally available protocol and you will use it at work.
  TCP/IP is a useful reference for understanding other protocols, because it includes elements that are representative of other protocols.
  TCP/IP is important because the router uses it as a configuration tool. The router uses Telnet for remote configuration, TFTP to transfer configuration files and operating system images, and SNMP for network management.
Transition: The next section moves down the model to discuss the transport layer.

## Slide 5: 传输层概述
Transmission Control
Protocol (TCP)
User Datagram
Protocol (UDP)
应用层
传输层
Internet层
数据链路层
物理层
面向连接
非面向连接
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure introduces the protocols used at the transport layer.
Emphasize: TCP is one protocol within the protocol suite of TCP/IP. TCP is an acknowledged transport-layer protocol. However, TCP has a large header so there is much overhead.
UDP is unacknowledged. By eliminating all of the acknowledgement mechanisms, UDP is fast and efficient. UDP does not divide application data into pieces. Reliability is assumed to be handled by the upper-layer protocols, by a reliable lower-layer protocol, or by an error-tolerant application. UDP does have a smaller header and less overhead.

## Slide 6: TCP 数据格式
Source port (16)
Destination port (16)
Sequence number (32)
Header length (4)
Acknowledgement number (32)
Reserved (6)
Code bits (6)
Window (16)
Checksum (16)
Urgent (16)
Options (0 or 32 if any)
Data (varies)
20 Bytes
Bit 0
Bit 15
Bit 16
Bit 31
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains what is contained in a TCP segment.
Emphasize:
Source Port and Destination Port are the connections to the upper-layer protocol.
Sequence and Acknowledgment numbers are the position in the user’s byte stream of this segment. Sequence numbers are used for establishing reliability.
HLEN is the header length. It tells us where the data begins.
Six bits are reserved for future use.
Code Bits distinguish session management messages from data.
Window is a term we will come back to in a few slides. For now, consider it the size of the receivers buffers.
Checksum is a cyclic redundancy check (CRC). It verifies that the datagram arrived intact.
Urgent Pointer is used to signify out-of-band data.
Options are used by vendors to enhance their protocol offering.
The data portion of the frame contains the upper-layer protocol data.

## Slide 7: 端口号
TCP
端口号
F T P
传输层
T E L N E T
D N S
S N M P
T F T P
S M T P
UDP
应用层
21
23
25
53
69
161
R I P
520
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains how TCP uses port numbers to connect applications.
Emphasize: These port numbers were standardized in RFC 1340. This RFC has been obsoleted by RFC 1700. However, many of the port numbers outlined in RFC 1340 are still being used as standards.
It is possible to filter on TCP port numbers.
The TCP port number, combined with other information, is what UNIX C language developers call a socket. However, work sockets have different meanings in XNS and Novell, where they are service access point abstractions or programming interfaces rather than service access point identifiers.

## Slide 8: TCP 端口号
源端口
目标端口
…
Host A
1028
23
…
SP
DP
Host Z
Telnet Z
目标端口 = 23.
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure continues to explain how TCP uses port numbers.
Emphasize: In most cases the TCP port number on one side of a conversation is the same on the other side. For example, when a file transfer takes place, the software on one host is communicating with a peer application on another host.
In this example we see a Telnet (TCP port 23) session. It is possible to have multiple Telnet sessions running simultaneously on a host or router. Telnet selects an unused port number above 1023 to represent the source port for each independent session. Notice that the destination port is still 23.
Port numbering is important to understand in order to configure IP extended access lists. The lack of symmetry in port number use is a critical factor in establishing effective security.

## Slide 9: TCP 三次握手
发送 SYN
(seq=100 ctl=SYN)
接收 SYN
Host A
Host B
1
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 3:
Host A begins by sending a SYN segment indicating that host A will use sequence numbers starting with sequence number 100.
Emphasize: TCP is a simple protocol in terms of connection establishment. Some protocols have dozens of negotiation messages that are transmitted prior to session initialization.
TCP implements a strategy that is both necessary and sufficient.

## Slide 10: TCP 三次握手
发送 SYN
(seq=100 ctl=SYN)
接收 SYN
发送 SYN, ACK
(seq=300 ack=101 ctl=syn,ack)
Host A
Host B
接收 SYN
1
2
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 3:
Host B sends an ACK and acknowledges the SYN it received from host A. Host B also sends a SYN. Note that the acknowledgment field indicates host B is now expecting to hear sequence 101, acknowledging the SYN that occupied sequence 100.

## Slide 11: TCP 三次握手
发送 SYN
(seq=100 ctl=SYN)
接收 SYN
发送 SYN, ACK
(seq=300 ack=101 ctl=syn,ack)
建立会话
(seq=101 ack=301 ctl=ack)
Host A
Host B
1
2
3
接收 SYN
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 3:
In the next segment, host A sends some data. Note that the sequence number of the segment in step 3 is the same as as the ACK in step 2.
Emphasize: This sequence is like two people talking. The first person wants to talk to the second, so she says, “I would like to talk with you.” (SYN.) The second person responds, “Good. I want to talk with you.” (SYN, ACK.) The first person then says, “Fine—let us talk. Here is what I have to say.” (SYN, ACK, DATA.)
At this point either side can begin communicating and either side can break the connection. TCP is a peer-to-peer (balanced) communication method (no primary/secondary).
Note: This figure explains TCP connection establishment. For more information regarding the three-way handshake in establishing a TCP connection, refer to RFC 793.

## Slide 12: TCP 简单确认
滑动窗口 = 1
发送方
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 7:
The window size is the number of messages transmitted before the sender must wait for an acknowledgment. Window size was presented earlier in the course, so this slide is a review.
The initial state, no messages being sent.

## Slide 13: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 7:
Data message 1 sent. (Send 1, Receive 1)

## Slide 14: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 7:
Acknowledgment message 2 sent. (Send ACK 2, Receive ACK 2)

## Slide 15: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
发送 2
接收 2
Notes: <number>
<footer>
<header>
<date/time>
Layer 4 of 7:
Data message 2 sent. (Send 2, Receive 2)

## Slide 16: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
发送 2
接收 2
接收 ACK 3
发送 ACK 3
Notes: <number>
<footer>
<header>
<date/time>
Layer 5 of 7:
ACK for message 2. (Send ACK 3, Receive ACK 3)

## Slide 17: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
发送 2
接收 2
接收 ACK 3
发送 ACK 3
发送 3
接收 3
Notes: <number>
<footer>
<header>
<date/time>
Layer 6 of 7:
Send 3, Receive 3.

## Slide 18: TCP 简单确认
滑动窗口 = 1
发送方
接收方
发送 1
接收 1
接收 ACK 2
发送 ACK 2
发送 2
接收 2
接收 ACK 3
发送 ACK 3
发送 3
接收 3
接收 ACK 4
发送 ACK 4
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 7:
ACK for message 3. (Send ACK 4, Receive ACK 4)
This sequence helps to convey the delay associated with a window size of one.
Note: TCP acknowledgments are expectational and are sometimes called forward referenced, which means that they refer to the segment they are expecting to receive, not the one just sent.
Acknowledgment field sizes can become an issue when transmitting data at FDDI and ATM speeds.

## Slide 19: TCP 顺序号和确认号
源端口
目标端口
…
顺序号
#
确认号
#
Source
Dest.
Seq.
Ack.
1028
23
10
1
我发送 #10.
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 4:
Layer 1 shows the Sequence number is 10.

## Slide 20: TCP 顺序号和确认号
我已收到 #10,
现在我需要 #11.
源端口
目标端口
…
顺序号
#
确认号
#
1028
23
Source
Dest.
10
Seq.
1
Ack.
1028
23
Source
Dest.
11
Seq.
1
Ack.
我发送 #10.
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 4:
Layer 2 shows the acknowledgment number is 11.

## Slide 21: TCP 顺序号和确认号
源端口
目标端口
…
顺序号
#
确认号
#
1028
23
Source
Dest.
11
Seq.
2
Ack.
1028
23
Source
Dest.
10
Seq.
1
Ack.
1028
23
Source
Dest.
11
Seq.
1
Ack.
我已收到 #10,
现在我需要 #11.
我发送 #10.
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 4:
Layer 3 shows the next sequence number is 11.

## Slide 22: TCP 顺序号和确认号
源端口
目标端口
…
顺序号
#
确认号
#
1028
23
Source
Dest.
11
Seq.
2
Ack.
1028
23
Source
Dest.
10
Seq.
1
Ack.
1028
23
Source
Dest.
11
Seq.
1
Ack.
1028
23
Source
Dest.
12
Seq.
2
Ack.
我已收到 #11,
现在我需要 #12.
我发送 #11
Notes: <number>
<footer>
<header>
<date/time>
Layer 4 of 4:
Layer 4 shows the acknowledgment number is 12.
Emphasize: The Sequence and Acknowledgment numbers are directional. The slide highlights the communication going in one direction. The sequence and acknowledgments take place with the sender on the right. TCP provides full-duplex communication.

## Slide 23: TCP 窗 口
发送方
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 5:
This figure points out the benefit of a larger window size. Layer 1 is in the initial state, no messages being sent.

## Slide 24: TCP 窗 口
Window size = 3
Send 2
发送方
接收方
Window size = 3
Send 1
Window size = 3
Send 3
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 5:
Layer 2 illustrates how the sending device defines its window buffer as 3 and sends three bytes.

## Slide 25: TCP 窗 口
Window size = 3
Send 2
发送方
Window size = 3
Send 1
Window size = 3
Send 3
ACK 3
Window size = 2
数据 3 被丢弃
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 5:
In layer 3, the receiving device acknowledges the two first bytes, drops 3, and advertises its window size as 2.

## Slide 26: TCP 窗 口
Window size = 3
Send 2
发送方
Window size = 3
Send 1
Window size = 3
Send 3
ACK 3
Window size = 2
数据 3 被丢弃
Window size = 3
Send 4
Window size = 3
Send 3
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 4 of 5:
In layer 3 the sending device transmits 2 bytes but maintains a window size of 2.

## Slide 27: TCP 窗 口
Window size = 3
Send 2
发送方
Window size = 3
Send 1
Window size = 3
Send 3
ACK 3
Window size = 2
数据 3 被丢弃
Window size = 3
Send 4
Window size = 3
Send 3
ACK 5
Window size = 2
接收方
Notes: <number>
<footer>
<header>
<date/time>
Layer 5 of 5:
In layer 5, the receiving device acknowledges the 2 bytes and still advertises its window size as 2.

## Slide 28: UDP 数据格式
没有顺序号和确认号
Source port (16)
Destination port (16)
Length (16)
Data (if any)
1
Bit 0
Bit 15
Bit 16
Bit 31
Checksum (16)
8 Bytes
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This graphic explains the format of UDP.
Emphasize: UDP is simple and efficient but not reliable. The UDP segment format includes a source port, a destination port, a length field, and an optional checksum field. It has no sequencing, acknowledgments, or windowing.
Example: TFTP uses a checksum. At the end of the transfer if the checksum does not match then the file did not make it. The user is notified and must type in the command again. As a result, the user has become the reliability mechanism.
Transition: The next section discusses the network layer of the OSI model and how it corresponds to the TCP/IP internet layer.

## Slide 29: Internet 层概述
OSI 网络层对应的是TCP/IP的internet层
Internet Protocol (IP)
Internet Control Message
Protocol (ICMP)
Address Resolution
Protocol (ARP)
Reverse Address
Resolution Protocol (RARP)
应用层
传输层
Internet层
数据链路层
物理层
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure presents a list of the protocols operating at the Internet layer.
Emphasize: Review the protocols briefly. They are covered in detail on the coming pages.
Routing protocols are usually considered layer-management protocols that support the network layer.

## Slide 30: IP 数据
Version (4)
Destination IP Address (32)
Options (0 or 32 if any)
Data (varies if any)
1
Bit 0
Bit 15
Bit 16
Bit 31
Header Length (4)
Priority & Type of Service (8)
Total Length (16)
Identification (16)
Flags (3)
Fragment offset (13)
Time to live (8)
Protocol (8)
Header checksum (16)
Source IP Address (32)
20 Bytes
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains what is contained in an IP datagram.
Emphasize: Discuss the format of the IP datagram.
The current generation of IP is version 4. We need the Header Length (HLEN) and the Total Length in this example because the IP Options field allows a variable length.
Time-To-Live (TTL) is a countdown field. Every station must decrement this number by one or by the number of seconds it holds onto the packet. When the counter reaches zero, the time to live expires and the packet is dropped. TTL keeps packets from endlessly wandering the internet in search of nonexistent destinations.
The next generation of IP (called IPng) is IP version 6. It is covered in RFC 1752.
Good references for this topic are Douglas Comer’s books on TCP/IP.

## Slide 31: 协议域
决定上层协议
Transport Layer
Internet Layer
TCP
UDP
Protocol Numbers
IP
17
6
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains the use of the protocol field.
Emphasize: Protocol numbers connect, or multiplex, IP to the transport layer. These numbers are standardized in RFC 1700. Cisco uses these numbers in filtering with extended access lists.

## Slide 32: ICMP协议
Application
Transport
Internet
Data Link
Physical
Destination Unreachable
Echo (Ping)
Other
ICMP
1
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains which messages are ICMP messages.
Emphasize: Describe ICMP messages and ping.

## Slide 33: ARP协议
172.16.3.1
172.16.3.2
IP: 172.16.3.2 = ???
我需要知道176.16.3.2的物理地址.
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 4:
Purpose: This figure shows how ARP is used to determine an IP address.
In layer 1, host 172.16.3.1 needs the MAC address of host 172.16.3.2. It sends an ARP request message.

## Slide 34: ARP协议
172.16.3.1
172.16.3.2
IP: 172.16.3.2 = ???
我知道你的请求，这是我的物理地址
我需要知道176.16.3.2的物理地址.
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 4:
In layer 2, host 172.16.3.2 is on the same wire and receives the ARP request message.

## Slide 35: ARP协议
172.16.3.1
IP: 172.16.3.2
Ethernet: 0800.0020.1111
172.16.3.2
IP: 172.16.3.2 = ???
我知道你的请求，这是我的物理地址
我需要知道176.16.3.2的物理地址.
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 4:
In layer 3, host 172.16.3.2 sends an ARP reply with its MAC address to host 172.16.3.1.

## Slide 36: ARP协议
映射 IP Ethernet
Local ARP
172.16.3.1
IP: 172.16.3.2
Ethernet: 0800.0020.1111
172.16.3.2
IP: 172.16.3.2 = ???
我知道你的请求，这是我的物理地址
我需要知道176.16.3.2的物理地址.
Notes: <number>
<footer>
<header>
<date/time>
Layer 4 of 4:
In layer 4, the bulleted items at the bottom of the slide appear.
Emphasize: ARP provides translation between network and data link layers.
Discuss why it is necessary to have a mechanism like ARP.
Describe ARP operation.
Not all protocols use ARP. Some use other methods for address translation.
Note: For the message to be transmitted uniquely to a single interface on the multiaccess link, it is necessary to build a frame with the unique MAC address of the interface

## Slide 37: RARP协议
Ethernet: 0800.0020.1111 IP = ???
我的地址是多少？
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 4:
Purpose: This figure explains how RARP works.
In layer 1, the host on the left needs its IP address. It sends a RARP request with its MAC address.

## Slide 38: RARP协议
Ethernet: 0800.0020.1111 IP = ???
我的地址是多少？
我听到了广播你的地址是 172.16.3.25.
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 4:
In layer 2, the host on the right, functioning as a RARP server, maps the MAC address to an IP address.

## Slide 39: RARP协议
Ethernet: 0800.0020.1111
IP: 172.16.3.25
Ethernet: 0800.0020.1111 IP = ???
我的地址是多少？
我听到了广播你的地址是 172.16.3.25.
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 4:
In layer 3, the host on the right sends the IP address to the requester in a RARP reply message.

## Slide 40: RARP协议
映射 Ethernet IP
Ethernet: 0800.0020.1111
IP: 172.16.3.25
Ethernet: 0800.0020.1111 IP = ???
我的地址是多少？
我听到了广播你的地址是 172.16.3.25.
Notes: <number>
<footer>
<header>
<date/time>
Layer 4 of 4:
In layer 4, the bulleted items appear at the bottom of the slide.
Emphasize: RARP is used to boot diskless workstations over a network.

## Slide 41: TCP/IP地址介绍
  断点连接需要确定的地址
  路径选择
Location is represented by an address
172.18.0.2
172.18.0.1
172.17.0.2
172.17.0.1
172.16.0.2
172.16.0.1
SA
DA
HDR
DATA
10.13.0.0
192.168.1.0
10.13.0.1
192.168.1.1
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This is an introduction slide to the IP addressing section.
Emphasize: Stations with internetwork access must have unique addresses.

## Slide 42: IP 地 址
255
255
255
255
Dotted Decimal
Maximum
Network
Host
32 bits
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 3:
Purpose: This figure show the general format of an IP address.
In layer 1, the address is 32 bits with a network and host portion.

## Slide 43: IP 地 址
255
255
255
255
Dotted Decimal
Maximum
Network
Host
128 64 32 16 8 4 2 1
11111111
11111111
11111111
11111111
Binary
32 bits
1
8
9
16
17
24
25
32
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 3:
In layer 2, one can convert the address to binary.

## Slide 44: IP 地 址
255
255
255
255
Dotted Decimal
Maximum
Network
Host
128 64 32 16 8 4 2 1
11111111
11111111
11111111
11111111
10101100
00010000
01111010
11001100
Binary
32 bits
172
16
122
204
Example Decimal
Example Binary
1
8
9
16
17
24
25
32
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
128 64 32 16 8 4 2 1
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 3:
In layer 3, an example of dotted-decimal format and binary are displayed.
Emphasize: IP address format is dotted-decimal. Dotted-decimal makes it easy to work with IP addresses. However, in this course we will work with the addresses on the bit level, so we will convert these addresses into binary, make changes to them, and convert them back.
The central authority for addresses is the Internet Assigned Numbers Authority.
Note: This most common form of addressing reflects the widely used IP version 4. Faced with the problem of depleting available addresses, Internet Engineering Task Force (IETF) work is under way for a backward-compatible next generation of IP (IPng, also called IP 6).
IP 6 will offer expanded routing and addressing capabilities with 128-bit addresses rather than the 32-bit addressing shown on the graphic. Addresses from both IP versions will coexist. Initial occurrences will probably be at locations with address translator software and firewalls.

## Slide 45: IP 地址分类
Class A:
Class B:
Class C:
Class D: 多址地址
Class E: 科研用
Network
Host
Host
Host
Network
Network
Host
Host
Network
Network
Network
Host
8 bits
8 bits
8 bits
8 bits
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This graphic describes the three most common classes of IP address.
Emphasize: Discuss classes of addresses. Each address contains information about the network number and the host number of the device. Class A addresses are for very large organizations. Class B addresses are for smaller organizations, and Class C addresses for even smaller ones.
As the number of networks grows, classes may eventually be replaced by another addressing mechanism, such as classless interdomain routing (CIDR). RFC 1467, Status of CIDR Deployment in the Internet, presents information about CIDR. RFC 1817, CIDR and Classful Routing, also presents CIDR information.

## Slide 46: IP 地址分类
1
Class A:
Bits:
0NNNNNNN
Host
Host
Host
8
9
16
17
24
25
32
Range (1-126)
1
Class B:
Bits:
10NNNNNN
Network
Host
Host
8
9
16
17
24
25
32
Range (128-191)
1
Class C:
Bits:
110NNNNN
Network
Network
Host
8
9
16
17
24
25
32
Range (192-223)
1
Class D:
Bits:
1110MMMM
Multicast Group
Multicast Group
Multicast Group
8
9
16
17
24
25
32
Range (224-239)
Notes: <number>
<footer>
<header>
<date/time>
Emphasize: Highlight the fixed values that start each class address.
The first octet rule states that when an address falls into a specified range, it belongs to a certain class. Students should soon be able to recognize the address class of any IP address on sight.
Note: If time or interest permits, you can use the initial bit patterns in the first octet and show how a class of IP network derives the range of network numbers for that IP address class.

## Slide 47: 主机地址
172.16.2.1
172.16.3.10
172.16.12.12
10.1.1.1
10.250.8.11
10.180.30.118
E1
172.16
12
12
网络
主机
.
.
网络
端口
172.16.0.0
10.0.0.0
E0
E1
路由表
172.16.2.1
10.6.24.2
E0
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure presents an overview of host and network address conventions.
Emphasize: In the example, 172.16.0.0 and 10.0.0.0 refer to the wires at each end of the router.
Explain how the routing table is used. Entries in the routing table refer to the network only. The router does not know the location of hosts—it knows the location of networks.
.

## Slide 48: 计算可用的主机地址
11111111
172 16 0 0
10101100
00010000
00000000
00000000
16 15 14 13 12 11 10 9
8 7 6 5 4 3 2 1
网络
主机
00000000
00000001
11111111
11111111
11111111
11111110
...
...
00000000
00000011
11111101
1
2
3
65534
65535
65536
-
...
2
65534
N
2N-2 = 216-2 = 65534
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains how to calculate the number of available hosts in a network.
Emphasize: 2N-2 is the calculation to determine available hosts. N is the number of binary digits in the host field. Subtract 2 because a host cannot be all 0s or 1s.
The same principal applies when determining the number of available networks.

## Slide 49: IP地址分类练习
地址
类别
网络
主机
10.2.1.1
128.63.2.100
201.222.5.64
192.6.141.2
130.113.64.16
256.241.201.10
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 2:
Purpose: This exercise verifies that the students understand IP address classes, network numbers, and host numbers.
Give the students time to list the address class, network, and host number for each IP address in the table. Review the correct answers interactively.
The answers are given in the following figure.

## Slide 50: IP地址分类练习 （答案）
地址
类别
网络
主机
10.2.1.1
128.63.2.100
201.222.5.64
192.6.141.2
130.113.64.16
256.241.201.10
A
B
C
C
B
Nonexistent
10.0.0.0
128.63.0.0
201.222.5.0
192.6.141.0
130.113.0.0
0.2.1.1
0.0.2.100
0.0.0.64
0.0.0.2
0.0.64.16
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 2:
Purpose: This answers to the exercise are given in the figure.
Note: Students can also find the answers to this exercise in the “Answers” appendix.

## Slide 51: 不设子网的地址
网络 172.16.0.0
172.16.0.0
172.16.0.1
172.16.0.2
172.16.0.3
…...
172.16.255.253
172.16.255.254
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains what networks look like without subnets.
Without subnets, use of network addressing space is inefficient.
The Class B network is like a highway with no exits—there is no place to exit, so all of the traffic is in one line.

## Slide 52: 设置子网的地址
网络 172.16.0.0
172.16.1.0
172.16.2.0
172.16.3.0
172.16.4.0
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure describes network structure when subnets are used.
Emphasize: The host bits of an IP address can be subdivided into a subnetwork section and a host section. The subnetwork section in this example is the full third octet.
Point out the difference in the addressing between the previous slide and this slide.
A subnetted address space is like a highway with exits.
A network device uses a subnet mask to determine what part of the IP address is used for the network, the subnet, and the device ID.
A subnet mask is a 32-bit value containing a number of one bits for the network and subnet ID and a number of zero bits for the host ID.
Given its own IP address and subnet mask, a device can determine if an IP packet is destined for 1) a device on its own subnet, 2) a device on a different subnet on its own network, or 3) a device on a different network.
A device can determine what class of address the device has been assigned from its own IP address. The subnet mask then tells the device where the boundary is between the subnet ID and the host ID.

## Slide 53: 子网地址
172.16.2.200
172.16.2.2
172.16.2.160
172.16.2.1
172.16.3.5
172.16.3.100
172.16.3.150
E0
172.16
网络
网络
端口
172.16.0.0
172.16.0.0
E0
E1
新路由表
2
160
主机
.
.
172.16.3.1
E1
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 2:
Purpose: This figure shows what would happen if there were no subnetting.
Emphasize: If networks could not be broken down into more granular, subnetworks few networks could exist, each with a capacity for many hosts.

## Slide 54: 子网地址
172.16.2.200
172.16.2.2
172.16.2.160
172.16.2.1
172.16.3.5
172.16.3.100
172.16.3.150
172.16.3.1
E0
E1
172.16
2
160
网络
主机
.
.
网络
端口
172.16.2.0
172.16.3.0
E0
E1
新路由表
子网
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 2:
Emphasize: By turning on more bits in the mask, we reserve some bits as network information and can use these bits to describe subnetworks.
Describe how the router makes use of this technique. Point out that there is more information in the routing table now.
Note: As you enter the discussion about subnet masks, a question might arise about whether it is legal to define a discontiguous subnet mask. A discontiguous subnet mask consists of intervening zeros, as in 101111011000, rather than all ones followed by zeros, as in 1111111100000000. The question has two answers. According to RFC 950 that describes IP, a discontiguous subnet mask is legal. However, the hardware expense to produce an interface that supports discontiguous masking is cost-prohibitive. Thus in practice it is not supported on most vendors’ equipment, including Cisco. Also, discontiguous masking has no benefit, and it is much more difficult to maintain a network based on this design. Later RFCs make noncontiguous subnet masks illegal because they are incompatible with future addressing schemes such as CIDR.

## Slide 55: 子网掩码
172
16
0
0
255
255
0
0
255
255
255
0
IP Address
Default Subnet Mask
8-bit Subnet Mask
Network
Host
Network
Host
Network
Subnet
Host
“/16” 表示子网掩码有16位.
“/24”表示子网掩码有24位.
11111111
11111111
00000000
00000000
Notes: <number>
<footer>
<header>
<date/time>
Emphasize: Turn on more bits to represent subnets.
Compare the default or standard subnet mask with the subnet mask in the slide.
These are the rules for IP addressing:
  An address is 32 bits, divided into three components:
    First octet rule bits
    Network bits (path selection bits)
    Node bits
  The first octet rule states that the most significant bit pattern in the first octet determines the class of the address.
  Path selection bits cannot be all ones or zeros.
  Certain addresses are reserved. RFC 1918 defines some of those.
  Prefix or mask one bits are path selection significant; zero bits are host bits and therefore not significant.
  Use the logical AND to combine the address and mask bits to get the subnet address.
  The maximum number of available subnets equals 2 prefix bits - 2; the maximum number of available hosts equals 2 32- prefix bits - 2.

## Slide 56: 十进制和二进制的转换
1 0 0 0 0 0 0 0 = 128
1 1 0 0 0 0 0 0 = 192
1 1 1 0 0 0 0 0 = 224
1 1 1 1 0 0 0 0 = 240
1 1 1 1 1 0 0 0 = 248
1 1 1 1 1 1 0 0 = 252
1 1 1 1 1 1 1 0 = 254
1 1 1 1 1 1 1 1 = 255
128 64 32 16 8 4 2 1
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains how subnet masks are converted to decimal addresses.
Emphasize: Review binary-to-decimal conversion, bit weighting, and conversion.
Explain logical AND.
One possible explanation of logical AND follows: We will need to be able to perform a logical AND on the binary numbers. Just take two binary numbers and place one above the other. The ones in the bottom are like a pipe—the number above it just drops through. The zeros are like a clogged pipe, so nothing comes out in the answer.
Presenting a truth table will help some students understand. You might need to give more than one explanation.
Note: You might want to hand out a binary-to-decimal conversion sheet if you have not already done so. We have not included one in the lab section. It is more useful to have one that is on a separate page from the labs.

## Slide 57: 缺省情况下的子网掩码
16
网络
主机
172
0
0
10101100
11111111
10101100
00010000
11111111
00010000
00000000
00000000
10100000
00000000
00000000
缺省情况下子网未划分
00000010
172.16.2.160
255.255.0.0
网络号
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This graphic explains how routers use addresses that have no subnet mask.
Emphasize: Explain how masking works at the bit level. Zero bits mask host information.
Note: This is an easy place to lose students. At this point, they need to learn several abstract mathematical concepts before we can show them how to lay out an IP-addressed network. To the novice these techniques may seem unrelated, making the presentation confusing. To a more experienced audience, these techniques will be familiar.

## Slide 58: 利用子网掩码划分子网
扩展了8位地址的网络
16
网络
主机
172.16.2.160
255.255.255.0
172
2
0
10101100
11111111
10101100
00010000
11111111
00010000
11111111
00000010
10100000
00000000
00000000
00000010
子网
网络号
128
192
224
240
248
252
254
255
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure shows how the router determines an address when subnetting is used.
Emphasize: This example makes a Class B address space look like a collection of Class C address spaces.
Now the logical AND allows us to extract the subnet number as well as the assigned network number.
An exercise follows that tests the students’ understanding of subnet masks.

## Slide 59: 利用子网掩码划分子网
网络
主机
172.16.2.160
255.255.255.192
10101100
11111111
10101100
00010000
11111111
00010000
11111111
00000010
10100000
11000000
10000000
00000010
子网
扩展了10位地址的网络
16
172
2
128
网络好
128
192
224
240
248
252
254
255
128
192
224
240
248
252
254
255
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure shows how the router determines an address when subnetting is used.
Emphasize: This example is different from the previous example in that the the subnet and host are divided within an octet.
Transition: An exercise follows that tests the students’ understanding of subnet masks.

## Slide 60: 子网掩码练习
地址
子网掩码
类别
子网
172.16.2.10
10.6.24.20
10.30.36.12
255.255.255.0
255.255.240.0
255.255.255.0
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 2:
Purpose: This exercise is for the students to take the given IP addresses and associated subnet masks and perform a logical AND to extract the subnet number. Provide time in class and review the answers after the majority of students have finished.
The answers are given in the following figure.

## Slide 61: 子网掩码练习 （答案）
地址
子网掩码
类别
子网
172.16.2.10
10.6.24.20
10.30.36.12
255.255.255.0
255.255.240.0
255.255.255.0
B
A
A
172.16.2.0
10.6.16.0
10.30.36.0
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 2:
Purpose: This answers to the exercise are given in the figure.
Note: Students can also find the answers to this exercise in the “Answers” appendix.

## Slide 62: 广播地址
172.16.1.0
172.16.2.0
172.16.3.0
172.16.4.0
172.16.3.255
(Directed broadcast)
255.255.255.255
(Local network broadcast)
X
172.16.255.255
(All subnets broadcast)
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains how broadcast addresses work.
Emphasize: A range of addresses is needed to allocate address space. A valid range of addresses is between subnet zero and the directed broadcast.
These RFCs provide more information about broadcasts:
  RFC 919, Broadcasting Internet Datagrams
  RFC 922, Broadcasting IP Datagrams in the Presence of Subnets
Cisco’s support for broadcasts generally complies with these two RFCs. It does not support multisubnet broadcasts that are defined in RFC 922.

## Slide 63: 地址汇总示例
16
172
2
160
10101100
00010000
10100000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
4
1
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 9:
Purpose: This example summarizes The IP addressing that was covered earlier in this chapter.
Emphasize:
In layer 1, convert the address to a binary host address.

## Slide 64: 地址汇总示例
10101100
11111111
00010000
11111111
11111111
10100000
11000000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
16
172
2
160
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 9:
Emphasize: In layer 2, write the subnet mask in binary.

## Slide 65: 地址汇总示例
10101100
11111111
00010000
11111111
11111111
10100000
11000000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
7
16
172
2
160
Notes: <number>
<footer>
<header>
<date/time>
Layer 3 of 9:
Emphasize: In layer 3, draw a line after the recursive ones in the subnet mask.

## Slide 66: 地址汇总示例
10101100
11111111
00010000
11111111
11111111
10100000
11000000
10000000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
16
172
2
160
Notes: <number>
<footer>
<header>
<date/time>
Layer 4 of 9:
Emphasize: In layer 4, fill in zeros beyond the vertical line for the subnet.

## Slide 67: 地址汇总示例
10101100
11111111
00010000
11111111
11111111
10100000
11000000
10000000
00000010
10111111
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
5
6
16
172
2
160
Notes: <number>
<footer>
<header>
<date/time>
Layer 5 of 9:
Emphasize: In layer 5, fill in ones beyond the vertical line for the broadcast address.

## Slide 68: 地址汇总示例
10101100
11111111
00010000
11111111
11111111
10100000
11000000
10000000
00000010
10111111
10000001
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
5
6
16
172
2
160
Notes: <number>
<footer>
<header>
<date/time>
Layer 6 of 9:
Emphasize: In layer 6, fill in 0s beyond the vertical line except for the last bit. Make that bit a 1. This is the first usable host address.

## Slide 69: 地址汇总示例
10101100
11111111
00010000
11111111
11111111
10100000
11000000
10000000
00000010
10111111
10000001
10111110
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
5
6
7
16
172
2
160
Notes: <number>
<footer>
<header>
<date/time>
Layer 7 of 9:
Emphasize: In layer 7, fill in 1s beyond the vertical line except for the last bit. Make that bit a 0. This is the last usable host address.

## Slide 70: 地址汇总示例
10101100
11111111
10101100
00010000
11111111
00010000
11111111
00000010
10100000
11000000
10000000
00000010
10101100
00010000
00000010
10111111
10101100
00010000
00000010
10000001
10101100
00010000
00000010
10111110
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
5
6
7
8
16
172
2
160
Notes: <number>
<footer>
<header>
<date/time>
Layer 8 of 9:
Emphasize: In layer 8, copy the binary network and subnetwork address from the top row into the lower rows.

## Slide 71: 地址汇总示例
10101100
11111111
10101100
00010000
11111111
00010000
11111111
00000010
10100000
11000000
10000000
00000010
10101100
00010000
00000010
10111111
10101100
00010000
00000010
10000001
10101100
00010000
00000010
10111110
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
172.16.2.128
172.16.2.191
172.16.2.129
172.16.2.190
1
2
3
4
5
6
7
8
9
16
172
2
160
Notes: <number>
<footer>
<header>
<date/time>
Layer 9 of 9:
Emphasize: In layer 9, convert binary back to dotted decimal.

## Slide 72: B类地址子网规划
IP Host Address: 172.16.2.121
Subnet Mask: 255.255.255.0
Subnet Address = 172.16.2.0
Host Addresses = 172.16.2.1–172.16.2.254
Broadcast Address = 172.16.2.255
Eight bits of subnetting
Network
Subnet
Host
10101100
00010000
00000010
11111111
172.16.2.121:
255.255.255.0:
10101100
11111111
Subnet:
10101100
00010000
00010000
11111111
00000010
00000010
11111111
01111001
00000000
00000000
Broadcast:
Network
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure shows an example of a Class B network with a subnet.

## Slide 73: 子网划分
Other
subnets
192.168.5.16
192.168.5.32
192.168.5.48
20 子网
5 主机/子网
C类地址：
192.168.5.0
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure explains how to plan subnet numbers.
Emphasize: What if this were a Class B address? How many bits would we have for subnetting then? Where do you want to draw the line now?
Alternatives to review: Creating the subnet at the octet boundary is easier to work with—more host bits and more subnet bits.
Explain that the decision is really a guess on how you think your network will grow—will it have more subnets or more hosts?
RFC 1219 Mirroring: Mirroring hedges the subnetting decision by buying time. Do not use mirroring if you intend to use route summarization or variable-length subnet masking (VLSM); they are incompatible with mirroring.

## Slide 74: C类地址子网规划
11111000
IP Host Address: 192.168.5.121
Subnet Mask: 255.255.255.248
Network
Subnet
Host
192.168.5.121:
11000000
11111111
Subnet:
11000000
10101000
10101000
11111111
00000101
00000101
11111111
01111001
01111000
255.255.255.248:
Subnet Address = 192.168.5.120
Host Addresses = 192.168.5.121–192.168.5.126
Broadcast Address = 192.168.5.127
Five Bits of Subnetting
Broadcast:
Network
Network
11000000
10101000
00000101
01111111
Notes: <number>
<footer>
<header>
<date/time>
Purpose: This figure shows an example of a Class C network with a subnet.
Emphasize: Contrast the Class C network subnet mask with the previous Class B example.

## Slide 75: 广播地址练习
地址
类别
子网
广播地址
201.222.10.60
255.255.255.248
子网掩码
15.16.193.6
255.255.248.0
128.16.32.13
255.255.255.252
153.50.6.27
255.255.255.128
Notes: <number>
<footer>
<header>
<date/time>
Layer 1 of 2:
Purpose: Have the students calculate the subnet numbers and the broadcast address for each subnet from the given IP addresses and subnet masks.

## Slide 76: 广播地址练习 （答案）
153.50.6.127
地址
类别
子网
广播地址
201.222.10.60
255.255.255.248
C
201.222.10.63
201.222.10.56
子网掩码
15.16.193.6
255.255.248.0
A
15.16.199.255
15.16.192.0
128.16.32.13
255.255.255.252
B
128.16.32.15
128.16.32.12
153.50.6.27
255.255.255.128
B
153.50.6.0
Notes: <number>
<footer>
<header>
<date/time>
Layer 2 of 2:
Purpose: This answers to the exercise are given in the figure.
Note: Students can also find the answers to this exercise in the “Answers” appendix.

## Slide 77: 问题回顾
  1. TCP协议和UDP协议有和不同？
  2. 和IP地址为： 192.168.20.1 255.255.255.240, 在同一网段的主机有哪些？
  3. 在实现不同VLAN间通讯时什么是必须的？
Notes: <number>
<footer>
<header>
<date/time>
Purpose: Review the chapter with open ended questions.
Note: The questions in this section are open ended questions designed to foster further discussion.
Answers the the review questions are in the “Answers” appendix.