## Slide 1
第六章 时序逻辑电路设计
6.1 触发器
6.2 计数器

## Slide 2
在时序电路中，是以时钟信号作为驱动信号的，也就是说时序电路是在时钟信号的边沿到来时，它的状态才会发生改变。因此，在时序电路中时钟信号是非常重要的，它是时序电路的执行条件和同步信号。
在用VHDL描述时序逻辑电路时，通常采用时钟进程的形式来描述，也就是说，时序逻辑电路中进程的敏感信号是时钟信号。时钟作为敏感信号的描述方式有两种：
1.时钟信号显示地出现在PROCESS语句后面的敏感信号表中。
2. 时钟信号没有显示地出现在PROCESS语句后面的敏感信号表中，而是出现在WAIT语句的后面。
在时序逻辑电路中，时钟是采用边沿来触发的，时钟边沿分为上升沿和下降沿。以下是这两种边沿的描述方式。
对于上升沿，其物理意义是指时钟信号的逻辑值是从‘0’跳变到‘1’。下面是时钟上升沿的几种描述形式：

## Slide 3
上升沿描述:
描述1：
label1：PROCESS（clk）
BEGIN
IF（clk’EVENT AND clk = ‘1’）THEN
┇
AND PROCESS；
描述2：
label2：PROCESS（clk）
BEGIN
WAIT UNTIL clk = ‘1’；
┇
AND PROCESS；

## Slide 4
下降沿描述:
描述1：
label1：PROCESS（clk）
BEGIN
IF（clk’EVENT AND clk = ‘0’）THEN
┇
AND PROCESS；
描述2：
label2：PROCESS（clk）
BEGIN
WAIT UNTIL clk = ‘0’；
┇
AND PROCESS；

## Slide 5
6.1 JK触发器
例[]
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY JKff_v1 IS
PORT(J,K: IN STD_LOGIC;
clk: IN STD_LOGIC;
set: IN STD_LOGIC;
reset: IN STD_LOGIC;
Q,QB: OUT STD_LOGIC);
END JKff_v1;
ARCHITECTURE behave OF JKff_v1 IS
SIGNAL Q_temp,QB_temp: STD_LOGIC;

## Slide 6
BEGIN
PROCESS (clk,set,reset)
BEGIN
IF (set ='0' AND reset ='1')THEN
Q_temp <= '1';
QB_temp <= '0';
ELSIF (set ='1' AND reset ='0')THEN
Q_temp <= '0';
QB_temp <= '1';
ELSIF (clk'EVENT AND clk = '1')THEN
IF(J='0' AND K='1')THEN
Q_temp <= '0';
QB_temp <= '1';

## Slide 7
ELSIF(J='1' AND K='0')THEN
Q_temp <= '1';
QB_temp <= '0';
ELSIF(J='1' AND K='1')THEN
Q_temp <= NOT Q_temp ;
QB_temp <= NOT QB_temp;
END IF;
END IF;
Q <= Q_temp;
QB <= QB_temp;
END PROCESS;
END behave；

## Slide 8
JK触发器仿真波形

## Slide 9
6.2 60进制递增计数器
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
ENTITY cntm60v IS
PORT( en : IN std_logic;
clear : IN std_logic;
load : IN std_logic;
dl,dh : IN std_logic_vector(3 downto 0);
clk : IN std_logic;
cout : out std_logic;
ql : buffer std_logic_vector(3 downto 0);
qh : buffer std_logic_vector(3 downto 0) );

## Slide 10
END cntm60v;
ARCHITECTURE behave OF cntm60v IS
signal ent2 : std_logic;
BEGIN
PROCESS (clk)
VARIABLE tmpl,tmph :std_logic_vector(3 downto 0);
BEGIN
IF(clear='0') THEN
tmpl:="0000";
tmph:=“0000”; - -异步清零
ELSIF(clk'EVENT AND clk = '1') THEN

## Slide 11
IF load='0' THEN
tmpl:=dl;
tmph:=dh; - - 同步置数
elsif(en='1') then
if (tmpl="1001") then
tmpl:=“0000”; - -个位计数器9+1=0
if(tmph="0101") then
tmph:=“0000”; - -十位计数器5+1=0 59+1=0
else
tmph:=tmph+1;
end if;
else
tmpl:=tmpl+1;
end if;

## Slide 12
end IF; --end lf (load)
END IF; --end if clear
ql <= tmpl;
ent2 <= tmpl(3) and tmpl(0) and en;
qh<=tmph;
cout<=tmph(2) and tmph(0) and ent2;
- -计数器为59时进位信号 cout 输出‘1’。
END PROCESS;
END behave ;

## Slide 13
60进制计数器波形仿真